## Slide 1: PVDIS baffle
Zhiwen Zhao
2013/10/15

## Slide 2: Intro
Previously, I couldn’t obtain an ideal baffle with the code (makebaf5.C)
For the writeup, we used “BaBar more1 block” which is based on Eugene’s BaBar baffle with 5 additional plates and 1 more degree in phi and photon blocks before EC
Now I take a look at baffle design again and try to develop a method

## Slide 3: How it’s done, Step 1
Use CLEO v8 field map
eDIS (W>2) of 40cm long LD2 target, from code eicRate
11 baffle plates from Z=40cm – 180cm, 30 slits in 1 plate, 20 blocks in 1 slit
1st baffle min radius at 5cm (>5.2o, to avoid Moller e-)
Study phi change from these eDIS events at every baffle plate front face. Allow 96%(from 2% to 98% of phi change) of rate weighted events with 0.35<x<0.8 and p>1.5GeV to pass through. This define the opening for a very narrow phi slice of eDIS events from the target
Enlarge this opening by 3.5o where positive leaks start to appear, expect 30%=3.5/12 acceptance for eDIS events with 0.35<x<0.8 and p>1.5GeV. I name this “baffle 0.35x3.5deg”

## Slide 4: Rate VS Phi turning
20 blocks at 1st baffle

## Slide 5: Rate VS Phi turning
20 blocks at 11th baffle

## Slide 6: “Baffle 0.35x3.5deg”
It looks similar to “BaBar more1”

## Slide 7
source
Z(-10,30)cm
R(0,3.536)mm
for 5x5mm raster
neutral
negative
positive
Acceptance,
Baffle 0.35x3.5deg

## Slide 8: How it’s done, Step 2
Further block photons by adding more material
  At the last (11th) baffle, negative and neutral mixes with each other at low phi where high x and high P events are. Block photon here will harm eDIS acceptance at high x. I name this “baffle 0.35x3.5deglast”
  At EC, negative and neutral split well from each other due to the additional flight path. Photon block at EC works better. I name this “baffle 0.35x3.5degblock”

## Slide 9
source
Z(-10,30)cm
R(0,3.536)mm
for 5x5mm raster
neutral
negative
positive
Acceptance,
Baffle 0.35x3.5degblock
EC module R(110,265)cm
EC photon block (“baffle 3.5degblock”)
30 of them
R(105-200)cm
Start from 3 degree and width 4 degree. (They can be further optimized)
5cm(8*X0) thick lead, hope to reduce photon energy by 1 order

## Slide 10: Another adjustment
Optimize for eDIS 0.55<x<0.8 (instead of 0.35<x<0.8)
Enlarge the opening by 5o (instead of 3.5o) where positive leaks start to appear, expect 40%=5/12 (instead of 30%)
Keep all other conditions same

## Slide 11
source
Z(-10,30)cm
R(0,3.536)mm
for 5x5mm raster
neutral
negative
positive
Acceptance,
Baffle 0.55x5deg

## Slide 12
Further block photons by adding more material
  At the last (11th) baffle, negative and neutral mixes with each other at low phi where high x and high P events are. Block photon here will harm eDIS acceptance at high x
  At EC, negative and neutral split well from each other due to the additional flight path. Photon block at EC works better. I name this “baffle 0.55x5degblock”

## Slide 13
source
Z(-10,30)cm
R(0,3.536)mm
for 5x5mm raster
neutral
negative
positive
Acceptance,
Baffle 0.55x5degblock
EC module R(110,265)cm
EC photon block (“baffle 3.5degblock”)
30 of them
R(105-205)cm
Start from 2.8 degree and width 4 degree.
5cm(8*X0) thick lead, hope to reduce photon energy by 1 order

## Slide 14: eDIS acceptance comparison at EC
“0.55x 5deg” and “0.55x 5deg block” has best acceptance at high x

## Slide 15: eDIS rate comparison at EC
“0.55x 5deg” and “0.55x 5deg block” has no low mom leak which could leads to high trig rate

## Slide 16: Err_Apv(%)
x | 0.20-0.30 | 0.30-0.35 | 0.35-0.40 | 0.40-0.45 | 0.45-0.50 | 0.50-0.55 | 0.55-0.60 | 0.60-0.67 | 0.67-0.80
BaBar more1 block | 0.290 | 0.304 | 0.287 | 0.294 | 0.319 | 0.356 | 0.427 | 0.468 | 0.641
0.35x 3.5deg | 0.246 | 0.266 | 0.267 | 0.283 | 0.318 | 0.367 | 0.434 | 0.470 | 0.645
0.35x 3.5deg Block | 0.315 | 0.316 | 0.307 | 0.309 | 0.335 | 0.378 | 0.440 | 0.473 | 0.646
3.5deg Last | 0.281 | 0.302 | 0.303 | 0.328 | 0.373 | 0.447 | 0.530 | 0.585 | 0.789
0.55x 5deg | 0.283 | 0.303 | 0.289 | 0.289 | 0.309 | 0.343 | 0.397 | 0.424 | 0.573
0.55x 5deg Block | 0.311 | 0.310 | 0.291 | 0.289 | 0.309 | 0.344 | 0.398 | 0.426 | 0.578
EC R(110,250)cm nominal acceptance
Assume 50uA, 40cm LD2
Pol_beam 85%, 120 days
No trig cut

## Slide 17: For eDIS x>0.8
For eDIS with cut W>2GeV, events with x>0.8 only happen for large angle
The acceptance shown has cut 22<theta<35deg
There are some acceptance for 35<theta<40deg from the downstream part of the target, but its x only extends to 0.81 (see next slide)
The largest x output by the generator with cut W>2GeV is at 0.84 (see slide after next)

## Slide 18: eDIS rate comparison from generator
Red with theta 22-35 deg, blue with theta 22-40 deg

## Slide 19: eDIS rate comparison from generator
Red with theta 22-35 deg, blue with theta 0-180 deg