## Slide 1: Photon rejecting scintillator
Jin Huang
Los Alamos National Lab

## Slide 2: Generic discussion
Add scintillator before preshower to reject photons VS electron
  Interested energy range 1~few GeV (photon rate drop quickly)
  Need to be simple & fast for trigger implementation
Generic rate for single photon on stand alone scintillator:
  Prob. for photon energy dep = 1-exp(-L/L0)
  Where L0 ~ 55 cm for scintillator
  Simulated by Zhiwen:
Zhiwen’s simulation
10cm 22%
5cm 14%
2cm 5%
1cm 3.3%
0.5cm 2.3%
0.25cm 0.65%

## Slide 3: From last week - Radiation dose is OK
Before the preshower Pb and without protection from lower energy EM background
Turn out to be not very bad since photon penetrate more depth
Log10(Eϒ/GeV)
Photon-rej Scintillator
Preshower
Ratio of energy deposition in active layers from a input photon
Majority E
Photon-rej Scintillator
Preshower
Dominated by
low-E γ & electron

## Slide 4: Geant4 Simulating scintillator before preshower
Scintillator
Thickness = 5 mm
Preshower Pb
Preshower Scint
γ
Lots of back scattering!

## Slide 5: Simulated efficiency & rejection
MIP peak
Electron
Pion
Photon
Energy range: 1-7 GeV, flat phase space for SIDIS-forward
~1:7 γ-rej with cut below MIP peak
Efficiency
Cut on energy dep.

## Slide 6: Simulated efficiency & rejection
Most photon focus on lower energy side (π0 decay)
And lower energy photon produce less back scattering
Therefore, do the study again with 1<Eγ<2 GeV
E dep for photons (MeV)
Eγ (GeV)
Electron
Pion
Photon
1<Eγ<2 GeV
~1:20 γ-rej with cut below MIP peak
Efficiency
Cut on energy dep.

## Slide 7: Discussion
Photon rejection:
  1:20 (1-2 GeV)
  1:7 (full E range)
  Cut well below MIP peak
Back scattering from calorimeter is significant
We can try
  Move scintillator away from preshower?
    Ex. put it before the heavy gas cherenkov
  Use two layer of scintillator to rej backscattering?
    Probably not efficient
More to study
  Background level – plan to use background imbedding
  Correlated photon background from π0 delay
  Energy deposition to trigger level smearing