Update on EM Calorimeters
Calorimeter Group

---
Overview
SoLID Collaboration Meeting

---
SoLID EM Calorimeter Overview
PVDIS forward angle
SIDIS forward angle
SIDIS large angle

---
Default design for calorimeter modules
Scintillator Pad
Scintillator Pad (SPD)
  - Reject high energy photons for electron trigger and hadron trigger at SIDIS forward angle
Preshower (PS)
– HERMES/LHCb style passive radiator + scintillator design
  - 2 X0 lead radiator + 2 cm scintillator tile w/ WLS readout
Shower
– COMPASS style Shashlyk calorimeter design
  - Layer structure : 0.5 mm lead + 1.5 mm scintillator + 0.12 mm gap x 2
  - X0 = 24cm, RM ~ 5 cm, 194 layers, 43 cm in depth

---
Scintillator for rejecting background photon
back scattering for high-E γ
Scintillator
Thickness = 5 mm
(thicker version shown)
Preshower Pb
Preshower Scint
γ

---
Thin scintillator pad to reject photons at trigger level
Features
  - Scintillator thickness of 5mm: simulation shows 2.3% of photons from SIDIS pi0 would deposit energy, the rejection factor estimated at least 20
  - Segment into fan shape for readout by WSL fiber or PMT directly
Background is important: dominated by low energy electrons
Source of low energy electrons
  - 20% from end cap of heavy gas Cerenkov, other from more upstream
  - Have to be placed before MPRC, which have lots of material for conversion!
Rate: if 120 segment take 2MHz MIP per segment
Particle species at front surface:
Electron
Low energy gamma
All

---
How signal looks like
60 sectors
4 MHz MIP
30 sectors
8 MHz MIP
240 sectors
1 MHz MIP
Signal of each MIP hit
 (amp. variation not included)
Sum of all signals

---
Optimizing the segment
Lower energy photon (1-2 GeV) are dominant, which we have higher rejection
Trigger require 5:1 rejection. Satisfied with margin at a 120 segments
A 50ns coincidental window with calorimeter assumed. Expect improvement in FPGA level
Low-E (1-2 GeV)
Full E range (1-7 GeV)

---
Orthographic projection along z axis
Orthographic projection along φ axis
2X0 lead absorber
2cm pre-sh. scint
2cm Al frontplane
4cm Al backplane
Hexagon Calorimeter Simulation
3GeV electron shower
On hexagon calorimeter grid
The support Al plate was just added, not used in this study
3GeV e-
3GeV e-

---
All rejection/efficiency reviewed with hexagon-shape calorimeter modules
From last meeting:
Pion rejection with
square module 3x3 clustering
94% electron efficiency
No background yet assumed at this step
Expect go high w/ higher stat.
Preshower ID power drop significantly at this bin

---
Review of Background Simulation
3rd iteration of GEMC + CaloSIM background study

---
Calorimeter background simulation with GEMC + CaloSIM
GEMC simulate spectrum and rate of background particle at the front surface of calorimeter (Zhiwen)
CaloSIM (standalone calorimeter simulation, on SoLID SVN) build calorimeter response from a wide range of incoming particle species and energy range
Combine above two and sum over all contributions (EM, DIS, pi0, pi+,pi-) stochastically within a 50ns coincidental window (assumed at this moment)
-> background distribution at each trigger
Imbed background into the signal simulation (high energy e, pi) and perform analysis (clutering, e/pi separation, etc.)

---
Radiation dose prediction remain stable
Dose is not a problem for SIDIS configuration.
  - Calorimeter design to stand >105 radiation dose
  - Important to have this safty margin
Still missing final PVDIS radiation dose, need final baffle w/o direct line of sight
Particle species at front surface:
Electron
Low energy gamma
Pi- / pi+
pi0 -> gamma
SIDIS – He3– Large Angle Calorimeter
SIDIS – He3– Forward Calorimeter

---
Full background simulation
For SIDIS Forward Calorimeter

---
SIDIS forward background
We have good “shielding” with 2X0 preshower, save us from 1GHz/cm2 photon background
Dominated background: low energy photon 1-100 MeV, which lead to 10kHz/cm2 MIP signal on preshower
The background on shower is small
Used in this study:
  - Most inner side (highest rate)
  - 100 cm2 segmented preshower -3 MHz MIP rate
  - For outer radius, rate is 10x lower, less segmentation can be used there
preshower MIP rate categorized with its source
Particle species at front surface:
Electron
Low energy gamma
Pi-

---
Compare background to signal
Electron
Background
Pions
Background
Pion
Electron
Background
Pion
Electron
Background
MIP Background is significant in preshower
Background is much less significant for shower

---
Offline: No change in eff., reduce rejection at low-p end
Rejection reduced due to preshower pile up
w/o background
w/ background

---
Hexagon Calorimeter Trigger
Hexagon Provide nice shower area cuts – can be used in both online and 1st-order offline analysis
  - clustering – contains ~96% of shower energy
  - FPGA-based pattern trigger (HEX 1+6 trigger)

---
Online: Trigger with background
Hadronic shower which introduce a pion contamination, usually spread into larger area compared to EM shower
A localized trigger, e.g. HEX1+6 trigger can significantly suppress the hadron response, while maintaining high eff. for electrons
Ratio of EM shower contained
Ratio of Pion shower contained

---
If we only trigger on total EM energy
Do receive very high electron efficiency in simulation
However, for SoLID, wide momentum range is used.
  - Therefore to accept lowest momentum electrons, the shower cut have to be low.
  - the rejection for high momentum pion will be very limited
From DAQ group (Xin, Alex): use position dependent threshold, consider plus preshower trigger
Simulated with background imbedding. The pion response is shown below:
HEX1+6 Trigger
> 1.95GeV
HEX1+6 Trigger
> 0.95GeV
* Accepted
* All

---
Pion trigger response
* Accepted
* All
Charged Particle (Pion) trigger efficiency
Full background simulation for pion efficiency shown on the right.
Trigger cut is HEX1+6 trigger raw signal is larger than 85% MIP
(which is MIP – 2σ = 220MeV calibrated)
The background which pass this cut
  - rate ~20Mhz
  - is dominated by photon.
  - With an additional 1/5 suppression from scintillator, we get ~4MHz trigger rate, which fit in the DAQ limit (PR12-10-006)
  - Will join global DAQ study for final verification

---
Design Updates
- Fiber connector

---
Fiber connection
Shower will use 1-1 bundle fiber connector.
Used in previous experiments (LHCb, Minos)
custom made fiber connector, quote by LEONI (see next slide)
Preshower will use comercial 1-1 single fiber connector, a few $ each.
LHCb shower
fiber bundle to PMT connector, cost estimate $25/module

---
Fiber connector
Concept design from LEONI
1 connector for 100
fiber pairing
made of Al
35% worst light loss
$100/each

---
Budget Update

---
Budget
+ Prototyping ~ 0.3 M$
+ Support ~

---
backup

---
Shower – quick review
Choice of technology
  - Shashlyk design was chosen based on advantage of radiation resistance + cost + ease of readout
Features
  - Pb/Scint ratio 1:3 (V) : chosen to reach <5%/√E energy resolution and ~100:1 pion rejection
  - Scintillator thickness of 1.5mm: based past designs to balance sampling fineness VS lateral light transmission loss
  - Total length of 20 X0 : contain 98% of shower and maximize pion-electron difference
    → MIP = 270 MeV (real) / 320 MeV (reconstructed)
  - Lateral size of 10x10 cm2: max size allowed (to reduce $$) before position resolution significantly deteriorates (σ~1 cm after cor.)

---
Preshower – quick review
Choice of technology
  - HERMES/LHCb style VS full Shashlyk design, former is much easier to readout and high in radiation resistance
Features
  - Absorber of 2 X0 lead :
    - Thinner – loose preshower rejection
    - Thicker – loose shower resolution
    - Scanned for 1.5, 2 and 3 X0;
      2 X0 serve SoLID best
  - Scintillator of 2 cm:
    - MIP = 4 MeV, electron cut ~ 3 MIP

---
Simulation setup with hexagon calorimeter modules

---
Back up 1/2 for previous slides
All events
Accepted events w/ 3D cut
Electron eff. for SIDIS large angle calorimeter

---
Back up 2/2 for previous slides
All events
Accepted events w/ 3D cut
Pion eff. for SIDIS large angle calorimeter

---
Backup - Simulated efficiency & rejection
Electron
Pion
Photon
Energy range: 1-7 GeV, flat phase space for SIDIS-forward
MIP peak
~1:7 γ-rej with cut below MIP peak
Cut on energy dep.
Efficiency

---
Backup - Simulated efficiency & rejection
Most photon focus on lower energy side (π0 decay)
And lower energy photon produce less back scattering
Therefore, do the study again with 1<Eγ<2 GeV
Electron
Pion
Photon
1<Eγ<2 GeV
~1:20 γ-rej with cut below MIP peak
Cut on energy dep.
E dep for photons (MeV)
Eγ (GeV)
Efficiency

---
Design Updates
- Shape

---
Change from square to hexagon
Main reason from supporting structure and layout (see Paul Reimer’s talk)
Physics feature should be similar to square shape and we will go through test and prototyping

---
Design Updates
- Layout Update

---
SIDIS and PVDIS FAEC (beam view)
Both can share supporting structure, only need to move along beam direction to change configuration
Supporting structure needs to be made from 100cm to 261cm
261cm
118cm
100cm
215cm
PVDIS FAEC (green + blue)
SIDIS LAEC (blue + red)

---
Ideas to minimize SIDIS LAEC Acceptance gap
We want to cover full azimuthal angle and leave no gap between modules, so module can not be tilted and need to be along Z axis
Prefer having short outer module so that the outer module area can cover more and inner module area can cover less
Inner module need to be special shape to avoid blocking acceptance. One way to solve it is to have smaller 5x5cm (like COMPASS) module with various length
600mm
assume 600mm full module length
Blue: LAEC acceptance angle
Orange : angle between inner and outer
10x10x60cm module
Outer module
(500mm in radius)
24o
5x5x41cm
inner module
(150mm in radius)
5x5x22cm
17.5o
600mm
14.7o
Reviewed using G4 simulation next few pages

---
SIDIS LAEC (beam view)
Type I (10x10cm) module in blue, type II (5x5cm long) module in green, type III (5x5cm short) module in purple.
Supporting structure needs to be made from 75cm to 140cm
140cm
75cm

---
Design Updates
- Edge effects for LAEC

---
LAEC layout in G4 Simulation

---
LAEC in full standalone G4 Simulation
Track transportation provided by GEMC, CLEO field

---
How much does inner modules help?
LAEC catch 80% of shower
Go freely to forward acceptance
Stand conf. 404 10x10 cm2 modules
+ 116 5x5 cm2 inner modules
Minor improvement

---
Design Updates
- Shower cluster size cut

---
Previously showed pion rejection
94% electron eff.
PID selection used 3-D cut on PS, e/p and momentum
PS and e information come from sum signal in all non-zero modules
Enemy here is very specific: almost fully absorved hadronic shower with high energy deposition

---
Shower area difference
Electron shower
Hadronic shower (e/p>80%)
Φ - spread (mm)
Φ - spread (mm)
Notice the difference in color scale
R spread (mm)
R spread (mm)

---
Apply additional cut to limit max size of cluster around track projection
Limit cluster to be not larger than 3x3 modules around track projection to shower central depth
Minor cut on EM shower but effectively removed hadronic showers of very high energy deposition
w/ >=94% electron eff.
Pion
BIG improvement @ high p end
Miss identified
Flat phase
space in PVDIS
acceptance

---
Can it be further improved?
Further limit cluster to be not larger than 2x2 modules around track projection to shower central depth
Now loose ~5% of EM shower, but hadron shower cuts faster
Change cut and maintain
>=94% electron eff.
All hadron rej. better than
100:1
Pion
Miss identified
Flat phase
space in PVDIS
acceptance

---
Design Updates
- Radiation dose

---
What’s new
LHCb/HERMES preshower, instead full Shashlyk preshower
  - As shown before, the preshower scintillator receive most of the radiation, due to the low energy backgrounds
  - This part radiation dose are now absorbed in 2X0 absorber, and we just see its EM tail now
  - Especially, lead absorber effectively kill all low energy electron background
New background distribution updated by Zhiwen
  - SIDIS:
    - With target collimator (suppress background by 4)
    - First large angle simulation
  - PVDIS: have option to remove direct photon sight (expected to be removed in the final baffle design)
Dominating background, photons 1-10 MeV
  - After preshower, which attenuate them a lot, they still penetrate ~10 layers in Shashlyk

---
PVDIS – current baffle (with direct γ)
γ dominate
But attenuated quickly
Layer #1 is 2cm preshower scint.

---
PVDIS – preview for a baffle w/o direct γ
γ get reduced by ~5
π- become important here
Layer #1 is 2cm preshower scint.

---
SIDIS – Forward
γ dominate
But attenuated quickly
Layer #1 is 2cm preshower scint.

---
SIDIS – Large-Angle
γ dominate
But attenuated quickly
Layer #1 is 2cm preshower scint.

---
Light Readout

---
WLS fiber in scintillator pad
Drill on scintillator and glue WLS in
Used by LHCb etc.
Will use by CLAS12 FT-Hodo
CLAS12 FT-Hodo
LHCb Preshower

---
Fiber
WSL fiber in shower, 100/module
  - Bicron BCF-91A
    - multi-clad, 1/e length >3.5m
    - 1mmD, bend 20cmD (?)
    - $0.87/m
    - less rad hard
WLS fiber in preshower pad, 1-2/module
  - KURARAY Y-11(200)MS
    - multi-clad, 1/e length >3.5m
    - 0.5mmD, bend 5cmD
    - $1/m
    - more rad hard
Clear fiber for both, 101-102/module
  - Bicron BCF-98
    - $1/m

---
Fiber connection
Shower will use 1-1 bundle fiber connector.
Used in previous experiments (LHCb, Minos)
custom made fiber connector $175/module, quote by LEONI
Preshower will use comercial 1-1 single fiber connector, a few $ each.
LHCb shower
fiber bundle to PMT connector, cost estimate $25/module

---
Readout
PMT option - Hamamatsu R3998-02
  - 28mmD Bialkali Photocathode
  - $600 each
  - Used by CLAS TPE calorimeter which has COMPASS module
  - As our baseline design
APD/SiPM option
  - High resistance to magnetic field
  - Need to be careful due to high neutron background
  - Contacting vendor for high radiation resistance designs (sensor + amp.)
  - Estimating neutron background @ photon detectors

---
Budget Update

---
Budget table
– calorimeter group version
+ Prototyping ~ 0.3 M$
Lab estimate : 5.7 (base)+3.8 (Labor)
JP : 6.2 (base) + 1.3 (Labor)

---
Budget Update

---
Budget table
– calorimeter group version
+ Prototyping ~ 0.3 M$
Lab estimate : 5.7 (base)+3.8 (Labor)
JP : 6.2 (base) + 1.3 (Labor)

---
What we need

---
What we need
Engineering support (Zhiwen)
  - Support structure
  - How to do maintenance and install it back
Inquiries
  - IHEP (Xiaochao)
  - Fiber connection (Mehdi)
  - Photon detectors (Zhiwen)
Background effect (Jin)
  - Event mixing with signal and background simulation
Prototyping

---
Support structure ideas
Overview
  - One support for LAEC, one support
  1. for FAEC
  - Only a few cm gap between outer radius of SIDIS LAEC and inner radius of cryo, is it enough?
  - Only a few cm gap between outer radius of FAEC and inner radius of nose cone, is it enough?
  - Need to consider the supporting with overall magnet cryo and yoke structure.
“super” Modules
  - Group 1-3 row of modules into supermodule
  - shift supermodule’s horizontal position to make layers

---
backup

---
WLS radiation hardness

---
Fiber connection (Backup option)
Fiber splicing
  - Robust connection and excellent transmission (2%)
  - CLAS12 Forward Tagger Hodoscope will fuse WLS and clear fiber. Commercial vendor has been contacted and They are also developing their own method.
  - We will collaborate with them to examine the labor and cost requirement.
joint