## Slide 1: SIDIS Polar-Angles Acceptance Gap from Calorimeter
Jin Huang
Los Alamos National Lab

## Slide 2: Where does the gap come from
Calorimeter defines the inner-R edge of large-angle acceptance
The proposal assumed a 2.5 degree polar angle gap (14.5-17)

## Slide 3: Contributions to the gap
Physical separation
  Ideally can be zero
Charged particle is bended
  Depending on the momentum, charged particle can be bended by <=1 degree on polar angle at calorimeter (1 GeV, θ=15 degree, z= 3.5m)
  The result is that gap range is momentum dependent. But gap size is similar for different momentum
Extended target
  Polar angle differs from front to back side of target tube by 1.5 degree
  The result is that gap range is momentum dependent. But gap size is similar for different Vz
Calorimeter induced gap
  May dominate the size of the gap
  Up to 2.5 degree

## Slide 4: Calorimeter-induced gap for default design
Geometry limits - 2.5 degree
  A 600-cm long calorimeter along z axis introduce 2.5 degree polar acceptance gap, within which track path through calorimeter but not full length
Shower size limits - ~ 1 degree
  Molière radius of calorimeter is ~0.8 degree, which corresponding to ~1 degree loss to contain full shower

## Slide 5: What if partial shower is contained
We can use partial shower to get E/p to certain extent:
  full designed length (20 X0), the pion rejection is 50-100:1
  75% of designed length (15 X0), we can still maintain ~30:1 rejection for preshower + shower
  60% of designed length (12 X0), we can get ~17:1 rejection for preshower + shower
  preshower length (4 X0), the preshower rejection is ~7:1

## Slide 6: Fixing the dominate gap – shower geometry
Triangle calorimeter
  Don’t expect it is possible to build
Shorter inner calorimeter modules
  May save half of the 2.4 degree gap
Rotate module
  Introduce gap in calorimeter, not favored
New idea: tilted modules

## Slide 7: Large Angle EC
We want to cover full azimuthal angle and leave no gap between modules, so module can not be tilted and need to be along Z axis
Prefer having short outer module so that the outer module area can cover more and inner module area can cover less
Inner module need to be special shape to avoid blocking acceptance. One way to solve it is to have smaller 5x5cm (like COMPASS) module with various length
24o
14.7o
inner module
(150mm in radius)
Outer module
(500mm in radius)
17.5o
Blue: LAEC acceptance angle
Orange : angle between inner and outer
600mm
600mm
5x5x41cm
10x10x60cm module
assume 600mm full module length
5x5x22cm

## Slide 8: “Shorter inner calorimeter modules” option cost
Module cost
  10x10cm module cost $1500 each (Bicron WLS fiber, not Kuraray Y11)
  5x5cm modules cost $750 each (Bicron WLS fiber, not Kuraray Y11)
Note: final number of module is to be determined by layout.
 | 5x5cm module | 10x10cm module
SIDIS LAEC number | 214 | 360
SIDIS FAEC number |  | 1140
PVDIS FAEC number |  | 1700
Total number | 214 | 1700
Total cost | 0.16M | 2.55M

## Slide 9: Tilted modules
Make the calorimeter layers progress larger from 1st layer to last (need ~ 200 molds)
Make the front and back side have same layout, but the back side is (3.5m+0.5m)/3.5m=114% larger
Stack the calorimeter in an angle like below
  Each module have different 2D – tilt, but same tile-set
  WLS fibers can be threaded through with hole diameter in scintillator is 0.7mm larger than the fiber
Compare to other tilt designs
  No calorimeter gap between modules
  Same set of mold for all calorimeter modules
Compared to Shorter inner calorimeter modules
  Pro: calorimeter always align neatly along the track direction
  Con:
    Need 200 molds – Few M$??
    Cannot simply share calorimeter module with forward calorimeters
    Mechanical support for each module is complex
15 degree
25 degree
Outter R=1.5m
Inner R=1.5m
tracks

## Slide 10: Conclusion
Polar angle gap mostly due to default calorimeter layout
An new calorimeter layout is proposed
  Align calorimeter always along track direction
  Cost is mainly 200 mold
The final decision probably between short inner module and new layout, balance gap and cost