## Slide 1: SoLID EC Design
2012/09

## Slide 2: Basic Features of Preliminary Design
Based on COMPASS Shashlyk module design.
0.5mm lead/1.5mm scintillator, 240 layers, 48.3 cm in length (20 X0)
  Reach energy resolution of 5%/sqrt(E) with good linearity
  Balance between resolution and longitudinal size
10x10cm of transverse size in square shape
  reach 1cm position resolution
  Balance between number of modules (cost), position resolution and background
  Total about 2000 modules.
Splitting : 5 X0 for preshower and 15 X0 for shower
  Maximizing e-pi separation (20:1 - 100:1 pion rejection depending on momentum)
100 WLS fibers/module
  1/cm2 fiber density to sample the EM shower
  Use KURARAY Y11 for higher radiation hardness and longer attenuation length or use Bicron fibers to save cost.
Readout options in orders of preference:
  Directly couple to PMT, if B-field permits
  PMT readout with WLS to clear fiber extension (with Winston cone or fuse-fiber connection) to out-of-B-field region
  APD/SiPM, if B-field is significant and if the radiation allows

## Slide 3: Preshower/Shower Design 1(preferred)
Preshower has 1 layer of 2X0 lead as passive radiator and 1 layer of a few cm scintillator with embedded WLS fiber for readout
.
Pros:
  Used by LHCb and Hermes
  Good hadron rejection
  No change to Shashlyk module prodution
  Preshower lead layer work as radiation shielding
  Significant reduction of the number of fibers for readout in preshower
Preshower (2X0 lead + scintillator)
Shower, 20-2 X0, Shashlik
Shower WLS fibers
Preshower WLS fibers

## Slide 4: Preshower/Shower Design 2
Preshower and shower have separate WLS for readout. Preshower WLS fibers bend and go back from the side.
Shower
Preshower
Shower WLS
Pros:
  Current COMPASS module production method unchanged.
Concerns
  Will the light loss in the preshower WLS fibers be too much due to the bending?
  Radiation damage on the fibers in front
Preshower WLS

## Slide 5: Preshower/Shower Design 3
Preshower and shower have separate WLS for readout. Preshower WLS fibers go to back through hollow supporting rods. The number of preshower WLS fibers is limited by the hollow rod diameter.
Shower
Preshower
Pros:
  Small change to COMPASS module production method
Concerns
  Will the light collected in the preshower be enough due to much fewer number of WLS fibers?
  Additional mold is required for preshower to allow WLS fibers to sample light.
Shower WLS
Preshower WLS
hollow rod

## Slide 6: Preshower/Shower Design 4
Preshower has thin WLS plate for readout and use embedded clear fibers to send signal at back. Shower has WLS for readout.
Shower
Preshower
Pros:
  Significant reduce number of fiber for readout in preshower.
Concerns
  No enough light collected by the pad due to light transmission in the thin scintillator layers limited within around 1cm?
  Somewhat bigger change to COMPASS module production method
Shower WLS
Preshower Clear fiber
WLS plate