## Slide 1: SoLID EC Design for IHEP
2012/10

## Slide 2: Basic Features of Preliminary Design
Based on COMPASS Shashlyk module design.
0.5mm lead/0.12mm air gap/1.5mm scintillator/0.12mm air gap
  Assume Lead X0=0.56mm, scintillator X0=42.4cm, air gap needs to be replaced with actual wrapping or coating.
  each layer 2.24mm(0.93X0), total 216 layers, 48.3 cm in length (20 X0)
  Reach energy resolution of 5%/sqrt(E) with good linearity
  Balance between resolution and longitudinal size
10x10cm of transverse size in square shape
  reach 1cm position resolution
  Balance between number of modules (cost), position resolution and background
  Total about 2000 modules.
Splitting : preshower and shower
  Maximizing e-pi separation (20:1 - 100:1 pion rejection depending on momentum)
100 WLS fibers/module
  1/cm2 fiber density to sample the EM shower
  Use KURARAY Y11 for higher radiation hardness and longer attenuation length or use Bicron fibers to save cost.
Readout options in orders of preference:
  Directly couple to PMT, if B-field permits
  PMT readout with WLS to clear fiber extension (with lightguide or connector) to out-of-B-field region
  APD/SiPM, if B-field is significant and if the radiation allows

## Slide 3: Preshower/Shower Design 1(preferred)
Preshower has 1 layer of 11.2mm (2X0) lead as passive radiator and 1 layer of 20 mm scintillator with embedded WLS fiber for readout
.
  Used by LHCb and Hermes
  Good hadron rejection
  No change to Shashlyk module prodution
  Preshower lead layer work as radiation shielding
  Significant reduction of the number of fibers for readout in preshower
Preshower (2X0 lead + scintillator)
Shower, 18 X0, Shashlik
Shower WLS fibers
Preshower WLS fibers
434.5mm (194 layers)
20mm
11.2mm
100mm ?
Total length 569mm ?
clear fibers
clear fibers
connector
connector
Not shown
Supporting rod

## Slide 4: Preshower/Shower Design 2
Preshower and shower have separate WLS for readout. Preshower WLS fibers bend and go back from the side.
Shower (15X0)
Preshower (5X0)
  Only small change to current COMPASS module production method
  preshower WLS fibers need to have bending radius > 70mm
  Radiation damage on the fibers in front, need shielding?
362mm (162 layers)
121mm (54 layers)
100mm ?
70mm?
clear fibers
clear fibers
connector
Not shown
Supporting rod
Total length 653mm ?

## Slide 5: Preshower/Shower Design 3
Preshower and shower have separate WLS for readout. Preshower WLS fibers go to back through hollow supporting rods. The number of preshower WLS fibers is limited by the hollow rod diameter.
Shower
Preshower
  change to COMPASS module production method
  Same or less number of WLS fibers in preshower than shower.
  0.7mm WLS fibers could be use instead of 1mm for preshower
  Add more supporting rods to 9 or 16
  Additional mold is required for preshower to allow WLS fibers to sample light
  Need more R&D
Shower WLS
Preshower WLS
hollow rod
Total length 583mm ?

## Slide 6: Preshower/Shower Design 4
Preshower has thin WLS plate for readout and use embedded clear fibers to send signal at back. Shower has WLS for readout.
Shower
Preshower
Pros:
  Significant reduce number of fiber for readout in preshower.
Concerns
  change to COMPASS module production method
  No enough light collected by the pad due to light transmission in the thin scintillator layers limited within around 1cm?
Shower WLS
Preshower Clear fiber
WLS plate

## Slide 7
SoLID PVDIS
EM Calorimeter
(forward angle)
GEM
Cherenkov
Baffle
Target
CLEO II Coil and Yoke

## Slide 8
EM Calorimeter
(large angle)
EM Calorimeter
(forward angle)
Target
GEM
Light Gas
Cherenkov
Heavy Gas
Cherenkov
CLEO II Coil and Yoke
MRPC
SC
Collimator
SoLID SIDIS and J/ψ

## Slide 9: Large Angle EC
We want to cover full azimuthal angle and leave no gap between modules, so module can not be tilted and need to be along Z axis
Prefer having short outer module so that the outer module area can cover more and inner module area can cover less
Inner module need to be special shape to avoid blocking acceptance. One way to solve it is to have smaller 4x4cm (like COMPASS) module with various length
24o
14.7o
inner module
(160mm in radius)
Outer module
(500mm in radius)
17.5o
Blue: LAEC acceptance angle
Orange : angle between inner and outer
600mm
600mm
4x4x43cm
4x4x32cm
4x4x27cm
10x10x60cm module
assume 600mm full module length

## Slide 10: Position resolution VS lateral size
Electron
Hadron
Blue: calorimeter modules along z axis
Red: calorimeter modules along central track
Shifted pion ΔR
Calorimeter theta angle coverage PVDIS (22-35), SIDIS(8-15,15-24)

## Slide 11: LHCb Calorimeter Preshower
LHCb used diamond mill to make curvy groove and glue WLS fibers in
Can curvy grooves be made with scintillator mold? Will it be cheaper compare to diamond mill cut?
Can straight grooves be made with scintillator mold? Will it be cheaper compare to diamond mill cut?

## Slide 12: How to bend WLS fibers from preshower scintillator pad?
WLS fibers come out of preshower scintillator pad and go back along module for readout.
To have large bending angle, let fibers go transversely first and then go longitudinally to back.
100mm
20mm
Red: straight part of fiber inside pad
Orange: Curvy part of fiber outside pad
Assume straight holes

## Slide 13: Impact to energy resolution from the passive preshower
Simulated with 2 X0 passive radiator and 2 cm scintillator as preshower
Minor degrade on energy resolution observed for our energy range
Passive preshower + 18 X0 Shashlyk
20 X0 Shashlyk

## Slide 14: Pion rejection comparisons
1/pion rejection with 94% electron eff.
Passive preshower + 18 X0 Shashlyk
20 X0 Shashlyk
Passive preshower show degrade on pion rejection for higher energy range