## Slide 1
SoLID EC
Zhiwen Zhao
2011/12/09

## Slide 2
Outline
Configuration
Requirements
Calorimeter design
Beam Test plan
Help we need

## Slide 3
SIDIS/PVDIS CONFIGURATIONS
SIDIS Large Angle
SIDIS Forward
Angle
PVDIS Forward
Angle

## Slide 4
Requirement
Pion rejection 100:1 (preshower/shower)
Energy resolution: 5~ 6%/√E
Position resolution: 1cm
Time resolution: 100-500ps
Radiation hardness: 400krad/year
Swap modules: layout
Readout outside of field: fiber connection

## Slide 5
Calorimeter Design: Best Option
Lead-Scintillator Sampling Calorimeter:
Shashlyk Calorimeter
Fibers collect and read out the light
  Great flexibility, tunable energy resolution: ~ 6%/√E is not a problem
Good radiation Hardness: ~ 500 krad
Well developed and mature technology: used previously
in other experiments

## Slide 6
Calorimeter Design: Lateral Size
Chart: 
| 2 | 4 | 8 | 10 | 16 | 20
Resolution. (cm) | 0.7042 | 0.7013 | 0.8373 | 1.029 | 2.045 | 2.99
Back Ground (%) | 0.36 | 0.64 | 0.64 | 1 | 2.56 | 4
Cost (M$) | 32.15 | 8.325 | 2.4 | 1.67 | 0.85313 | 0.68
block Size (cm)
Good Balance

## Slide 7
Calorimeter Design: Layout - Ring Sector
Excellent coverage
(no edge effect)
Small minimum number of
blocks but several molds
(~50 k each!)
Block size varies with the
radius, so does the position
resolution

## Slide 8
Calorimeter Design: Fibers
Fibers:
Wave Length Shifting fibers (WLS):
KURARAY Y11: - good attenuation length (3.5-4m),
(M.J. Varanda et al. / NIM in Phys. Res. A 453 (2000) 255}258)
- good radiation hardness : <30% loss of
light output after a 693 krad irradiation.
- Recovery: few percents after 10 days
Clear Fibers:
KURARAY clear PS, Super Eska…, options under study.

## Slide 9
Man power
Faculty
  Xiaochao Zheng
  Paul Reimer
Postdoc
  Zhiwen Zhao (UVa) preshower/shower, beam test
  Jin Huang (LANL) simulation
  Mehdi MEZIANE (Duke) layout, fiber

## Slide 10
Beam test plan
Goal
  Learn the modules, train personnel
  Test energy, position, time resolution
  Anchor simulation
Time now till next summer
(May shoutdown, July/Aug return module)
Location HallB under photon tagger
            (HallA option looked)
Stages
  Preparation readout,electronics, mouting
  Bench test gain match
  Beam test

## Slide 11
Test module
Used for CLAS TPE exp. Belongs to Will Brooks, located at ODU

## Slide 12
Old Readout housing
Used for CLAS TPE exp. Belongs to Will Brooks, located at ODU

## Slide 13
Readout
DVCS proton array readout, need to take them off
and make a adaptor or new housing because PMT is longer

## Slide 14
HallA test?

## Slide 15
HallB test setup
G14 runs at 2,4,5 GeV, two rounds, first round ends at end of Mar
Setup is independent of CLAS
HallD FCAL running test now with FADC ( no ending data) yet.
May borrow supporting structure

## Slide 16
HallD test supporting structure

## Slide 17
HallD test trigger box
http://www.flickr.com/photos/63927802@N02/6340030123/sizes/l/in/set-72157627993117345/
https://halldweb1.jlab.org/wiki/index.php/2011_Hall_B_FCAL_Beam_Test

## Slide 18
What we need
Write up a plan, and ask HallB with OSP later, taking
into consideration of other tests (HallD BCAL etc)
Making the adaptor for readout
Take the readout off and assembly with module
Make the mounting or the whole supporting structure.
Get electronics
Do test