## Slide 1: Solid/EIC GEM prototype assembling @UVa
Yuxiang Zhao, Kondo Gnanvo, Xinzhan Bai, Chao Gu, Nilanga K.Liyanage

## Slide 2: Design of Solid/EIC prototype
First 2D readout Chamber with this size
COMPASS-like 2D stereo angle (12°) U/V readout
Pitch = 550 μm, top strips = 140 μm, bottom = 490 μm

## Slide 3: Frames and GEM foil
Spacers: 300μm
Extra frame material for the alignment and
to hold the tension on GEM foil during assembly
 cut out after
GEM foil: 32 sectors on top, 16 each on 2 sides
2 sectors on bottom, 1 each on 2 sides

## Slide 4: Preparation for assembling---I
Clean and Coat the epoxy frames

## Slide 5: Preparation for assembling---II
HV test for GEM foil in a box filled with N2
  For each sector, 550V  ~1nA

## Slide 6: Assembling ---step 1: paste the 2mm frame onto the readout board

## Slide 7: Assembling ---step 2: stretch the GEM foil and paste 2mm frame onto the foil

## Slide 8: Assembling ---step 3: HV test for the foil again and paste it onto the base got in step 1

## Slide 9: Assembling processes
Step 1: page 6
Step 2: page 7
Step 3: page 8

## Slide 10: Solid/EIC prototype
HV Divider
And HV distribution board

## Slide 11: Gas flow
3mm
Gas
2mm
2mm
2mm
Mylar foil
2D Readout foil
Drift cathode
GEM 1
GEM 2
GEM 3

## Slide 12: Status of Solid/EIC prototype
Just arrived at Fermi lab
Will flow with N2 gas for several days
Setup for the beam test beginning at 1st OCT.