## Slide 1: Trigger and DAQ for SoLID SIDIS Programs
Yi Qiang
Jefferson Lab
for SoLID-SIDIS Collaboration Meeting
3/25/2011

## Slide 2: DAQ Requirement of SoLID-SIDIS
High Luminosity: 1036 cm-2 s-1
Record coincident 3He(e, e’h)X events

## Slide 3: Hall D L1 Trigger-DAQ Rate
Low luminosity (107 g/s in 8.4 < E < 9.0 GeV)
  20 kHz L1
High luminosity (108 g/s in 8.4 < E < 9.0 GeV)
  200 kHz L1
  Reduced to 20 kHz L3 by online farm
Event size: 15 kB; Rate to disk: 3 GB/s
Detectors which can be used in the Level-1 trigger:
SC
Forward Calorimeter (FCAL) | Energy
Barrel Calorimeter (BCAL) | Energy
Start Counter (SC) | Hits
Time of Flight (TOF) | Hits
Photon Tagger | Hits
Energy FCAL (GeV)
Energy FCAL (GeV)
Energy FCAL (GeV)
Energy BCAL (GeV)
Energy BCAL (GeV)
Energy BCAL (GeV)
Electromagnetic background
Hadronic E < 8 GeV
Hadronic E > 8 GeV
Basic Trigger Requirement:
EBCAL + 4 ∙ EFCAL > 2 GeV
and a hit in Start Counter

## Slide 4: Custom Electronics for JLab
VME Switched Serial (VXS) backplate
  10 Gbps to switch module (J0)
  320 MB/s VME-2eSST (J1/J2)
All payload modules are fully pipelined
  FADC125 (12 bit, 72 ch)
  FADC250 (12 bit, 16 ch)
  F1-TDC (60 ps, 32 ch or 115 ps, 48 ch)
Trigger Related Modules
  Crate Trigger Processor (CTP)
  Sub-System Processor (SSP)
  Global Trigger Processor (GTP)
  Trigger Supervisor (TS)
  Trigger Interface/Distribution(TI/D)
  Signal Distribution (SD)
FADC125
F1-TDC

## Slide 5: L1 Trigger Diagram
CPU
SSP
SSP
SSP
SSP
SSP
SSP
GTP
SD
SSP
SSP
SSP
SSP
SSP
SSP
TI
VXS Crate
SSP
CPU
FADC
FADC
FADC
FADC
FADC
FADC
CTP
SD
FADC
FADC
FADC
FADC
FADC
FADC
TI
VXS Crate
CPU
TD
TD
SD
TS
VXS Crate
TD
TD
TD
TD
TD
TD
TD
TD
TD
TD
SD
VXS Serial Link
16 bit @ 250 MHz: 4 Gbps
FADC250
12 bit @ 250 MHz, 16 ch
Sums amplitude from all channels
Transfer total energy or hit pattern to CTP
Crate Trigger Processor
Sums energies from FADCs
Transfer total energy or hit pattern to SSP
Fiber Optics
64 bit @ 125 MHz
SSP
CTP

## Slide 6: L1 Trigger Diagram
CPU
SSP
SSP
SSP
SSP
SSP
SSP
GTP
SD
SSP
SSP
SSP
SSP
SSP
SSP
TI
VXS Crate
SSP
CPU
FADC
FADC
FADC
FADC
FADC
FADC
CTP
SD
FADC
FADC
FADC
FADC
FADC
FADC
TI
VXS Crate
CPU
TD
TD
SD
TS
VXS Crate
TD
TD
TD
TD
TD
TD
TD
TD
TD
TD
SD
CTP
TS
Global Trigger Processor
Collect L1 data from SSPs
Calculate trigger equations
Transfer 32 bit trigger pattern to TS
VXS Serial Link
32 bit @ 250 MHz: 8 Gbps
Sub-System Processor
Consolidates multiple crate subsystems
Report total energy or hit pattern to GTP
Copper Ribbon Cable
32 bit @ 250 MHz: 8 Gbps
SSP

## Slide 7: L1 Trigger Diagram
CPU
FADC
FADC
FADC
FADC
FADC
FADC
CTP
SD
FADC
FADC
FADC
FADC
FADC
FADC
TI
VXS Crate
TI
CPU
SSP
SSP
SSP
SSP
SSP
SSP
GTP
SD
SSP
SSP
SSP
SSP
SSP
SSP
TI
VXS Crate
SSP
CPU
TD
TD
SD
TS
VXS Crate
TD
TD
TD
TD
TD
TD
TD
TD
TD
TD
SD
Trigger Supervisor
Calculate 8 bit trigger types from 32 bit trigger pattern
Prescale triggers
Transfer trigger and sync signal to TD (16 bit total)
VXS Serial Link
16 bit @ 62.5 MHz: 1 Gbps
Trigger Distribution
Distribute trigger, clock and synchronize signals to TI in each Crate
Fiber Optics
16 bit @ 62.5 MHz: 1 Gbps
GTP

## Slide 8: L1 Trigger Diagram
VME Readout Controller
Gigabit ethernet
CPU
TD
TD
SD
TS
VXS Crate
TD
TD
TD
TD
TD
TD
TD
TD
TD
TD
SD
TD
CPU
SSP
SSP
SSP
SSP
SSP
SSP
GTP
SD
SSP
SSP
SSP
SSP
SSP
SSP
TI
VXS Crate
SSP
CPU
FADC
FADC
FADC
FADC
FADC
FADC
CTP
SD
FADC
FADC
FADC
FADC
FADC
FADC
TI
VXS Crate
Signal Distribution
Distribute common signals to all modules: busy, sync and trigger 1/2
VXS Serial Link
4 bit @ 250 MHz: 1 Gbps
Trigger Interface
Receive trigger, clock and sync signals from TD
Make crate trigger decision
Pass signals to SD
TID

## Slide 9: L3 Farm
ROC
ROC
ROC
ROC
ROC
ROC
ROC
ROC
ROC
Front-End Crates
Read Out Controllers
~60 crates
~50MB/s out per crate
EB1
Event Builder
stage 1
EB1
Event Builder
stage 1
EB1
Event Builder
stage 1
EB2
Event Builder
stage 2
EB2
Event Builder
stage 2
Staged Event Building
blocked event fragments
partially recombined event fragments
N x M array of nodes (exact number to be determined by available hardware at time of purchase)
Level-3 Trigger and monitoring
full events
L3 Farm
node
node
node
node
node
node
node
Raid Disk
ER
Event Recorder
Event Recording
300MB/s in
300MB/s out
All nodes connected with 1GB/s links
Switches connected with 10GB/s fiber optics

## Slide 10: SoLID SIDIS Detector Rates
In 50 ns windows, 11 GeV
Detector | Rate | Hits | Type | Data Size per hit
GEM | 4.4 GHz | 220 | Hits (time) | 4 Byte x 2 (X/Y)
LC | 120 kHz | 1 | Energy, Hits | 8 Byte x 2 (PS/SH)
FC | 200 MHz | 10 | Energy, Hits | 8 Byte x 2 (PS/SH)
LGC | 40 MHz | 3 | Energy, Hits | 8 Byte x 2 (split)
HGC | 60 MHz | 4 | Energy, Hits | 8 Byte x 2 (split)
MRPC | 850 MHz | 45 | Hits | 4 Byte
SC | 300 MHz | 15 | Energy, Hits | 8 Byte
Total |  |  |  | 2.5 kB
With header and other over head
event size is ~ 4 kB

## Slide 11: L1 Trigger
Electron Singles Trigger:
  LC > 400 MeV|| (FC > 400 MeV && LGC)
  Total event rate: 190 - 240 kHz
  Frontend data rate: 800 – 1000 MB/s
  ROCs can barely handle this rate
    Assuming 10 VME crates, 100 MB/s per ROC
    add more crates since PVDIS uses > 30
  Maybe a little bit too much to write to the tape
  Not much room for improvement, already very close to electron yield.

## Slide 12: Reduce L1 Trigger: Two Options
Make coincidence with another charged particle in Forward detector
  FC > 200 MeV && MRPC && Scintillator
  Coincidence rate with 35 ns window ~ 50 kHz
Use L3 farm
  With powerful parallelism computing, we can easily reduce the rate by a factor of 5
  Reduce the difficulty to put MRPC (customized VME board) into the trigger logic
Both options give 200 MB/s data rate to the tape

## Slide 13: Estimated Channels
Detector | Total Channel | Front End Module | Number of Modules
GEM | 300 k ? | Customized VME | ?
LC | 180 | FADC250/F1-ADC | 12/6
FC | 360 | FADC250/F1-ADC | 23/12
LGC | 30 | FADC250 | 2
HGC | 30 | FADC250 | 2
MRPC | 3000 | Customized VME | ?
SC | 30 | FADC250/F1-ADC | 2/1

## Slide 14: Cost Estimation
Module Name | Unit Price | # of Modules | Total Cost
FADC250 | $ 4,000 | 41 | $ 164,000
FADC125 | $ 4,000 |  | 
F1-TDC | $ 4,000 | 19 | $ 76,000
CTP | $ 5,000 | 6 + ?? (4) | $ 30,000 + ??
SSP | $ 5,000 | 1 + ? (1) | $ 5,000 + ?
GTP | $ 5,000 | 1 | $ 5,000
TS | $ 5,000 | 1 | $ 5,000
TID | $ 3,000 | 10 + ?? (4) | $ 30,000 + ??
SD | $ 2,500 | 8 + ?? (4) | $ 20,000 + ??
VXS Crate | $ 8,000 | 8 + ?? (4) | $ 64,000 + ??
Total |  |  | $ 401,000 + ??? ($ 79,000)

## Slide 15: To Do List
Final VXS pair mapping has ben established, some collaborations already started their customized VXS payload modules based on it (e.g. GEM tracker of Super BigBite). We’d better start the same approach as well if we plan to use Jlab customized trigger system.
Optimize detector granularity, estimate number of channels of each detector.
Work with electronics and DAQ groups to acquire necessary support and hardware.

## Slide 16: Backup Slides

## Slide 17: The GlueX Detector
TOF
time of flight
SC
start counter
2.2T superconducting solenoidal magnet
Fixed target (LH2)
108 tagged g/s (8.4-9.0GeV)
hermetic
2.2 Tesla
Solenoid
Calorimetry
Barrel Calorimeter (lead, fiber sandwich)
Forward Calorimeter (lead-glass blocks)
PID
Time of Flight wall (scintillators)
Start counter
Barrel Calorimeter
Charged particle tracking
Central drift chamber (straw tube)
Forward drift chamber (cathode strip)

## Slide 18: GlueX Data Rate
 | Front End DAQ Rate | Event Size | L1 Trigger Rate | Bandwidth to mass Storage
GlueX | 3 GB/s | 15 kB | 200 kHz | 300 MB/s
CLAS12 | 0.1 GB/s | 20 kB | 10 kHz | 100 MB/s
ALICE | 500 GB/s | 2,500 kB | 200 kHz | 200 MB/s
ATLAS | 113 GB/s | 1,500 kB | 75 kHz | 300 MB/s
CMS | 200 GB/s | 1,000 kB | 100 kHz | 100 MB/s
LHCb | 40 GB/s | 40 kB | 1000 kHz | 100 MB/s
STAR | 50 GB/s | 1,000 kB | 0.6 kHz | 450 MB/s
PHENIX | 0.9 GB/s | ~60 kB | ~ 15 kHz | 450 MB/s
LHC
JLab
BNL
*
CHEP2007 talk
Sylvain Chapelin
private comm.
* Jeff Landgraf Private Comm. 2/11/2010
** CHEP2006 talk MartinL. Purschke
**

## Slide 19
fADC250
CTP Crate Trigger Processor
TI Trigger Interface
SD Signal Distribution
Detector
Signals
VXS Crate
VXS Crate
Trigger Distribution Crate
SSP
GTP
Fiber Optic Link
(~100 m)
(64bits @ 125 MHz)
(8)
(2)
(12)
TD
TS
(1)
TS
VXS Crate
Copper Ribbon Cable
(~1.5 m)
(32bits @ 250 MHz)
Fiber Optic Links
Clock/Trigger
(16bits @ 62.5MHz
Global Trigger Crate
Front-End Crate
VXS Backplane
(16)
(1)
(1)
(1)
(1)
(1)
Trigger Latency ~ 3 μs
(F1TDC pipeline ~3.9 μs)
( ) – Number in parentheses
refer to number of modules
Custom Designed
Boards at JLAB
Pipelined detector readout electronics:
fADC and F1TDC
Level-1 Trigger Electronics

## Slide 20: CODA3 – What’s different
CODA 2.5 | CODA 3
Run Control (X, Motif, C++) (rcServer, runcontrol) | Experiment Control – AFECS (pure JAVA) (rcPlatform, rcgui)
Communication/Database (msql, cdev, dptcl, CMLOG) | cMsg – CODA Publish/Subscribe messaging
Event I/O C-based simple API (open/close read/write) | EVIO – JAVA/C++/C APIs Tools for creating data objects, serializing, etc…
Event Builder / ET System / Event Recorder (single build stream) | EMU (Event Management Unit) Parallel/Staged event building
Front-End – vxWorks ROC (Interrupt driven – event by event readout) | Linux ROC, Multithreaded (polling – event blocking)
Triggering: 32 ROC limit, (12 trigger bits -> 16 types) TS required for buffered mode | 128 ROC limit, (32 trigger bits -> 256 types) TI supports TS functionality. Timestamping (4ns)

## Slide 21: FADC Encoding Example

## Slide 22: GTP Trigger Bit Example