## Slide 1
Calorimeter Design
for SoLID Project
Jin Huang, Mehdi Meziane, Zhiwen Zhao
Physics Division Review Session on SoLID Project
Sept 30, 2011, Jefferson Lab

## Slide 2: Outline
Requirement
Conclusion
Budget Estimation
Design Progress
Shashlyk calorimeter
Preshower/shower separation
Clear fiber connector

## Slide 3: Calorimeters for SoLID experiments
PVDIS forward angle
SIDIS forward angle
SIDIS large angle

## Slide 4: Requirement
Electron-hadron separation
  100:1 pion rejection in electron sample
  Energy resolution: σ(E)/E ~ 6%/√E
Provide shower Position
  σ ~1cm, for tracking initial seed / suppress background
Time response
  σ <~ few hundreds ps
  provide trigger/identify beam bunch (TOF PID)
Radiation resistant
  PVDIS forward angle
    EM <=2k GeV/cm2/s + pion (GeV/cm2/s), total ~<60 krad/year
  SIDIS forward angle
    EM <=5k GeV/cm2/s + pion , total, total ~<100 krad/year
  SIDIS large angle
    EM <=20k GeV/cm2/s + pion, total, total ~<400 krad/year
Notes: Back up slides pion/electron rate

## Slide 5: Best option: Shashlyk calorimeter
Shashlyk calorimeter
  Lead-scintillator sampling calorimeter
  Fiber collects and reads out light
Satisfy the SoLID requirement
  Good energy resolution (tunable)
  Radiation hardness ~ 500kRad
Easier to collect and read out the light
Well developed technology, many experiments
Typical Shashlik
Polyakov, COMPASS Talk, 2010
KOPIO

## Slide 6: Flexible Design of Shashlyk Detectors
Flexible design to customize for exp. needs
Experience collaborations contacted
  IHEP@Protvino (design & production), INR@Trozik (design), Uniplast (production)
  200 module/month mass production (~1500 needed)
Experiment | COMPASS | PANDA | KIPIO
Pb Thick/ Layer (mm) | 0.8 | 0.3 | 0.28
Sci Thick/ Layer (mm) | 1.5 | 1.5 | 1.5
Energy Res. a/sqrt(E) | 6.5% | ~3% | ~3%
Rad. Length, X0 (mm) | 17.5 | 34 | 35
Total Rad. Length (X0) | 22.5 | 20 | 16
Moliere radius (mm) | 36 | 59 | 60
Typical Detecting Energy | 101~102GeV? | <10GeV | <1GeV
Trans. Size (cm) | ~4x4 | 11x11 | 11x11
Active depth(cm) | 400 | 680 | 555

## Slide 7: Tuning for SoLID/Lead-Sci Ratio
  Dedicated Geant4 MC developed
  Reach 100:1 pion rejection w/ Pb thick =0.6mm/Layer
p (GeV)
p (GeV)
Electron Efficiency
1/(Pion rejection)
97%
100:1 Rejection
Active:
3~7 GeV

## Slide 8: Tuning for SoLID/Lateral Size Rough numbers
Chart: 
| 2 | 4 | 8 | 10 | 16 | 20
Resolution. (cm) | 0.7042 | 0.7013 | 0.8373 | 1.029 | 2.045 | 2.99
Back Ground (%) | 0.36 | 0.64 | 0.64 | 1 | 2.56 | 4
Cost (M$) | 32.15 | 8.325 | 2.4 | 1.67 | 0.85313 | 0.68
block Size (cm)
Good Balance

## Slide 9: Layout map
Square 10*10 cm
Hexagon
Ring Sector
Square 10*10 cm
Preferred
Also studied

## Slide 10: Preshower/shower
Preshower-shower separation for better electrion ID
Options
  Curve fiber from front, example (ZEUS) below
  Run fiber through shower part within light-protected tube
  Run preshower fiber (separately) to outside magnetic field
ZEUS forward Cal.
Bamberger, NIM, 2000

## Slide 11: Photon Readout Options
Large angle calorimeter
  Prefer transporting photons to outside magnetic field
  No field/PMT read out/easy to maintain
Forward calorimeter
  In field readout (<~100G), PMT with mu-metal shielding
  Transport photons to outside end cap
  Options still under study.
Fiber connectors and clear fiber
  Clear fiber are cheaper, w/ longer attenuation length
128-fiber connector
LHCb

## Slide 12: Budget (preliminary)
Experiment | Angle(degree) | Radius(cm) | Area(m2) | Number of modules | Module cost (M$) | Fiber Extension (M$) | PMT+ support (M$) | Total cost
PVDIS (forward angle) | 22-35 | 110-258 | ~10 | 1000? ~Baffle design | 1.5 | 0 | 0.6 | 2.1
SIDIS (forward angle) | 9-15 | 107-202 | 11 | 948 |  |  |  | 
SIDIS (large angle) | 17-24 | 82-141 | 5 | 460 | 0.8 | 0.3(?) | 0.3 | 1.4
+Support structure: 0.2M$ (?)
10x10cm Shashlyk module costs about $1~1.5K each
PVDIS : factor 0.5 reduction due to only covers ~half of azimuthal angle, which depends on baffle design.
PVDIS and SIDIS forward angle calorimeter will rearrange modules

## Slide 13: Summary
Shashlik calorimeter is the best option
  Good energy resolution/Radiation resistant/Concentrated photon output/Matured production
Tuning the design for SoLID
  Tuning Pb-Sci ratio/Preshower-shower thickness/lateral size and shape/layout
Exploring new features
  Preshower/shower splitting/clear fiber extensions