## Slide 1: New Technologies for Cherenkov Light Detection: Hadron Blind Detector Thomas K Hemmick Stony Brook University
SoLID Collaboration Meeting
October 14, 2011

## Slide 2: The HBD Team
Brookhaven National Lab: B. Azmoun, R. Pisani, T. Sakaguchi, A. Sickles, C. Woody
Columbia University: C.-Y. Chi
Stony Brook University: W. Anderson, Z. Citron, M. Connors, J. M. Durham, T.Hemmick, J. Kamin, B. Lewis, M. Proissl, J. Sun, V. Pantuev,
University of California, Riverside:
A. Iordanova, S. Rolnick, R. Seto
Weizmann Institute of Science: A. Dubey, Z. Fraenkel, A. Kozlov, A.Milov,
M. Naglis, I. Ravinovich, D. Sharma,
I. Tserruya

## Slide 3: Lepton-Pair Continuum Physics
Axel Drees
known sources of lepton pairs at s = 200 GeV
Modifications due to QCD phase transition
Chiral symmetry restoration
continuum enhancement
modification of vector mesons
thermal radiation
& modified heavy flavor
suppression
(enhancement)
Sources “long” after collision:
  p0, h, w Dalitz decays
  (r), w, f, J/y, y‘ decays
Early in collision (hard probes):
  Heavy flavor production
  Drell Yan, direct radiation
Baseline from p-p
Thermal (blackbody) radiation
  in dileptons and photons
  temperature evolution
Medium modifications of meson
  pp  r  l+l-
  chiral symmetry restoration
Medium effects on hard probes
  Heavy flavor energy loss
3

## Slide 4: Key Challenge for PHENIX: Pair Background
Axel Drees
No background rejection  Signal/Background  1/100 in Au-Au
Combinatorial background: e+ and e- from different uncorrelated source
  Need event mixing because of acceptance differences for e+ and e-
  Use like sign pairs to check event mixing
4
>100x

## Slide 5
Why don’t we Spot Background?
Typically only 1 electron from a pair falls within the PHENIX acceptance.
  The magnetic field bends the pair in opposite directions.
  Some spiral in the magnetic field and never reach tracking detectors.
~12 m
To eliminate these problems:
Detect electrons in field-free region near beampipe
Need >90% efficiency

## Slide 6: Separating Signal from “Background”
π
φ
pads
relativistic electrons
Spectrum from photon conversion tightly peaked around 2me
Mass spectrum from pion Dalitz decays peaked around 2me
Opening angle can be used to cut out photon conversion and Dalitz decays
→MUST BE ABLE TO DISTINGUISH SINGLE HITS (“INTERESTING” ELECTRONS) FROM DOUBLE HITS (DALITZ AND PHOTON CONVERSION).
Heavier meson decays have large opening angles

## Slide 7
Looking Closer…
Inner coil can cancel B-field at r < 60 cm
Not enough room for traditional optics… mirrors won’t work.
Just put the detector right in the middle of things!
Has potential, but…
  must be thin
  must detect a single UV photon and still be blind to all ionizing particles passing through it!!!

## Slide 8: Unfocused Cherenkov “Blobs”
Cherekov Radiation
e-
Windowless: Radiator Gas = Avalanche Gas
  CF4 (n≈1.000620)
  Blind to hadrons w/ <4 GeV
Some challenges:
No room for traditional optics (ie. focusing mirror).
Cherenkov light collected as an unfocused blob.
1.5 m^2 photosensitive region
Low radiation length:
  minimize photon conversions.
Charged particles from collision will pass through:
  ionization must not interfere with photoelectron detection.

## Slide 9
Gas Electron Multiplier (GEM)
Two copper layers separated by insulating film with regular pitch of holes
Just add the photocathode
HV creates very strong field such that the avalanche develops inside the holes
By the way: no photon feedback onto photocathode
150μ
The original idea by F.Sauli (mid 90s) US Patent 6,011,265
Traditionally CHARGED PARTICLE detectors (not photons)
80μ

## Slide 10
Watch the Magic…
Start with a GEM
Put a photocathode (CsI) on top
photoelectron from Cherenkov light avalanches in the high density E-field
Use more GEMs for larger signal
Pick up the signal on pads
What about ionizing particles (hadrons)?
We need a mesh with a reverse voltage on it to blow electrons away!!!
HV
We have a detector sensitive to UV and blind to ionizing particles!
~150 μm

## Slide 11: Ways to use GEM stacks
Mesh
CsI layer
Triple
GEM
Readout Pads
e-
primary
ionization
g
HV
photo
electron
Readout Pads
charged
particle
or photon
primary
ionization
HV
Lateral spread of avalanche is ~500 μm, thereby limiting resolution.
Single electron gain ~104
Reverse Bias (HBD)
Forward Bias
Limited by the transparency of gas
CF4, ~1-12 eV photons
Limited by the absorption of gas

## Slide 12: Hadron Blindness: UV photons vs charged particles
At slightly negative Ed, photoelectron detection efficiency is preserved whereas charge collection is largely suppressed.
Charge collected from ~150μ layer above top GEM
Target Ed ~0.1 kV/cm

## Slide 13
Dilepton pair
Beam Pipe
HBD Gas Volume: Filled with CF4 Radiator (nCF4=1.000620, LRAD=50 cm)
Cherenkov light forms “blobs” on an image plane
(rBLOB~3.36cm)
Triple GEM detectors
(12 panels per side)
Space allocated for services
Windowless Cherenkov Detector
Radiator gas = Avalanche Gas
Electrons radiate, but hadrons with
P < 4 GeV/c do not
Pcb pad readout (~ 2x2 cm2)
5 cm
55 cm
e-
e+
q
Pair Opening
Angle
The HBD Detector
CsI photocathode covering GEMs

## Slide 14: Mechanical Detail

## Slide 15: Radiation Budget

## Slide 16: The Clean Tent at USB
Entrance Foyer
“Class” of Clean Room
evaporator
GEM
storage vessel
laminar flow hood
(“Class”: number of ≤0.5 μm particles/m3)
glove box

## Slide 17: Preparation for Evaporation
Cleaning GEMs:
GEMs are “de-dusted” with Ar
Installation into Evaporation Box:
GEMs mounted in evap box
leads connected underneath
test-chicklets installed
READY FOR EVAPORATION

## Slide 18: The Evaporator
Evaporation Chamber
Quantum Efficiency Station
Magnetically coupled driver for moving the GEMs inside the vacuum.
on loan from INFN Roma

## Slide 19: The Evaporation Chamber
~24 hrs to pump down vessel
vacuum ~10-7 mbar
  no water!!
Evaporate 4 GEMs simultaneously
Molybdenum boats
GEM
GEM mounting box w/ wheels on track
Harpoon for moving mounting box
CsI
AC
Boats are in series so they must be brought up to temperature slowly (~10 min)
250 – 450 nm layer of CsI at rate of ~2 nm/sec

## Slide 20: The Quantum Efficiency Station
GEM with CsI
Molybinum boats
GEM mounting box w/ wheels on track
Harpoon for moving mounting box
AC
γ
e-
e-
~ 100 V
~ 2mm
ampmeter
GEM w/ CsI
mirror
reference PMT
mesh
(e- collection)
D2 lamp
(λ=160,185,200 nm)

## Slide 21: QE System
Quantum Efficiency:
LabView DAQ interface
records:
  Photocathode Current
  Reference PMT Current
  Mirror Orientation
  Y-coordinate (manually)
  X-coordinate (automatically)
String potentiometer
Revamped QE:
Can this system be made user-friendly??
Of Course!!

## Slide 22
Relative QE
(results from the evaporator)
Encouraging results:
Highly uniform QE across GEMs.

## Slide 23
Encouraging results:
Highly uniform QE across GEMs.
Chicklet results confirm high QE.
Absolute QE
(results from BNL)
10 eV
6 eV

## Slide 24: Railroad System “low rider”
Chuggin’ along on the railroad:
After flushing the foyer,
Transport box rolls effortlessly out of the airlock...
…and into the glovebox.
To reach over the edge and inside transport box, the “low rider” system was developed.

## Slide 25: Electric Lift System (1)
Where to store the lid of the transport box??
Transport box lid is big and cumbersome.
Nowhere to set the lid down during GEM extraction.
And, of course,
out of the transport box…
…and into the HBD!
…nowhere but UP, that is!!!

## Slide 26: Monitoring QE over Time
Lucite with Al/MgF2 coating
Coincidence of SSB and pads
We can measure CF4 scintillation at 160 nm.
Gain is calibrated using an 55Fe source.
No loss of QE over two year period!

## Slide 27: Gas System Quality VITAL!
5 lpm!
Stay below 10 ppm O2 and H2O

## Slide 28: Transmission Scans
HBD-CF4 @ 4.5lpm (Recirculation mode, incl. scrubbing)
Maintained ~90% integrated transparency over full run.
Notes: 28

## Slide 29: Gain Monitor/Stability
Gain is monitored live via scintillation.
P/T (n/V) corrections applied via High Voltage

## Slide 30: Hadron Response
The HBD response to hadrons:
  Landau in Forward Bias
  “Blind” in reverse bias.
Pedestal
Scintillation
MIPs
Scintillation produces single photo-electron signals.
Provides ABSOLUTE gain measurement.
Cosmic ray triggers

## Slide 31: Electron Response

## Slide 32: Letter of Intent for Detector R&D Towards an EIC Detector
TK Hemmick for the EIC Tracking R&D Group
Brookhaven National Laboratory
Florida Institute of Technology
Iowa State University
Lawrence Berkeley National Laboratory
Massachusetts Institute of Technology
Riken Research Center at BNL
Stony Brook University
Temple University
University of Virginia
Yale University

## Slide 33: Brookhaven Lab
Hadron-Blind Detector
Chevron charge division
Fast drift/low mass TPC
ASIC development
VUV spectrometry

## Slide 34: Florida Institute of Technology
Single-mask GEM cross section
CERN workshops
CMS High-h GEM Upgrade
RD51 SRS readout System
Large-Area GEM production

## Slide 35: University of Virginia
Prototype GEM tracker tested at Jlab now
Super Big Bite
SoLID
prototype tracker prepared for beam test.

## Slide 36: Yale University
Forward GEM Tracker
Developed Strip-pixel readout system.
Short term proposal:
  3-coordinate strip-pixel readout.

## Slide 37: Strip-pixel R&D
Position by charge division (~100 mm).
Readout count set by occupancy:
  2D uses X-Y charge matching allows up to 10 particles per “patch”
  3D uses chg & GEOMETRY matching requires R&D to determine limit.
STAR FGT
COMPASS
PROPOSED
NOTE: Redundancy “hardens” detector against failure.

## Slide 38: Stony Brook University
Hadron-Blind Detector
Large Clean Room
Gas Chromatography
CsI Photocathodes

## Slide 39: PID via Cherenkov Angle
Ring Radius determines qc

## Slide 40: Barrel Concept (‘ala ALICE HMPID)
Proximity-focused RICH.
Liquid Radiator.
New concept:
  CsI GEMs for readout instead of wire avalanche.
  Improved HV stability.
  Reduced Hadron response

## Slide 41: Forward Concept 1…Multi-Radiator RICH
Threshold Device.
BIG blob from C4F8O (~10 cm)
Small blob from CF4
Even though concentric get two thresholds…
C4F8O
Windowless
CF4
CaF2
Momentum | C4F10 | CF4 | Particle id.
3 < p < 5 | 1 | 0 | Π
5 < p < 9 | 1 | 1 | Π
9 < p < 16 | 1 | 1 | Π
 | 1 | 0 | K
 | 0 | 0 | p
16 < p < 30 | 1 | 1 | Π,K
 | 1 | 0 | p

## Slide 42: Forward Concept 2 – Forward RICH & Blob
Rings from CF4…Blobs from C4F8O
PID to ~20 GeV.
Other variations possible including using liquid radiator for lower momentum PID.
CAUTION! Mirrors are not perfect!

## Slide 43: Commercial (small) mirror Reflectivities
Bare aluminum mirrors no good (AlO…high cutoff).
Better has MgF2 overcoat (right hand).
  Exists and has been made to large scale.
Thin film(?) goes REALLY low.
  Can this be made larger than 2” diameter?
 | n | lambda | p.e. per meter | p.e. MgF2 | p.e. quartz
CF4 | 1.00062 | 108 | 108 | 33 | 6.4
C2F6 | 1.00094 | 150 | 32 | 32 | 9.7
C4F10 | 1.001444 | 160 | 29 | 29 | 15
C4F8O | 1.001389 | 175 | 9.6 | 9.6 | 9.6
NOTE: Idealized… reality is half

## Slide 44: Particle ID…
C4F10 and CF4 mixed radiator cherenkov angles.
E-pi separation clearly requires EMCal (not cherenkov).
Good pi-K-p PID to about 20 GeV.

## Slide 45
The older unit with a mirror is better for next stage of R&D.
Larger rings will require some mods (or just capture a fraction of a ring.
OTHER EQUIPMENT:
  High Purity High Flow recirc. Gas system.
  Gas Chromatograph

## Slide 46: Ideas for Hall A Testing
Standard RD51 10x10 chamber
Comes with 4x128 channels readout.
Full SRS readout chain.
Total cost $4k
Replace entrance window with Al flange.
Attach to existing vacuum/gas vessels.
Blobs
Rings

## Slide 47: Summary
R&D will be done putting 10x10cm2 GEMS paired with a mirror using vacuum vessels from prior efforts.
Test beam will be taken at J-Lab using resources from our friends:
  J-Lab existing resources.
  SBU portable high purity gas system
  Perhaps SRS systems?
Clear interest for EIC.
Possible interest for SoLID
Join forces and address both needs!

## Slide 48
R1
R1
R2
R2
R2
R2
R2
2R2
R1
Mesh to Top GEM Sparking
Two separate power supplies per stack allows for flexibility between FB and RB
But following a GEM trip, a V gap built between the Mesh and top GEM creating a spark.
R1 = 2.2 MΩ, R2 = 10 MΩ, Vin = 3720 V, dV/GEM = 500V, Ichain = 150 μA
HV
HV + bias
TRIP!!
Led to damage of top GEMs
Grid patterned “burns” line up with mesh.
Optical coupling between modules led to multiple stacks tripping simultaneously.
removed capacitors (reducing stored energy)
double zener diode btwn mesh-top GEM.
Damage made GEM stacks inoperable
→Insufficient active area to do physics in Run 7.
→Forced us back into construction with new GEMs

## Slide 49: Improvements
Better understanding and control of the HV system.
  Adust transfer gap V (between GEMs), allows higher gain w/out increasing GEM voltage
  Improved trip procedure
Operating at a less severe reverse bias will allow us to improve the photoelectron yield.
Higher gas flow will improve transmission.
Photoelectrons
~20% potential light gain
~25% gain increase w/out more GEM stress
Relative Gain
Drift gap
Transfer gap

## Slide 50
E-Field Line Directions
Forward Bias
Reverse Bias
Lines go to mesh
Lines go to pad
Lines go to GEM bottom
In this simulation…
electrons were created at the surface of the GEM.
electron path follows E-Field lines
recorded PE’s final destination.
Reverse Bias (-30V):
most (~91%) e’s from the GEM surface end up on pads.
~3% are swept up to mesh.
~6% lost to GEM bottom.
note:
field line destinations and actual charge destinations are different due to diffusion and avalanche.
Line density does NOT represent field strength!

## Slide 51
E-Field Line Directions
Reverse Bias
For an intuition of what different negative drift fields look like…
notice that “reverse bias” doesn’t turn on immediately
Lines go to mesh
Lines go to pad
Lines go to GEM bot
Line density does NOT represent field strength!

## Slide 52: Experimental results
Hadrons (actually 55Fe) drop suddenly in efficiency as bias goes reverse.
Photon-electrons fall off slowly with increasing reverse bias.
HBD will operate best when placed “just barely” into the reverse bias mode.
Since voltages are roughly 4000 V, need 0.1% precision to get bias correct to 4V!!!
55Fe
Scintillation

## Slide 53: Spectra in Beam
Spectra show two components:
  Single Scintillation Electrons (expo)
  MIP (Landau)
Scintillation
MIPs
FORWARD
REVERSE

## Slide 54: Goal List for HBD
Forward/Reverse threshold (standalone):
  Change bias step-by-step.
  Search for loss of MIP peak.
  DONE (and we thought this would be hard)
Gain Calibration (Standalone):
  Observe scintillation signal in every channel.
  Fit scintillation slope to get gain.
  Adjust voltages to get nearly uniform gain.
  DONE (better than 10%...WOW)
High Statistics Reverse Bias (tracking)
  Determine Hadron Response.
  Determine isolated electron response.
  Determine “double” electron response.
  DONE (excellent Results)

## Slide 55
DV Scan
Color scheme
RUN LINE COLOR BIAS
274058 Red +30V
059 Black 0V
060 Green -5V
061 Blue -10V
062 Yellow -15V
063 Magenta -20V

## Slide 56
EN1 -15V
EN2 -10V
EN3 -15V
EN4 -10V

## Slide 57: Important for Detector Design
Detector must be multi-purpose
  One detector for inclusive (ep -> e’X), semi-inclusive (ep->e’hadron(s)X), exclusive (ep -> e’pp) reactions in ep/eA interactions
  run at very different beam energies (and ep/A kinematics)
  Ep/A/Ee ~ 1 – 65  HERA: 17 – 34; lepton beam energy always 27GeV
Inclusive DIS:
  with increasing center-of-mass energy lepton goes more and more in original beam direction
  high Q2 events go into central detector
  low Q2 events have small scattering angle and close to original beam energy
  need low forward electron tagger for low Q2 events
  low-mass high resolution trackers over wide angular acceptance
Semi-Inclusive DIS
  hadrons go from very forward to central to even backward with lepton beam energy increasing
  good particle-ID over the entire detector
Exclusive Reactions:
  decay products from excl. r / f / J/ψ go from very forward to central to even backward with lepton beam energy increasing

## Slide 58: Emerging Detector Concept
high acceptance -5 < h < 5 central detector
good PID and vertex resolution (< 5mm)
tracking and calorimeter coverage the same  good momentum resolution, lepton PID
low material density  minimal multiple scattering and brems-strahlung
very forward electron and proton detection  dipole spectrometers
low Q2 e’ Spectrometer:

## Slide 59: Why a LOI Response to a Call for Proposals?
Tracking and PID technologies must be driven by the physics goals of the EIC, not by the technology du jour.
Detector performance a “coupled problem”
  E vs hadron for Q^2
  Tracking provides “some” PID.
  Cherenkov is velocity measure through BOTH TOF and Ring
Success will be defined by
  Gathering a community that cross-cuts R&D with physics.
  Use diverse experience to formulate reasoned plans.
Our Letter of Intent:
  Announces a fledgling community taking on this task.
  Contains requests for small scale “seed grant” work.
  Promises a full R&D tracking proposal in one year’s time.

## Slide 60: CsI Photocathode Research
The Stony Brook group wishes to investigate the feasibility of CsI-coated GEMs as a large area, B-field tolerant solution for RICH work.
Operating in CF4 the PHENIX HBD detector demonstrated the highest measured N0 (327) of any large Cherenkov Detector.
However, there are limitations due to the sensitivity range of CsI (110 – 200 nm).
  Windows provide provide higher cutoff.
  Most (not all) optics for reflection provide higher cutoff.
  Aerogel opaque in VUV