## Slide 1: SIDIS Cherenkov Detectors
Haiyan Gao, Gary Swift, Simona Malace (Duke U.)
Zein-Eddine Meziani, Eric Fuchey (Temple U.)
SoLID Collaboration Meeting, October 14-15 2011, JLab

## Slide 2
Outline
Requirements: 2 Cherenkov detectors for positive identification of electrons and pions
Design
 Mirrors
 Photon detector options: GEMs + CsI , PMTs
Detectors performance
 The electron Cherenkov: collection efficiency and signal
 The pion Cherenkov: work in progress

## Slide 3
SIDIS electron Cherenkov: 1.5 – 4.5 GeV
SIDIS pion Cherenkov: 2.5 – 7.5 GeV
Threshold Cherenkov:
electron-pion separation
pion-kaon/proton separation
2p coverage (SIDIS)
Perform in non-negligible magnetic field environment
Simple design: cost effective, easy to install, operate
Requirements
don’t care about performance below 1.5 GeV
positive identification of electrons
CO2, CF4 would work as radiator
gas length available: ~ 2 m (kinematics dependent)
positive identification of pions
C4F8O at 1.5 atm would work as radiator
gas length available: ~ 0.9 m (kinematics dependent)

## Slide 4
Optics: Spherical Mirrors
Purpose: focus on small size photon detectors + ensure good 2p coverage
How we “make” them: using the “small spread around the central ray” approximation
Input: xi (central ray) and xr (the photon detector coordinates)
Output: radius of sphere (mirror curvature) and position of its center
The mirror size is defined by the polar angular acceptance that needs to be covered and number of sectors (30)*
*SIDIS doesn’t need sectoring but PVDIS does
Cone section with size defined by the min and max polar angles intersects sphere of radius R to cut out one of the 30 spherical mirrors

## Slide 5
GEMs + CsI (used by PHENIX)
 CsI: sensitive to deep UV light, high quantum efficiency (up to 60-70% at 110 nm)
 Insensitive to magnetic field
We need:
Pure gas transparent to UV light
Mirrors with good reflectivity in deep UV
PMTs
 Sensitive to magnetic field
 Photocathodes typically sensitive to visible light mostly
Resistant in SoLID magnetic field
Suitable for tilling
Photon Detectors
We need PMTs:
H8500C-03
Other: we ‘ll keep looking

## Slide 6
The Electron Cherenkov (PMTs): Design
4”
4”
Radiator: CO2
Mirror: 30 spherical mirrors in 2 parts each*  2 rings of mirrors: inner and outer
Photon detector: now 4 2” H8500C-03 per sector in 2 by 2 arrays
Winston cones
*mirror splitting for manufacturing & coating purposes (see Eric’s talk)
 benefit: make each part of different curvature; went from 9 to 4 PMTs per sector (saves cost: 1 PMT = $3000)
 “exciting opportunity”: make them of light and rigid material to remove the need for double edge support
No impact on physics phase space

## Slide 7
Cherenkov Mirrors: Material & Support
Mirrors: light & rigid material so no double-edge support would be needed
Options: glass-coated beryllium technology & carbon fiber technology
Both extensively studied/tested at CERN for the RICH LHCb
(the carbon fiber was chosen: delivery time and cost)
support
no support
12 deg: cone of photons reflect on both mirrors (boundary)

## Slide 8
Cherenkov Mirrors: Material & Support
Mirrors: glass-coated beryllium
LHCb prototype (made in Russia): central point support on the beryllium rim (single bolt)  maximum deflection of the mirror due to gravity = 160mm
0.4 m x 0.6 m
R = 2.7 m
Advantages: radiation hard, fluorocarbon compatibility, non-magnetic, light-weight, good rigidity
20 mm thick beryllium rim at one edge to support it
3 mm beryllium
0.5 mm glass
Disadvantages: high manufacturing costs + high toxicity (requires special safety measures during manufacturing and handling)
Nuclear Instruments and Methods in Physics Research A 595 (2008) 197–199
Prototype for LHCb
Without glass (+ Al) coating, poor reflectivity in visible and UV: 50%;
with glass (+ Al) coating: 90% for l > 200 nm

## Slide 9
Cherenkov Mirrors: Material & Support
Mirrors: carbon fiber reinforced polymer (CFRP)
Nuclear Instruments and Methods in Physics Research A 593 (2008) 624– 637
70% carbon-fiber (reinforcement material) + 30% resin (binds the fibers together)
Advantages: same as glass-coated beryllium + considerably cheaper, with no safety implications
0.835 m x 0.64 m
33 mm thick
R = 2.7 m
LHCb mirrors
LHCb mirrors (made by CMA, US):
sandwich honeycomb structure: two outer CFRP layers (1.5 mm) + core cells in-between as reinforcement
reflectivity with Al + MgF2 coating: ~90% for l > 200 nm
May be a good choice for SoLID Cherenkovs
We need to:
Find best way of supporting CFRP mirrors (Gary)
Ask CMA (for example) for a quote
get good reflectivity below 200 nm as well

## Slide 10
The Electron Cherenkov (PMTs): Collection Efficiency
Good collection efficiency with 4 PMTs per sector + no support between the 2 mirror rings
Over 98% at most kinematics; ~90% at the lowest polar angle
Over 98% at most kinematics; over 95% at the highest polar angle
Over 98% regardless of the kinematics
12 deg

## Slide 11
The Electron Cherenkov (PMTs): Focusing
Examples
2 ways of loosing light

## Slide 12
The Electron Cherenkov (PMTs): Signal
Estimates include:
wavelength dependent corrections (Q.E. of H8500C-03 + mirror/Winston cone reflectivity)
effect of PMT window (Eric implemented that)
additional overall reduction of 0.7
(accounts for dead zone that result from tiling +…)
tile

## Slide 13
click me
The Electron Cherenkov (PMTs): Performance vs. F
click me
Fairly small effect at the “edge” of angular acceptance
12 deg
14.3 deg

## Slide 14
Dark area inside the shield = PMT array location
Request sent to Amuneal for “ideal” shield which will incorporate the Winston cones
longitudinal component of the magnetic field from 150 G to < 20 G
transverse component of the magnetic field from 70 G to 0 G
Estimates based on BaBar v4 field map
Amuneal:
possible with a 2 layer shield
Winston cone substantially more expensive than straight cone ($1350 per cone)
 inner: Amumetal 0.04”
 outer: 1008 carbon steel 1/8”
 mylar in between 0.062”
Ideal
could be higher though
(< 50 G)
at 20 G (longitudinal field): < 10% signal loss
at 70 G: 30%
From H8500C field tests at Temple U.
H8500C-03 in SoLID Magnetic Field
Need to check with simulation if we could use straight cones

## Slide 15
H8500C-03: Tentative Plan for Test in Hall A
Background on PMT window of concern
sum over all anodes would be fine but we could also take advantage of the pixeling and use coincidence between pixels to “cut” background
would like to test this approach during g2p
Place the PMT in a dark box with some shielding somewhere between 29 and 45 deg

## Slide 16
23 cm X 27 cm
(PHENIX size)
The Electron Cherenkov (GEMs+CsI): Design
Very similar configuration possible for SIDIS and PVDIS
same tank except for additional piece for SIDIS
same mirrors, mounted at the same location
same GEMs + CsI, mounted at different locations
same gas: CF4
14.3 deg, ztarget = -20 cm, p = 1.5 GeV
Not cost efficient to make mirrors of different curvatures

## Slide 17
The Electron Cherenkov (GEMs+CsI): Signal
Takes into account wavelength dependent corrections (mirrors reflectivity, gas absoption, Q.E. of CsI)
+
an additional multiplicative correction of 0.5 – the PHENIX factor - (optical transparency of mesh and photocathode, radiator gas transparency, transport efficiency etc.)

## Slide 18
48%
38%
B. Azmoun et al., IEEE TRANSACTIONS ON NUCLEAR SCIENCE, VOL. 56, NO. 3, JUNE 2009
Used in our simulation
65%
45%
PHENIX
The Electron Cherenkov (GEMs+CsI): CsI Q.E.
Wavelength-dependent corrections: CsI Q.E. + gas transparency
arXiv:1103.4277v1
We stop here

## Slide 19
The Electron Cherenkov (GEMs+CsI): Mirror Reflectivity in far UV
NIM A300 (1991) 501-510
1971 / Vol. 10, No. 3 / APPLIED OPTICS
Used in simulation
Wavelength-dependent corrections: mirror reflectivity

## Slide 20
Mirrors Reflectivity in far UV
Depends on angle of incidence and thickness of protective layer
Depends on protective layer material
We DO need to test a prototype with mirror, CF4 and GEM+CsI (see Eric’s talk)

## Slide 21
The Pion Cherenkov (PMTs): Design
Similar design as for electron Cherenkov, the PMT option
gas: C4F8O
 Before we knew we have to split the mirrors: very good collection efficiency with one mirror and 9 2” PMTs per sector

## Slide 22
The Pion Cherenkov (PMTs): Design
gas: C4F8O
Similar design as for electron Cherenkov, the PMT option
 We split the mirrors (different curvature) + went to 4 PMTs per sector
Work in progress

## Slide 23
Summary
Simulation and design: iterate!
 “finalize” the Cherenkovs design
 switch to CLEO when available and re-optimize
 migrate to GEMC
 …
Tests:
 test H8500C-03 during g2p
 test GEMs + CsI prototype during g2p: see next talk for details
 …