## Slide 1: SoLID DAQ for Transversity
Alexandre Camsonne
Yi Qiang
SoLID brainstorming session
January 6th 2011

## Slide 2: SIDIS: Single Electron Trigger
Large Angle: 65 kHz @ 11 GeV
  Calorimeter only
  Electron: 11 kHz
  High energy photon: 51.5 kHz
    (possible to be rejected by including GEM in trigger, need study)
  Hadron: <3 kHz (energy cut)
Small angle: 120 kHz @ 11 GeV
  Calorimeter + Gas Cherenkov
  Electron: 90 kHz
  High energy photon: 16 kHz (after Gas Cherenkov)
  Hadron: 15 kHz (after Gas Cherenkov and Calorimeter)
8.8 GeV gives about 240 kHz

## Slide 3: SIDIS: Hadron trigger
Calorimeter + MRPC + Scintillator
Hadron rate : 7.7 MHz
  Charged hadron: 6.1 MHz (dominated)
  Electron: 0.1 MHz
  Photon: 1.5 MHz (after MRPC and Scintillator)
Dominated by inclusive hadrons

## Slide 4: SIDIS: Coincidence @ 35 ns window
Coincidence rate: 50 kHz
Given the safety margin, expected to handle about 100 kHz.
  Include some single trigger to study detector performance etc.
4kB * 100 kHz ~ 400 MB/s to disk
  Goal to reduce things to 50 MB/s by L3 farm

## Slide 5: SIDIS channel count
Detector | Module type | Number of channels | Number of FADC
Forward Calorimeter | FADC | 1896 | 119
Large angle calorimeter | FADC(+TDC) | 920 | 58
Light Gas Cerenkov | FADC | 120 | 8
Heavy Gas Cerenkov | FADC | 270 | 17
Scintillator | FADC | 120 | 8
The FADC of LC can be programmed to produce timing signals with ~400ps resolution (already demonstrated by simulation) to remove the needs of TDC.

## Slide 6: APV25 readout
Buffer length 192 samples : 4.8 us Look back 160 samples : 4 us
Estimated occupancy : 220 hits per trigger, X Y data, 440 strips
GEM : 6 Layers 164 000 channels total, 28 000 channels per planes
Occupancy : 1.6 %
APV readout time :
t_APV = 141 x number_of_sample / 40 MHz
t_APV(1 sample) = 3.7 us.
Max rate APV front end :
270 KHz in 1 sample mode
90 KHz in 3 samples mode
Will be triggered by coincidence trigger around 50 KHz

## Slide 7: APV25 VME readout
220 hits x 2 x 2 bytes / 200 Mb
Average readout time for GEM
4.4 us / 11 crates
Readout time negligible and no dead time with buffering
More detailed simulation of APV25 and background being implemented will give confirmation in about 1 month

## Slide 8: GEM in trigger
Use signal of 5th GEM plane for fast trigger
Quality of signal to be tested
Could reduce rate in Large Angle from photon calorimeter by 50 KHz
Additionnal FADC channels to put in trigger

## Slide 9: Standard electronics
Pros
  Possibility for reuse of existing electronics
Cons
  Delay lines
  Dead time :
  Encoding time min 2.2 us
  Electronic deadtime 30 ns
  Trigger logic complicated
  Splitting signal
  Fastbus limitation to 40 Mb/s
  Sensitive to pile-up

## Slide 10: Standard electronics
Costs
  About 500 summing modules : 750 K$
  25 Or modules : 30 K$
  25 And module : 30 K$
  Total around 800 K$ not including cabling

## Slide 11: SIDIS electronics
Module | Unite price | Quantity | 
FADC 250 | 4500 | 210 | $945,000
CTP | 5000 | 19 | $95,000
SSP | 5000 | 3 | $15,000
GTP | 5000 | 1 | $5,000
VXS crate | 11500 | 1 | $11,500
TS | 3500 | 1 | $3,500
TI | 3000 | 30 | $90,000
TD | 3000 | 4 | $12,000
SD | 2500 | 30 | $75,000
VXS crate | 11500 | 30 | $345,000
VME CPU | 3400 | 31 | $105,400
L3 farm node | 5000 | 12 | $60,000
 |  | Total detectors | $1,762,400
VXS crate | 11500 | 1 | $11,500
Discriminators | 2500 | 60 | $150,000
VME64X crate | 8100 | 3 | $24,300
V1190 | 11010 | 15 | $165,150
VME CPU | 3400 | 4 | $13,600
TID | 3000 | 1 | $3,000
SD | 2500 | 1 | $2,500
 |  |  | $370,050
 |  | Grand Total | $2,132,450

## Slide 12
Trigger Crate
GTP
SSP x3:
LC x1 +
FC x2
TS
TD X4+1
DIS x20
MRPC
?
LC Trigger Crate x4
FADC x15
TI
FC/GC/HG/SC/MRPC Crate x15
CTP
FADC X10:
GC x8 +
GC/HG/SC x2
TI
SD
SD
Total Crate + CPU: 31+4
FADC: 210
DIS: 0+60
F1TDC: 0+30
CTP: 19
SD: 30+1
TI: 30+1
SSP: 3
GTP: 1
TS: 1
TD: 4+1
GEM Tracker Crate x11
APV25 X 16
TI
SD
DAQ/Trigger for SoLID SIDIS
LC Discriminator VME64X Crate x3
CPU
+ ?
CPU
CPU
CPU
CTP
CPU
V1190
x15
LC Timing Crate x1
TI
SD
CPU

## Slide 13: SIDIS electronics
Module | Unite price | Quantity | 
FADC 250 | 4500 | 210 | $945,000
CTP | 5000 | 19 | $95,000
SSP | 5000 | 3 | $15,000
GTP | 5000 | 1 | $5,000
VXS crate | 11500 | 1 | $11,500
TS | 3500 | 1 | $3,500
TI | 3000 | 30 | $90,000
TD | 3000 | 4 | $12,000
SD | 2500 | 30 | $75,000
VXS crate | 11500 | 30 | $345,000
VME CPU | 3400 | 31 | $105,400
L3 farm node | 5000 | 12 | $60,000
 |  | Total detectors | $1,762,400
VXS crate | 11500 | 1 | $11,500
Discriminators | 2500 | 60 | $150,000
VME64X crate | 8100 | 3 | $24,300
V1190 | 11010 | 15 | $165,150
VME CPU | 3400 | 4 | $13,600
TID | 3000 | 1 | $3,000
SD | 2500 | 1 | $2,500
 |  |  | $370,050
 |  | Grand Total | $2,132,450

## Slide 14: Other projects
SuperBigBite
  242 hadron calorimeter
    16 FADC
Hall 12 GeV upgrade
  VDC 2944 channels
    24 V1190 TDC
  50 FADC
  Additionnal Jlab modules
Other experiments : Primex ?

## Slide 15: SIDIS electronics
Modules | Unit price | Quantity | Price | Borrow
FADC 250 | 4500 | 144 | $648,000 | HRS + SBS
CTP | 5000 | 15 | $75,000 | HRS
SSP | 5000 | 2 | $10,000 | HRS
GTP | 5000 | 0 | $0 | HRS
VXS crate | 11500 | 0 | $0 | SBS
TS | 3500 | 0 | $0 | HRS
TI | 3000 | 24 | $72,000 | HRS
TD | 3000 | 2 | $6,000 | HRS
SD | 2500 | 24 | $60,000 | HRS
VXS crate | 11500 | 24 | $276,000 | HRS
VME CPU | 3400 | 19 | $64,600 | HRS
L3 farm node | 5000 | 12 | $60,000 | 
 |  | Total | $1,271,600 | 
VXS crate | 11500 | 0 | $0 | HRS
Discriminators | 2500 | 50 | $125,000 | HRS
VME64X crate | 8100 | 0 | $0 | HRS
V1190 | 11010 | 0 | $0 | HRS
VME CPU | 3400 | 0 | $0 | HRS
TID | 3000 | 0 | $0 | HRS
SD | 2500 | 0 | $0 | HRS
 |  | Total timing | $125,000 | 
 |  |  |  | With 20 % spare
 |  | Total detectors | $1,396,600 | $1,675,920

## Slide 16: Conclusion
APV25 limiting DAQ rate
Coincidence trigger to reduce rate to about 50 KHz
Timing needed for Large Angle Only for TOF
Use of standard electronics doable but not very convenient and not that much cheaper
Overlap of electronics with other experiment
Around 1.7 M $ including spares for PVDIS and SIDIS

## Slide 17: Backup

## Slide 18: SoLID SIDIS Detector Rates
In 50 ns windows, 11 GeV
Detector | Rate | Hits | Type | Data Size per hit
GEM | 4.4 GHz | 220 | Hits (time) | 4 Byte x 2 (X/Y)
LC | 120 kHz | 1 | Energy, Hits | 8 Byte x 2 (PS/SH)
FC | 200 MHz | 10 | Energy, Hits | 8 Byte x 2 (PS/SH)
LGC | 40 MHz | 3 | Energy, Hits | 8 Byte x 2 (split)
HGC | 60 MHz | 4 | Energy, Hits | 8 Byte x 2 (split)
MRPC | 850 MHz | 45 | Hits | 4 Byte
SC | 300 MHz | 15 | Energy, Hits | 8 Byte
Total |  |  |  | 2.5 kB
With header and other over head
event size is ~ 4 kB

## Slide 19: L1 Trigger
Electron Singles Trigger:
  LC > 400 MeV|| (FC > 400 MeV && LGC)
  Total event rate: 190 - 240 kHz
  Frontend data rate: 800 – 1000 MB/s
  ROCs can barely handle this rate
    Assuming 10 VME crates, 100 MB/s per ROC
    add more crates since PVDIS uses > 30
  Maybe a little bit too much to write to the tape
  Not much room for improvement, already very close to electron yield.

## Slide 20: Reduce L1 Trigger: Two Options
Make coincidence with another charged particle in Forward detector
  FC > 200 MeV && MRPC && Scintillator
  Coincidence rate with 35 ns window ~ 50 kHz
Use L3 farm
  With powerful parallelism computing, we can easily reduce the rate by a factor of 5
  Reduce the difficulty to put MRPC (customized VME board) into the trigger logic
Both options give 200 MB/s data rate to the tape

## Slide 21: Trigger using standard electronics
1. Electron trigger
1.1. Large angle side: 30 discriminators for Calorimeter (< 20 ns signal width)
1.2. Forward region: 30+30 discriminators for Calorimeter and Gas Cherenkov (< 10 ns signal width), 30 coincidence channels ( 20 ns window)
2. Hadron trigger
2.1 Forward region: 180+180+30 discriminators for Calorimeter, MRPC and Scintillator (<5 ns signal width), 180+30 coincidence modules ( 15 ns window)
3. Coincidence trigger 3.1 450 coincidence channels (20+15=35 ns window)
So in total, we need at least 480 discriminators and 690 coincidence modules and some logic and summing modules. Pipeline technique can really help a lot here.

## Slide 22: Use of standard electronic
Electron Trigger
  1896 FC calorimeter channels
    352 summing modules
    15 discriminators
    16 or module
  120 channels GC
    30 summing modules
    2 discriminators
    2 coincidence modules
  920 LC calorimeter channels
    115 summing modules
    8 discriminators

## Slide 23: Use of standard electronic
Hadron trigger
  Coincidence FC + Scintillators + MRPC
    8 discriminators for Scintillators
    32 Coincidence modules
Coincidence trigger
  6 Or modules ( 4 electron trigger + 2 hadron trigger)

## Slide 24: Fastbus
About 3200 channels of detector to be readout using Fastbus 1877 + MQT
  3200 delay lines
  ADC encoding deadtime 2.2 us
  Front end dead time 11 %

## Slide 25: Use of standard electronic
Conclusion
  Large amount of modules needed about twice more than Gep5 BigCal
  Not optimal because of OR and sums will be more sensitive to background
  Doable but trigger complicated
  Cost including cable of similar order