## Slide 1: Magnet Progress
Paul E. Reimer
6 Jan 2012

## Slide 2: Solenoid Size restrictions
Outer barrel
Beam line
SIDIS Target
(must be outside of solenoid or very well shielded)
24o
17o
14o
35o
20o
Or, if we were starting from scratch and designing a new magnet, what would we want?
Back-of-the-envelope arguements

## Slide 3: Solenoid Size restrictions
Outer barrel
Beam line
SIDIS Target
(must be outside of solenoid or very well shielded)
24o
17o
14o
14o line cannot hit solenoid i.e. radius/length > tan(14o)
Barrel Calorimeter should be able to intercept 17-24o without hitting 14o line
Calorimeter thickness (as seen by track) for p/e differentiation is about 40 cm
Minimum barrel radius of approximately 90 cm
Minimum barrel length of approximately 360 cm

## Slide 4: Solenoid Size restrictions
Outer barrel
Beam line
SIDIS Target
(must be outside of solenoid or very well shielded)
24o
17o
14o
Smaller calorimeter (either more dense or fewer rad lengths)
  Smaller radius and hence shorter length
  Still need angular coverage
Larger barrel-forward gap
  Acceptance hole
  Allows for longer or deeper colorimeter
Shift barrel-forward gap
  Small effect for reasonable shifts

## Slide 5: Choice of Solenoid
Field:
  The Q2 and x resolution requirements (from PVDIS) dictate the desired energy resolution that was found to be sE’/E’ < 3%.
  Coupling this with the tracking resolution dictate the minimum acceptable field.
  Simulations have shown that a solenoid with 1.5T central field and 6 planes of 500mm resolution tracking can meet this criteria.
  Not the only solution, but shown to work.
    Trade off more field ⇔ less tracking resolution
In other words, we have been looking at the correct size of solenoids regardless of cost.
Cost of fabricating a new magnet is approx. $8M based on Hall D

## Slide 6: Magnet Comparison
 | BaBar | CLEO | ZEUS | CDF | Glue-X | Other
Cryostat Inner Radius | 150 cm | 150 cm | 86 cm | 150 cm |  | Whatever we need
Length | 345 cm | 350cm | 245cm | 500 cm |  | 
Central Field | 1.49T | 1.5T | 1.8T | 1.47T |  | 
Yoke Aval? | Yes | Yes | No | No |  | 
Cool Icon | Yes | Yes | Yes | No |  | 
Variation in Current density with z? | Current Density in central 50% is ½ that in end 25% | Current Density in central 50% is 1/1.04 that in end 25% | Current density 25% more current at ends | No | Yes | 
Available | Probably Not?? | Probably | Probably Not?? | Needs $1M repair and possible Expt at Fermilab | Perhaps | $8M??

## Slide 7: Choice of CLEO magnet
 | CLEO
Cryostat Inner Radius | 150 cm
Length | 350cm
Central Field | 1.5T
Yoke Aval? | Yes
Cool Icon | Yes
Variation in Current density with z? | Current Density in central 50% is 1/1.04 that in end 25%
Available | Probably
Obtaining the Cleo Magnet
Magnet is owned by Cornell and not DOE or NSF
Coil is currently “captured” by CESR
We have been in contact with relevant CLEO and Cornell persons about obtaining this coil
Still needed
Cost estimate for removing and transporting coil
Engineering for Cryo and Flux return (this will cost $$)

## Slide 8: Field Map
Poisson 2-d simulation
Could still be optimized to
  Reduce steel
  Balance forces on coil
  Minimize field in PMT areas
  Done in 3D?

## Slide 9: Conclusions
CLEO magnet will produce the desired acceptance and resolution for both SIDIS and PVDIS
A new coil would be similar to CLEO and cost approx. $8M
We have been in contact with CLEO/Cornell but need cost estimate
Need to start Engineering on flux return
Reasonable field map
Outer barrel
Beam line
SIDIS Target
(must be outside of solenoid or very well shielded)
24o
17o
14o