## Slide 1: Summary of Requirements and Special Considerations
Xin Qian
KRL
Caltech

## Slide 2: SoLID-Spin (SSA + DSA on n)
We measure asymmetries (a few 10-4  a few 10-2)
Total statistical precision <10-5, Systematic: ~ 6% x A
Keys of SoLID:
Large Acceptance + High Luminosity  4-D mapping of asymmetries  Tensor charge, TMDs …
Lattice QCD, QCD Dynamics, Models.
Experimental Side:
Full Azimuthal Angular Coverage
 Double Cancellation in Asymmetries (both acceptance and luminosity fluctuation)
+ Fast Spin Flip for SSA
Control False Asymmetry
Challenges:
 Detectors Performance in high luminosity environment (GEM…)
 Fast DAQ (Hall D Standard, Other Halls)

## Slide 3: Requirement of SIDIS
Kinematics Coverage:
  0.05 ~ 0.6 in x (valence)
  0.3 ~ 0.7 in z (factorization region)
  PT up to ~ 1 GeV (TMD Physics)
  Fixed target  Q2 coverage 1-8 GeV2 (~ 2 GeV2 in ΔQ2 at fixed x)
Luminoisity:
  Unpolarized ~ 1037 N/cm2/s
Polarized 3He Target:
  ~ 60% higher polarization
  Fast spin flip (<20 mins)
Electron PID:
  <1% Pion contamination (asymmetry point of view)
Pion PID:
  <1% Kaons and Protons
  <1% electron contamination
Optics of Reconstruction:
  < a few % in δP/P.
  < a few mr in polar angle.
  < a few 10s mr in azimuthal angle
  ~ a few cm vertex resolution
  Similar precision required.
  A factor of 2-3 better already achieved in MC.
DAQ:
  ~ 3kHz Physics Coincidence
  ~ 200 kHz Single electron
  ~ 50 kHz Coincidence
  Limits: 300 MB/s to tape.

## Slide 4: Conceptual Design with BaBar

## Slide 5: Special Considerations
Uniformity:
  E.g. Design of Detector Support Structure to minimize holes in acceptance (especially in azimuthal angle)
Background in Detectors
Radiation:
  Design of Detector front end electronics and calorimeter
    Minimize radiation damage
    Maximize radiation hardness of design.
Multiple New Detectors:
  Need dedicated time to commission detectors and system integration.
  Multiple/Staged beam tests needed for detector R&D.
  Detailed Integration Plan.
Mechanical Design:
  Compact
  Detector maintenance
  Cable layout
  Switch plan among different configurations:
    Transverse vs. Longitudinal
    SIDIS vs. PVDIS
  Strong Engineering Support
Procedure to quick establishment of detector performance.
  Position of Tracking detectors
  Energy response in Calorimeter
  Background/Gain in Gas Cerenkov.
  Physics asymmetry in single hadron, and zero PV will help in this.

## Slide 6: Motivation for PVDIS
Standard Model
CSV at Quark Level
Di-quarks in
the nucleon
(Q2 Dependence)
d/u for Hydrogen
4 months at 11 GeV
2 months at 6.6 GeV
Error bar σA/A(%) shown at center of bins in Q2, x

## Slide 7: Summary of Requirement
0.5% precision over broad kinematics range.
  Beam Polarimetry (Paschke )
  Control false asymmetries in PID/Tracking.
New Cryotarget Design (Chen)
  Challenges in mechanical engineering.
  Control of false asymmetry.
High luminosity 1039 N/cm2/s
  Sieve to block direct photons
    Effectively reduce luminosities on detectors.
  Background in Cerenkov.
  Radiation dose in Calorimeter.
    Similar to SIDIS requirement
Electron PID:
  < ~1% Pion contamination
  Gas Cerenkov + E&M Calorimeter for < 3.0 GeV
  Calorimeter alone for high Momentum
  GEM for tracking
30 sectors, each employs an independent DAQ system.
  Simpler design than SIDIS.
  < 10 kHz per sector
Require L3 farm and online tracking.
  Proof-of-principle of tracking was achieved.
    2.5 kHz per sector @ 1 CPU @ 3.0 GHz.

## Slide 9: Special Considerations
Q2 Determination
  Elastic scattering Need Mont Carlo
  4.4 + 6.6 GeV?
  How clean are the peaks?
  How can they be centered? (not symmetric)
Sieve Slits (Optics)
  Run with lower B and B=0
  Rotate one or more baffles to get straight path
  Install slit with holes to calibrate angles
Pile-up and Dead Time
  Dither Intensity: ~10-2
  Empirically measure all effects.
  Reduce Acceptance and vary Intensity by 20%
  Correct for density variation
Calibrate BCM
  Solid target
  Linear Luminosity Monitor
Other considerations similar to that of SIDIS: Mechanical Design

## Slide 11: Conceptual Design (I)
Kinematics Coverage:
  Preference of Magnet
  Limited by SoLID geometry
  Data taking at 8.8 GeV for radiative corrections and expand Q2 coverage.
Luminoisity:
  Requirement on GEMs, Cerenkov.
  Radiation dose on E&M Calorimeter and front end electronics.
  Requirement on DAQ system.
Polarized 3He Target:
  Achieved performance assumed for this experiment
  Magnetic field shielding design and correction coils are keys for performances.
  Possibly benefits from new techniques developed for earlier 12 GeV experiments
Electron PID:
  Combination of E&M calorimeter + Gas Cerenkov (shared equipments with PVDIS)
  Advantage of coincidence measurement in SIDIS (additional Pion suppression)
Pion PID:
  Gas Cerenkov + E&M Calorimeter to suppress electron.
  TOF (MRPC) at low momentum to suppress kaons/protons
  Heavy Gas Cerenkov to suppress kaons in high momentum.

## Slide 12: Conceptual Design (II)
Optics of Reconstruction:
  Already demonstrated in MC, 200 um resolution in GEM leads to resolution performance.
    ~ 1% in δP/P
    < 6 mr in azimuthal angle
    < 0.5 mr in polar angle
    ~ 1 cm vertex resolution
Calibration Plan:
  2.2, 4.4 and 6.6 GeV beam
  Multi-Carbon Foils for Vertex.
  Elastic Hydrogen for momentum.
  Sieve Slit for angles.
  Varying strength of SoLID magnetic field. (e.g. No Field Run + Survey …)
  Very experienced team in optics calibration.
DAQ:
  JLab customized pipeline technology.
  Fast Tracking:
    Demonstrated tracking in expected experimental environment.
    Already achieved 1 kHz per 3.0 GHz CPU.
    Plenty of room to improve e.g. Multi-thread + Sectors + Algorithm Improvement (e.g. GPUs)
Additional Goals to be studied:
  Neutral Pion Identification (Limited by E&M calorimeter granularity)
  Two Hadron SIDIS (multiplicity at high W + acceptance)
    Complemantary Transversity Measurement

## Slide 13: Sensitivity: C1 and C2 Plots
World’s data

## Slide 14
Example projections of Neutron AUL moments, 1/48 bins in z vs. Q2.
Sys.: 0.1% (abs.) + ~6% (rel.) + Nuclear Effect/FSI
Expected Improvement of Sivers Function
These data will provide ultimate precision mapping of Neutron SSA/DSA in the valence region at low Q2!
50 days @ 11 GeV + 22 days @ 8.8 GeV (Coverage + RC) + 10 days on H/D (Dilution, FSI, Mechanism) + 8 days on calibration of new device + 35 days with longitudinal target spin
<10% d quark tensor charge Collins Effect
First Neutron (3He) Data
Notes: Top Right Plot used as place holder (to be replaced with results from A. Prokudin)