## Slide 1: Cherenkov Counters for SoLID
Z.-E. Meziani
on behalf of
Simona Malace & Haiyan Gao (Duke University)
Eric Fuchey (Temple University)

## Slide 2: PVDIS versus SIDIS Configurations
PVDIS
SIDIS
One Cherenkov Counter
Gas length constrained due to baffles
Highest luminosity
Calorimeter and Cherenkov for pion rejection: goal contamination less than 1%
Two Cherenkov Counters
Gas length extended in the magnet for the e- Cherenkov
Highest luminosity
Calorimeter and Cherenkov for pion rejection: goal contamination less than 1%

## Slide 3: Simulations
Optics simulation using GEANT4
  Present simulations uses BABAR magnet but CLEO magnet simulations are underway
  Target length and beam raster effects included in optics optimization
  Gas transparency + mirror reflectivity + cone reflectivity + photocathode response + UV glass transparency included

## Slide 4: Reference Design: PVDIS electron Cherenkov
Radiator: C4F8O/N2 mix
Length: ~ 1 m
Useful momentum range: 2-4 GeV
Pion rejection goal ~ 100
Photodetectors: Hamamatsu H8500C maPMTs (2”x2” size) tiled in 3x3 per sector
maPMTs array shielded with a mu-metal cone that is reflective.
Mirrors: spherical in 2 parts, inner and outer. Material: CFRP (70% Carbon fiber, 30% resin bond). Al_MgF2 reflective coating: > 85% for wavelengths greater than 200 nm
  Inner: L = 75.6 cm, R= 268.7 cm
  Outer: L =78.6 cm, R= 178.4 cm
Mirrors support

## Slide 5: Projected performance with safety margin

## Slide 6: Pion background
Goal is to keep the pion contamination less than 1% when combining the Cherenkov counter and the calorimeter
PVDIS
SIDIS

## Slide 7: Performance: PVDIS Cherenkov (continued)
The photo-detector per sector is tiled in a 3x3 maPMTs configuration, a compromise of cost and efficiency

## Slide 8: Projected Performance

## Slide 9: Hamamatsu H8500C

## Slide 10: H8500C maPMTs performance in magnetic field
Extensive study of magnetic field effects on the performance of the H8500C Hamamatsu maPMT (S. Malace, in collaboration with B. Sawatzsky & H. Gao)
Conclusions:
  Single photoelectron resolved
  Loss due to magnetic field mainly due to gain loss in the multiplication chain not at the first dynode for the longitudinal field
  Largest losses experienced when the magnetic field is parallel to the face of the PMT which can be easily shielded

## Slide 11: maPMT performance (continued)
Single photoelectron can be resolved
When the field is perpendicular to the face of the PMT small one photoelectron losses are observed.

## Slide 13: Shielding of the photo-detectors in a sector

## Slide 14: Reference design: SIDIS electron Cherenkov
Radiator: CO2 at ~1 atm
Radiator length: ~ 2 m
Useful momentum range: 1.5- 4.5 GeV
Pion rejection goal ~ 100
Photodetectors: maPMTs tiled 2x2 per sector with a total of 30 sectors
maPMTs array per sector shielded with mu-metal straight reflective cone to enhance the collection efficiency
Mirrors: spherical split in two with different radii of curvature to optimize the size of the photodetector array.
Material and reflectivity of mirrors similar to PVDIS description
Note: Radii of curvature different from PVDIS
Mirrors support
Extension of gas tank
4”
4”

## Slide 15: Projected Performance of SIDIS Electron Cherenkov
Large # of photoelectrons ~25 across electron energies and scattering angles

## Slide 16: Projected performance
pion distribution
electron distribution
Keep pion contamination below 1%, achieved with an 8 p.e. cut leaving a
high e- efficiency

## Slide 17: SIDIS Pion Cherenkov counter
Radiator: C4F8O at 1 .5 atm at 20 0C
Useful momentum range: 2.5-7.5 GeV
Kaon rejection goal ~ 100?
Photodetectors: maPMTs tiled 3x3=9 per sector with a total of 30 sectors
maPMTs array per sector shielded with a mu-metal cone that is reflective to enhance the angular acceptance.
Mirrors: one spherical mirror per sector. Al+MgF2 reflective coating
Optics optimized for both positive and negative pions
Tank considered a pressure vessel
Positive pions
Negative pions

## Slide 18: Light collection efficiency of Pion Cherenkovs
Negative Pions
Positive Pions

## Slide 19: Projected performance of the SIDIS Pion Cherenkov
Response for positive pions simulated with a safety factor of 0.5.
Positive Pions

## Slide 20
pion efficiency: 99.2%
kaon contamination: 0.8%
pion efficiency: 99.5%
kaon contamination: 0.3%
3
4
pion efficiency: 99.9%
kaon contamination: 0.2%
pion efficiency: 100%
kaon contamination: 0.2%
4
4
Pion Cherenkov: Projected Performance
Hypothesis:
kaon:pion = 1:10
(from proposal)
PMT resolution: 1 p.e. (from measurements)
no input from other PIDs
kaons give at most 1 p.e. below threshold

## Slide 21: Mirrors: Quote from Composite Mirrors Applications

## Slide 22: Distributions of photons on the photodetector
Coincidence between quadrants was tried successfully in a test, however, the reduction (a factor of 10) saturates due perhaps to cross talk between quadrants (to be checked)
Distribution of photons lead to a possible coincidence scheme of independents maPMTs within one sector to reduce random background

## Slide 23
 | SIDIS/PVDIS e- Cherenkov | SIDIS p Cherenkov
Mirrors/coating*** | $277 K x 2 = $554 K | $277 K
PMTs* | $3,000 K x 124 = $372 K | $3,000 x 279 = $837 K
Cones** | $41 K x 2 = $82 K | $47 K
Gas system |  | 
Tank |  | 
2.2 M
* we assume PVDIS will reuse PMTs from SIDIS
** quote for straight cones for the electron Cherenkovs and for parabolic cones for the pion Cherenkov
*** quote from CMA for CFRP mirrors (coating included)
Partial Cost Estimate

## Slide 24: Summary
Presented a reference design for the electron and pion Cherenkov detectors of SoLID
Realistic simulations with good safete margins. Projections of performance are sound given past experience.
Transverse magnetic field effects can be mitigated with mu-metal shielding while the longitudinal ones are not an issue
PMT option reference design offers many advantages:
  Proven technology
  Easy recovery due to multiplicity
  E&M or other background mitigation possible using coincidences between maPMTs within a sector
  Long term maintenance of mirror reflective properties possible.
  No dramatic performance expected from gas impurities.
Still to be done:
  Define the electronics logic and readout.
  Build a prototype of a 3x 3 photo-detector array including mu-metal shielding.
  Build a prototype of one sector with mirror mounts, photo-detector mounts etc..
  Design, build and test the optical alignment procedure
  Test the prototype at Idaho or Mainz in a high luminosity environment
  Specify the mechanical design of the pion Cherenkov pressure vessel
  Another option explored: LAPPD
  https://lappdtrac.uchicago.edu/