## Slide 1: Conceptual design of TOF and beam test results
Wang Yi
Department of Engineering Physics
Tsinghua University, Beijing, China

## Slide 2: Outline
Conceptual design of TOF
  TOF and MRPC
  Experiment Overview
Beam Test Setup
  Layout
  Preparation
  Some Details on Setup
Results & Conclusion
  Test Results
  Comparison
  Conclusion

## Slide 3
The MRPC is developed for the TOF of SoLID
Main Requirements for TOF:
  /k separation up to 2.5GeV/c
  Time resolution < 80ps
  Rate capability > 10kHz/cm²
MRPC TOF wall we designed contain 150 MRPC modules in total, with 50 gas boxes and 3 counters in each box, covering the area of 10m².
1.Conceptual design of SOLID-TOF
MRPC1
MRPC2
MRPC3
100cm
16cm
28cm
The MRPC module we tested is the prototype of smallest one.
Total channel ~3300

## Slide 4
1.Introduction: MRPC module
The prototype of high rate MRPC modules with low resistivity glass electrodes can work under the flux of 100kHz/cm² in previous test in HZDR and GSI.
Low resistivity glass is black in color, and the volume resistivity can reach ~1010.cm. (For float glass, the volume resistivity is ~1012.cm)
Volume resistivity: ~1010.cm

## Slide 5
The design of MRPC readout
1.Introduction: MRPC module
363mm
219mm
171mm
Interval | 3mm
Strip width | 25mm
Readout mode | Differential
Dimensions
 | Length/mm | Width/mm | Thickness/mm
Gas gap | - | - | 0.25×10
Inner glass | 320 | 130-171 | 0.7
Outer glass | 330 | 138-182 | 1.1
Mylar | 335 | 153-198 | 0.18
Inner PCB | 350 | 182-228 | 1.6
Outer PCB | 350 | 172-218 | 0.8
Honeycomb | 330 | 153-198 | 6
Outer glass
Inner glass
Mylar
Inner PCB
Outer PCB
Honeycomb
Gas Mixture(Pre-mixed) | Freon 90% iso-butane 5% SF6 5%
Working Voltage | ±6800V
Electrical field | ~108.8kV/cm

## Slide 6
TOF electronics
Fast preamplifier：
Maxim3760 (RICE Univ.)
Ninos (TOT) (ALICE)
Padi (TOT) (GSI)
CAD (TOT)(Tsinghua)
QDC (CAEN, 25fC/bin)
TDC
HPTDC (ALICE, 25ps/ch)
GET4 (GSI, 25ps/ch)
FPGA TDC (GSI and other)
DAQ

## Slide 7
7
Comparison of different FEE
 | CAD-1.0 | PADI-1 | NINO-25 | NINO-13
Peaking time | ~1ns | <1ns | 1ns | 0.6ns
Linear range | 1000mA*1 | -60-60mA*1 | 0-100fC*2 | 0-100fC*2
Time jitter | <20ps, rms*3 | <15ps, rms*4 | 10-25ps, rms | 6-25ps, rms
Power consumption | 10mW/ch | <30mW/ch | 30mW/ch | 5mW/ch
Input type | S.E. | DIFF. | DIFF. | DIFF.
Input impedance | 50-70W | 48-58W | 30-100W | 30-100W
Discriminator threshold | 263mA*1 | 10-400mA*1 | 20-100fC*2 | 20-100fC*2
CMOS process | 0.35mm | 0.18mm | 0.25mm | 0.13mm
*1: for current pulse with 0.3ns rise time, 1-2ns FWHM, and 0.3ns fall time
*2: for square current pulse with 200ps width
*3: for 200mA input current
*4: for 100mA input current

## Slide 8
Cosmic test
Cosmic ray test@Tsinghua August, 2011
Efficiency > 95% @ 96kV/cm (6.0kV)
Time resolution: ~ 52ps
PMT3
PMT4
PMT0
PMT2
PMT1
MRPC
Cosmic Ray Muon

## Slide 9
The experiment last out totally 3 months, contains several process. The MRPC is tested both with cosmic ray and beam.
Brief Timetable :
The MRPC material is activated, which increases dark current and noise signal, as the test goes.
We got the time resolution of 80ps
2.Beam test: Experiment Overview
Setting Up Feb 7th- Apr 7th | Preparation(Feb 7th-Mar 26th) |  |  | Setting in Hall A(Mar 26th-April 10th) |  | 
 | MRPC module and electronics; Placing High Voltage cable &gas supply; Work on DAQ and Decoding program; Pre-test with cosmic ray. |  |  | Set up test system in Hall A; Upgrading of DAQ system; Finish cable connection; Pre-test with beam. |  | 
Beam Test May 12th-May 17th | May 12th | May 13th | May 14th |  | May 15th | May 16-17th
 | Begin the test; Voltage Scan. Detector is 10m from Target with shield. | Replace LTD with CFD; continue test. Add T0 into calibration. | Place the MRPC 5m from Target with shield. Add scaler. |  | Test continue. Voltage scanning. | Take out the shield and continue testing

## Slide 10
3.Beam Test Setup: Preparing
MRPC
DAQ
10
Gas Out
6 ADC
Channels
90% Freon
5% iso-butane
5% SF6
6 TDC
Channels
6 TDC
Channels
6 ADC
Channels
PMT0
Pre-Amp
Pre-Amp
sis3320
Flash ADC
775
TDC
·
Trigger
&
Trigger
Stop
PMT1
·
·
LTD
Signal

## Slide 11
4.Beam Test Setup: In Hall A
Trigger
MRPC
DAQ
Gas Out
6 ADC
Channels
90% Freon
5% iso-butane
5% SF6
6 TDC
Channels
6 TDC
Channels
6 ADC
Channels
PMT3
PMT4
PMT0
Pre-Amp
Pre-Amp
sis3320
Flash ADC
775
TDC
·
Trigger
PMT2
PMT1
·
&
LTD
Stop
Amp
Delay
·
Taking all stuffs to Hall A
(Delay)
(Delay)
Trigger Area : 5 × 10 cm²
Fast Scintillator (5 ×15 cm² )

## Slide 12
Shield
4.Beam Test Setup: In Hall A
High Energy e-
Top View
PMT1
PMT2
PMT3
PMT4
PMT0
Target
Trigger Area : 5 × 5 cm²
Front View
PMT0
PMT1
PMT2
What is the beam like?
  2.5 GeV electrons hitting the target
  Uniformed particle(electron) and photon irradiation
  Large background and high flux
T0
T1
T2
Time calibration of 4 PMTs: ~300ps
Schematic top view of the test setup
 | Distance & Shielding | Current
Before May 13th | 10m , shielded | ~500-3500nA
May 13th – 16th | 5m, Shielded | ~8uA
After May 16th | 5m, not shielded | ~15uA

## Slide 13
4.Beam Test Setup: In Hall A
MRPC
Shield
Target

## Slide 14
4.Beam Test Setup: Upgrade
Trigger
MRPC
DAQ
·
Gas Out
6 ADC
Channels
90% Freon
5% iso-butane
5% SF6
6 TDC
Channels
6 TDC
Channels
6 ADC
Channels
PMT3
PMT4
PMT0
Pre-Amp
Pre-Amp
sis3320
Flash ADC
775
TDC
·
Trigger
Delay
PMT2
PMT1
·
&
CFD
Stop
Amp
(Delay)
(Delay)
Add “T0” into calibration
Use CFD for trigger
Improvements
  The stop signal is changed to delayed T_0
  LTD is replaced with CFD
Time calibration of 4 PMTs: ~100ps

## Slide 15
5.Results & Comparison: Calibration
Example: r175
Operated on May 13th
High Voltage: ±6800V
Condition: 10m from
target, shielded
PMT before calibration
MRPC before calibration
4 calibrations
Charge Cut：2 σ
Position Cut：2 σ

## Slide 16
Calibration of PMT
Calibration of MRPC
5.Results & Comparison: Calibration
Example: r175
Operated on May 13th
High Voltage: ±6800V
Condition: 10m from
target, shielded
Time resolution: 76ps
σ-PMT = 2.937(102.8ps)
σ-MRPC = 3.646(127.6ps)
σ-MRPC = 2.16(75.6ps)
In this test, T0 is about 100ps, the time resolution is deteriorated.

## Slide 17
5.Results & Comparison: HV Scan
Time Resolution: ~75ps
Efficiency: >95%

## Slide 18
5.Results & Comparison: Rate Scan
Voltage: 6800V
Flux:11kHz/cm²
Efficiency:~95%
Time Resolution: 78ps
Flux:16kHz/cm²
Efficiency:~95%
Time Resolution: 82ps

## Slide 19
5.Results & Comparison: Flux vs. Time
Run188, 6800V (5m to target, shielded)
Run193, 6800V (5m to target, not shielded)
2.5kHz/cm²
6kHz/cm²
12kHz/cm²
14-15kHz/cm²
16-18kHz/cm²
During a run, flux is not on a stable level, which from less than 3kHz/cm² to 16kHz/cm².
We can observe the performance by selecting data from different flux.

## Slide 20
Charge spectrum at different rate
5.Results & Comparison : Charge Distribution
Base Line
Signal
Significant reduction of charge distribution can be seen as the background rate increases.
The reduction of electrical field is caused mainly by both background irradiation and electron beams.
Rate capability of the counter is higher than 15kHz/cm².

## Slide 21
5.Results & Comparison : Beam Test
Beam Test@HZDR June, 2012

## Slide 22
5.Results & Comparison : Beam Test
22
Time Resolution < 40ps
Beam Test@HZDR June, 2012
HV scan
Rate scan

## Slide 23
6.Conclusions
Performance of MRPC is measured. The time resolution can reach 70-80ps and the efficiency is higher than 95%. The flux is up to 16kHz/cm².
The MRPC module is placed within 10m to the Target for 2 months, without significant performance deterioration. This means that the module can withstand long time irradiation.
The Irradiation is uniformed. During Test, the current is large even when the rate is not very high, which means the photon or neutron background irradiation is very strong.

## Slide 24: Thank you!
End