## Slide 1: SoLID DAQ Update
A. Camsonne, R. Miskimen, Y. Qiang
SoLID Collaboration Meeting
Dec 15th 2012

## Slide 2: Overview
DAQ Setup
Event Sizes and Data Rates
APV25 Test Stand
Future Plan

## Slide 3: PVDIS DAQ Setup
Trigger rate for each crate: 20 kHz
Detector | Module | # of Channels | # of Modules
Calorimeter (CAL) | FADC | 114 × 30 | 8 x 30
Gas Cherenkov (GC) | FADC | 9 × 30 | 
GEM | APV25-VME | 4800 × 30 | 5 x 30
PVDIS VXS Crate ×30
FADC ×8
SD
CPU
CTP
APV25 ×5
TI
  Crate Trigger Processor (CTP)
  Trigger Interface (TI)
  Signal Distribution (SD)

## Slide 4: SIDIS DAQ Channel/Module Counts
Detector | Module | # of Channels | # of Modules
Forward Calorimeter (FC) | FADC | 1920 | 120
Large-angle Calorimeter (LC) | FADC | 960 | 60
Light Gas Cherenkov (GC) | FADC | 270 | 20
Heavy Gas Cherenkov (HG) | FADC | 270 | 20
GEM Pad Readout (GP)* | FADC | 150(L)/270(F) | 10/20
GEM | AVP25-VME | 180k | 180
MRPC | VME | 7500 | 60
* Original scintillator bars in forward will be replaced by GEM pad readout if possible

## Slide 5: SIDIS DAQ/Trigger Setup
e−@Large: LC & GP 13 kHz
e−@Forward: FC(high) & GC 65 kHz
π@Forward: FC(low) & MRPC & GP 15 MHz
Coincidence: e− & π 60 kHz@50 ns
* Coincidence rate scales with the square of luminosity
Global Trigger VXS Crate
GTP
SSP x3
TS
TD x4
Discriminator x20
MRPC
x4
Large-Angle VXS Crate x5
FADC x12(LC)
+ x2 (GEM Pad)
TI
Forward VXS Crate x15
CTP
FADC x8 (FC)
+ x4 (GC+HG+GP)
TI
V1190 x8
SD
SD
GEM Tracker VXS Crate x10
APV25 x18
TI
SD
LC Timing VXS Crate x1
TI
SD
CPU
Optional TDC Crates for LC
CPU
CPU
CPU
CTP
CPU
Trigger Forming
Trigger Distribution
LC Timing VME Crate x3
CPU
  Crate Trigger Processor (CTP)
  Sub-System Processor (SSP)
  Global Trigger Processor (GTP)
  Trigger Supervisor (TS)
  Trigger Interface/Distribution(TI/D)
  Signal Distribution (SD)

## Slide 6: J/φ DAQ Setup
Same hardware as SIDIS
Different Trigger Logic:
  e−(scattered): FC(medium) & GC
  Lepton@Large-angle: LC & GP
  Lepton@Forward: FC(high) & GC
  Triple Coincidence: e− & l+ & l −
Trigger Rate:
  15 kHz for triple coincidence with 100 ns window

## Slide 7: Total DAQ Hardware
Module | PVDIS | SIDIS | Total | Unit Cost | Cost
VXS Crate | 30 | 31 | 31 | $11,500 | $356,500
VME CPU | 30 | 31 | 31 | $3,400 | $105,400
CTP | 30 | 20 | 30 | $5,000 | $150,000
SD | 30 | 30 | 30 | $2,500 | $75,000
FADC | 240 | 250 | 250 | $4,500 | $1,125,000
AVP25-VME | 150 | 180 | 180 | UVa/China | 
TI | 30 | 30 | 30 | $3,000 | $90,000
GTP |  | 1 | 1 | $5,000 | $5,000
TS |  | 1 | 1 | $3,500 | $3,500
TD |  | 4 | 4 | $3,000 | $12,000
MRPC-VME |  | 60 | 60 | China | 
Total | $1,842,000 | $1,872,400 |  |  | $1,922,400
* Optional SIDIS Large-angle Timing: $292,980

## Slide 8: PVDIS Event Size and Data Rate
GEM Rates per Sector (25 ns window, LH2, 11 GeV)
Event Size per Sector (50 ns window, 11 GeV)
Data Rate per Sector:
  20 kHz x 7 kB = 140 MB/s
 | Raw | w/ Threshold | Deconvolution
Hits | 1182 | 555 | 53
Occupancy | 25% | 12% | 1.1%
Detector | Rate | Hits | Type | Data Size per hit
GEM (25 ns) | 47 GHz | 555 (threshold) | 3xSamples, Time, Position | 12 Bytes
Calorimetry | 5 MHz | 1 | Energy, Time, Position | 8 Bytes x 2 (PS/SH)
Gas Cher | 10 kHz | 1 | Energy, Time, Position | 8 Bytes x 9 (Split)
Total |  |  |  | 7 kB

## Slide 9: Comments on PVDIS
Rates per sector are manageable.
High occupancy in GEM: 3 samples are absolutely needed. Deconvolution helps, but might be safer to send non de-convoluted signal for offline treatment as long as bandwidth allows.
Need two Ethernet links for each crate: ~ 200 MB/s.
Test convolution behavior at very high rate.
Strategy for online data reduction before recording:
  Trace back from shower to define region of interest
  PID cut
  Online coarse tracking

## Slide 10: SIDIS Event Size
GEM Rates (25 ns window, 11 GeV)
Event Size (50 ns window, 11 GeV)
 | Raw | w/ Threshold | Deconvolution | Proposal
Hits | 5826 | 1358 | 122 | 110
Occupancy | 3.2% | 0.8% | 0.1% | 0.1%
Detector | Rate | Hits | Type | Data Size per hit
GEM (25 ns) | 4.9 GHz | 122 (deconv.) | Integral, Time, Position | 8 Bytes
LC | 120 kHz | 1 | Energy, Time, Position | 8 Bytes x 2 (PS/SH)
FC | 200 MHz | 10 | Energy, Time, Position | 8 Bytes x 2 (PS/SH)
GC | 40 MHz | 3 | Energy, Time, Position | 8 Bytes x 9 (split)
HG | 60 MHz | 4 | Energy, Time, Position | 8 Bytes x 9 (split)
MRPC | 850 MHz | 45 | Time, Position | 6 Bytes
GEM Pad | 300 MHz | 15 | Energy, Time, Position | 8 Bytes
Total |  |  |  | 2.1 kB*
* 17 kB if use only apply threshold on GEM Readout with 3 sample mode

## Slide 11: SIDIS Data Rates
60 kHz Trigger Rate:
Crate Name | # of Crate | Detectors | Total Data Rate | Data Rate per Crate
GEM | 10 | GEM | 59 MB/s | 5.9 MB/s*
Large-angle | 5 | LC GEM Pad | 1.2 MB/s | 0.24 MB/s
Forward | 15 | FC GC HG GEM Pad MRPC | 63 MB/s | 4.2 MB/s
* 98 MB/s is only apply threshold w/ 3 sample mode

## Slide 12: Comments on SIDIS
Deconvoluted GEM rate consistent with proposal.
GEM occupancy is low, 1 sample may be OK for less noisy environment, but cannot be used if deconvolution method used.
Data rates well under control.
Still need to test GEM pad readout.

## Slide 13: APV25 GEM Readout
Switch Capacitor Array ASICs
  128 channels
  Sample rate: 40 MHz
  Buffer length: 192 samples, 4.8 us
  Look back: 160 samples, 4 us
Readout Time/Max Readout Rate:
  T_APV = 141 x Nsample / 40 MHz
  1 sample mode: 3.5 us, 280 kHz
  3 sample mode: 10.6 us, 90 kHz
PVDIS: 20 kHz
  3 sample mode is feasible and needed
SIDIS: 60 kHz
  1 sample mode if using a global GEM trigger, deconvolution cannot be applied
  3 sample mode if using crate dependent trigger, taking advantage of low occupancy

## Slide 14: APV25 Test Stand at UVa/JLab
University of Virginia:
  Running VME system using multi-purpose degitizer (MPD) modules with CAEN controller.
  SRS DAQ system.
  Some work ongoing on electronic noise
  Plan to move to JLab
Jefferson Lab
  Test setup deployed
  Development of readout with Intel VME CPU and CODA
  Should be able to start testing in 2013
Evaluation of electronics performance by 2013

## Slide 15: Future Plan
Continue work on GEM readout:
  Study threshold and deconvolution efficiency
  Data reduction
Trigger Simulation (Software):
  On top of existing physics simulation
  Find optimal trigger logic
    Information needed: Energy sum? Hit pattern?
    Formula to process information
    Bandwidth usage: within limit?
    Minimize background rate
    Maximum efficiency for real events, less bias
  Get more reliable trigger rates

## Slide 16: Future Plan (continued.)
Bench Top Tests of Trigger Electronics:
  Setup a small scale DAQ system
  No detector really needed as FADC can replay “predefined” waveforms
  Test the capability of the processing power of various modules: CTP, SSP, GTP
Possible Resources:
  Jlab: Pipeline electronics
  UVa: GEM related
  UMass: Testing hardware
  Duke: Min Huang

## Slide 17: Backup

## Slide 18: Comments on GEM Readout
No show stopper
Realistic effect of background
Need to define threshold from MIP signal
Study hit/tracking efficiency as function of threshold
Start work on data reduction