## Slide 1: Status of MRPC-TOF
Wang Yi
Department of Engineering Physics
Tsinghua University, Beijing, China

## Slide 2: Outline
Conceptual design of TOF
Beam test results
  Layout
  Preparation
  Some Details on Setup
Conclusion
  Test Results
  Comparison
  Conclusion

## Slide 3
The MRPC is developed for the TOF of SoLID
Main Requirements for TOF:
  /k separation up to 2.5GeV/c
  Time resolution < 80ps
  Rate capability > 10kHz/cm²
MRPC TOF wall we designed contain 150 MRPC modules in total, with 50 gas boxes and 3 counters in each box, covering the area of 10m².
1.Conceptual design of SOLID-TOF
MRPC1
MRPC2
MRPC3
100cm
16cm
28cm
The MRPC module we tested is the prototype of smallest one.
Total channel ~3300

## Slide 4
1.Introduction: MRPC module
The prototype of high rate MRPC modules with low resistivity glass electrodes can work under the flux of 60kHz/cm² in previous test in HZDR and GSI.
Low resistivity glass is black in color, and the volume resistivity can reach ~1010.cm. (For float glass, the volume resistivity is ~1012.cm)
Volume resistivity: ~1010.cm

## Slide 5
The design of MRPC readout
1.Introduction: MRPC module
363mm
219mm
171mm
Interval | 3mm
Strip width | 25mm
Readout mode | Differential
Dimensions
 | Length/mm | Width/mm | Thickness/mm
Gas gap | - | - | 0.25×10
Inner glass | 320 | 130-171 | 0.7
Outer glass | 330 | 138-182 | 1.1
Mylar | 335 | 153-198 | 0.18
Inner PCB | 350 | 182-228 | 1.6
Outer PCB | 350 | 172-218 | 0.8
Honeycomb | 330 | 153-198 | 6
Outer glass
Inner glass
Mylar
Inner PCB
Outer PCB
Honeycomb
Gas Mixture(Pre-mixed) | Freon 90% iso-butane 5% SF6 5%
Working Voltage | ±6800V
Electrical field | ~108.8kV/cm

## Slide 6
TOF electronics
Fast preamplifier：
Maxim3760 (RICE Univ.)
Ninos (TOT) (ALICE)
Padi (TOT) (GSI)
CAD (TOT)(Tsinghua)
QDC (CAEN, 25fC/bin)
TDC
HPTDC (ALICE, 25ps/ch)
GET4 (GSI, 25ps/ch)
FPGA TDC (GSI and other)
DAQ

## Slide 7
7
Comparison of different FEE
 | CAD-1.0 | PADI-1 | NINO-25 | NINO-13
Peaking time | ~1ns | <1ns | 1ns | 0.6ns
Linear range | 1000mA*1 | -60-60mA*1 | 0-100fC*2 | 0-100fC*2
Time jitter | <20ps, rms*3 | <15ps, rms*4 | 10-25ps, rms | 6-25ps, rms
Power consumption | 10mW/ch | <30mW/ch | 30mW/ch | 5mW/ch
Input type | S.E. | DIFF. | DIFF. | DIFF.
Input impedance | 50-70W | 48-58W | 30-100W | 30-100W
Discriminator threshold | 263mA*1 | 10-400mA*1 | 20-100fC*2 | 20-100fC*2
CMOS process | 0.35mm | 0.18mm | 0.25mm | 0.13mm
*1: for current pulse with 0.3ns rise time, 1-2ns FWHM, and 0.3ns fall time
*2: for square current pulse with 200ps width
*3: for 200mA input current
*4: for 100mA input current

## Slide 8
Cosmic test
Cosmic ray test@Tsinghua August, 2011
Efficiency > 95% @ 96kV/cm (6.0kV)
Time resolution: ~ 52ps
PMT3
PMT4
PMT0
PMT2
PMT1
MRPC
Cosmic Ray Muon

## Slide 9
2.Beam test @ Hall A
Shield
High Energy e-
Top View
PMT1
PMT2
PMT3
PMT4
PMT0
Target
Target
Test setup
The diagram of DAQ system

## Slide 10
5.Results & Comparison: Calibration
Example: r175
Operated on May 13th
High Voltage: ±6800V
Condition: 10m from
target, shielded
PMT before calibration
MRPC before calibration
4 calibrations
Charge Cut：2 σ
Position Cut：2 σ

## Slide 11
Calibration of PMT
Calibration of MRPC
5.Results & Comparison: Calibration
Example: r175
Operated on May 13th
High Voltage: ±6800V
Condition: 10m from
target, shielded
Time resolution: 76ps
σ-PMT = 2.937(102.8ps)
σ-MRPC = 3.646(127.6ps)
σ-MRPC = 2.16(75.6ps)
In this test, T0 is about 100ps, the time resolution is deteriorated.

## Slide 12
5.Results & Comparison: HV Scan
Time Resolution: ~75ps
Efficiency: >95%

## Slide 13
5.Results & Comparison: Rate Scan
Voltage: 6800V
Flux:11kHz/cm²
Efficiency:~95%
Time Resolution: 78ps
Flux:16kHz/cm²
Efficiency:~95%
Time Resolution: 82ps

## Slide 14
5.Results & Comparison: Flux vs. Time
Run188, 6800V (5m to target, shielded)
Run193, 6800V (5m to target, not shielded)
2.5kHz/cm²
6kHz/cm²
12kHz/cm²
14-15kHz/cm²
16-18kHz/cm²
During a run, flux is not on a stable level, which from less than 3kHz/cm² to 16kHz/cm².
We can observe the performance by selecting data from different flux.

## Slide 15
Charge spectrum at different rate
5.Results & Comparison : Charge Distribution
Base Line
Signal
Significant reduction of charge distribution can be seen as the background rate increases.
The reduction of electrical field is caused mainly by both background irradiation and electron beams.
Rate capability of the counter is higher than 15kHz/cm².

## Slide 16
5.Results & Comparison : Beam Test
Beam Test@HZDR June, 2012

## Slide 17
5.Results & Comparison : Beam Test
17
Time Resolution < 40ps
Beam Test@HZDR June, 2012
HV scan
Rate scan

## Slide 18
6.Conclusions
Performance of MRPC is measured. The time resolution can reach 70-80ps and the efficiency is higher than 95%. The flux is up to 16kHz/cm².
The MRPC module is placed within 10m to the Target for 2 months, without significant performance deterioration. This means that the module can withstand long time irradiation.
The Irradiation is uniformed. During Test, the current is large even when the rate is not very high, which means the photon or neutron background irradiation is very strong.

## Slide 19: Thank you!
End