## Slide 1: Track Vectoring
T.K. Hemmick

## Slide 2: Background in SoLID Trackers
Studies by Richard Holmes.
PVDIS w/no baffles…
Signal Projective
Bkg non-Projective
Signal MIP
BKG Large Signal

## Slide 3: How to measure both?
E-deposit measurements plagued by Landau Tail.
  Measure more samples on the track.
  Use a “truncated mean” to refine dE/dx.
  ALSO does e/pi separation at low momentum.
Thick collection gap = track vector.
Drift Gap
Transfer 1
Induction
Transfer 2
GEM 1
GEM 2
GEM 3
Mesh
X-Y Strips
Pitch: 400um
17mm
1.5mm
2mm
1.5mm
Preamp/Shaper
Primary Charge
Fluctuation

## Slide 4: Downside: Data Size
A detector “layer” comes from the pre-amp shaping time.
Simple model: Detector is like layers
  “Synchronous” Background: Data up, occupancy same.
  “Asynchronous” Background: Data up, Occ up
Possibly untenable due to high background rates.
Requires quantitative analysis
Orig. data
Extra data
Ghost of Tracks Past
Ghost of Tracks Yet to Come
signal
Signal:
--Starts on time
--Ends on time
--Single channel

## Slide 5: Mini-Drift GEM Det. + SRS Readout
Std. 10x10cm CERN 3-GEM Det.
ArCO2 (70/30)
Gain ~ 6500
~17mm Drift Gap
Drift Time ~600ns
SRS /512 channels APV 25
30 x 25ns Time Samples
Martin Purschke’s newly
developed RCDAQ
affords high flexibility
COMPASS style Readout:
256 x 256 X-Y Strips
~10cm x 400um pitch
Drift Gap
Transfer 1
Induction
Transfer 2
GEM 1
GEM 2
GEM 3
Mesh
X-Y Strips
Pitch: 400um
17mm
1.5mm
2mm
1.5mm
Preamp/Shaper
Primary Charge
Fluctuation
X
Y

## Slide 6: Preliminary Bench-Top Measurements
GEM trigger doesn’t provide precise timing, so rely on ability to measure the first pad fired as a measure of t_zero
Det. requirements: high gain, low noise, low diffusion gas
Use timing from ADC to reconstruct z-coord. of track
~50mm
Sr-90
Brass Source Holder
Tungsten Collimator
1.00mm hole
GEM TRIGGER
1nF
Reconstructing Low Energy Sr90 b- Tracks
Reconstructing Cosmic Ray Tracks
X-Axis
Y-Vector
Y-Axis (mm)
Top Scintillation Counter
GEM Detector
Bottom Scintillation Counter
Y-axis
Reconstructed Vectors
Reconstructed Vectors
Y-Axis

## Slide 7: Measuring Tracks at CERN Beam Test
finger
Sci (SA)
Beam profile
wire chamber
726
Si3
Si6
Y-inverted
26
26
Jura
TOP VIEW
Si1
26
s1
s640
z
x
y
veto
Sci
SB
SD
5
SB
Saleve
170
15
SC
5
41
X
X
X
X
X
X
X
X
T1
T2
T3
T4
T5
T6
T7
T8
XY
XY
Tmm3
Tmm2
XY
Tmm5
Freiburg frame
-θ
XY
Tmm6
1250
205
(π+, +120GeV/c)
s128
s256
s1
s1
s256
178
L1
X
410
2
XY
R17A
XY
R17B
Saclay
irradiated
Z1
XY
Test Beam Set Up at ENH1-H6 SPS Beam
3-GEM
Mini-Drift on
Rotating Table
10-12 Layer Micromegas Telescope
Si Tracking System
MM Telescope
Mini-Drift GEM
Si Tracker
120GeV/c
p+

## Slide 8: Beam Test Results (40 deg. Tracks)
Reconstructed Track from 1 Event
Raw Strip Signal
25ns Time Sample
Strip
~Strip Charge
Tot. Charge at each fired Strip
Strip Charge Arrival Time
The charge arrival time for each strip is determined by the time profile of the raw signal. The z-coord. is then reconstructed by taking the product of the arrival time and the drift velocity of the detector gas.
The x_coord. is taken as the center of each strip.
The vector is determined from a linear fit to the reconstructed (x, y) pairs for the event.
Reconstructed Track Segment

## Slide 9: Data Processing
Propagated Errors:
Angle: ~+/-18mrad
Charge arrival time: ~+/-1.8ns
Linear Fit to determine arrival time = x-int.
30 samples x 25ns = 750ns window
Raw Data: Waveforms in Time
Vector Signature: “Charge square”
Vector Recon:
X -coord. = middle of pad
Y-coord. = drift time * Drift Vel.
Fit (x,z) points to line
Vector Recon. Z-residual < 0.5mm

## Slide 10: Angular Resolution
Track Recon. Fails
(Rely on Charge Centroid)
Uncertain Boundary
Track Recon. Successful
MC Simulation of Angle and Position Resolution
A first look at the Angular Resolution
As a first attempt to determine the angular and position resolution, we do so without the aid of a reference track, determined by the high precision reference detectors within the beam test set up.
The angular resolution is determined here by simply taking the spread in the distribution of the reconstructed vector angle. This is known to be a reasonable approximation since the beam divergence is minimal.
T. Cao, Stony Brook
Preliminary Results
Preliminary Results

## Slide 11: Summary
Great idea for synchronous background rejection.
Ghosts of bunches past:
  Stubs appear to “end early”.
Ghosts of bunches future:
  Stubs appear to “begin late”.
Quantitative question:
  Does it hurt, does it help?