## Slide 1: Update on EM Calorimeters
Jin Huang (LANL), also for
Mehdi Meziane (Duke), Paul Reimer (ANL),
Zhiwen Zhao (UVa), Xiaochao Zheng (UVa)

## Slide 2: Overview

## Slide 3: SoLID EM Calorimeter Overview
PVDIS forward angle
SIDIS forward angle
SIDIS large angle
SoLID EM Calorimeters | Polar Angle (degree) | P (GeV / c) | Max π / e | Cerenkov Coverage | Area (m2)
PVDIS Forward-Angle | 22 - 35 | 2.3 – 6 | ~ 200 | <3-4 GeV/c | ~17
SIDIS Forward-Angle | 8-15 | 1 -7 | ~ 200 | <4.7 GeV/c | ~11
SIDIS Large-Angle | 17-24 | 3 - 6 | ~20 | None | ~5

## Slide 4: Default design for calorimeter modules
Preshower – HERMES/LHCb style passive radiator + scintillator design
  2 X0 lead radiator + 2 cm scintillator tile w/ WLS readout
Shower – COMPASS style Shashlyk calorimeter design
  Layer structure : 0.5 mm lead + 1.5 mm scintillator + 0.12 mm gap x 2
  X0 = 24cm, RM ~ 5 cm, 194 layers, 43 cm in depth

## Slide 5: Shower – quick review
Choice of technology
  Shashlyk design was chosen based on advantage of radiation resistance + cost + ease of readout
Features
  Pb/Scint ratio 1:3 (V) : chosen to reach <5%/√E energy resolution and ~100:1 pion rejection
  Scintillator thickness of 1.5mm: based past designs to balance sampling fineness VS lateral light transmission loss
  Total length of 20 X0 : contain 98% of shower and maximize pion-electron difference → MIP = 270 MeV (real) / 320 MeV (reconstructed)
  Lateral size of 10x10 cm2: max size allowed (to reduce $$) before position resolution significantly deteriorates (σ~1 cm after cor.)

## Slide 6: Preshower – quick review
Choice of technology
  HERMES/LHCb style VS full Shashlyk design, former is much easier to readout and high in radiation resistance
Features
  Absorber of 2 X0 lead :
    Thinner – loose preshower rejection
    Thicker – loose shower resolution
    Scanned for 1.5, 2 and 3 X0; 2 X0 serve SoLID best
  Scintillator of 2 cm:
    MIP = 4 MeV, electron cut ~ 3 MIP

## Slide 7: Design Updates - Layout Update

## Slide 8: SIDIS and PVDIS FAEC (beam view)
Both can share supporting structure, only need to move along beam direction to change configuration
Supporting structure needs to be made from 100cm to 261cm
261cm
118cm
100cm
215cm
PVDIS FAEC (green + blue)
SIDIS LAEC (blue + red)

## Slide 9: Ideas to minimize SIDIS LAEC Acceptance gap
We want to cover full azimuthal angle and leave no gap between modules, so module can not be tilted and need to be along Z axis
Prefer having short outer module so that the outer module area can cover more and inner module area can cover less
Inner module need to be special shape to avoid blocking acceptance. One way to solve it is to have smaller 5x5cm (like COMPASS) module with various length
24o
14.7o
inner module
(150mm in radius)
Outer module
(500mm in radius)
17.5o
Blue: LAEC acceptance angle
Orange : angle between inner and outer
600mm
600mm
5x5x41cm
10x10x60cm module
assume 600mm full module length
5x5x22cm
Reviewed using G4 simulation next few pages

## Slide 10: SIDIS LAEC (beam view)
Type I (10x10cm) module in blue, type II (5x5cm long) module in green, type III (5x5cm short) module in purple.
Supporting structure needs to be made from 75cm to 140cm
140cm
75cm

## Slide 11: Design Updates - Edge effects for LAEC

## Slide 12: LAEC layout in G4 Simulation

## Slide 13: LAEC in full standalone G4 Simulation Track transportation provided by GEMC, CLEO field

## Slide 14: How much does inner modules help?
Stand conf. 404 10x10 cm2 modules
+ 116 5x5 cm2 inner modules
Minor improvement
LAEC catch 80% of shower
Go freely to forward acceptance

## Slide 15: Design Updates - Shower cluster size cut

## Slide 16: Previously showed pion rejection
PID selection used 3-D cut on PS, e/p and momentum
PS and e information come from sum signal in all non-zero modules
Enemy here is very specific: almost fully absorved hadronic shower with high energy deposition
94% electron eff.

## Slide 17: Shower area difference
R spread (mm)
Φ - spread (mm)
R spread (mm)
Φ - spread (mm)
Notice the difference in color scale
Electron shower
Hadronic shower (e/p>80%)

## Slide 18: Apply additional cut to limit max size of cluster around track projection
Pion
Limit cluster to be not larger than 3x3 modules around track projection to shower central depth
Minor cut on EM shower but effectively removed hadronic showers of very high energy deposition
Miss identified
w/ >=94% electron eff.
BIG improvement @ high p end
Flat phase space in PVDIS
acceptance

## Slide 19: Can it be further improved?
Pion
Further limit cluster to be not larger than 2x2 modules around track projection to shower central depth
Now loose ~5% of EM shower, but hadron shower cuts faster
Miss identified
Change cut and maintain
>=94% electron eff.
All hadron rej. better than
100:1
Flat phase space in PVDIS
acceptance

## Slide 20: Design Updates - Radiation dose

## Slide 21: What’s new
LHCb/HERMES preshower, instead full Shashlyk preshower
  As shown before, the preshower scintillator receive most of the radiation, due to the low energy backgrounds
  This part radiation dose are now absorbed in 2X0 absorber, and we just see its EM tail now
  Especially, lead absorber effectively kill all low energy electron background
New background distribution updated by Zhiwen
  SIDIS:
    With target collimator (suppress background by 4)
    First large angle simulation
  PVDIS: have option to remove direct photon sight (expected to be removed in the final baffle design)
Dominating background, photons 1-10 MeV
  After preshower, which attenuate them a lot, they still penetrate ~10 layers in Shashlyk

## Slide 22: PVDIS – current baffle (with direct γ)
Layer #1 is 2cm preshower scint.
γ dominate
But attenuated quickly

## Slide 23: PVDIS – preview for a baffle w/o direct γ
Layer #1 is 2cm preshower scint.
γ get reduced by ~5
π- become important here

## Slide 24: SIDIS – Forward
Layer #1 is 2cm preshower scint.
γ dominate
But attenuated quickly

## Slide 25: SIDIS – Large-Angle
Layer #1 is 2cm preshower scint.
γ dominate
But attenuated quickly

## Slide 26: Light Readout

## Slide 27: WLS fiber in scintillator pad
Drill on scintillator and glue WLS in
Used by LHCb etc.
Will use by CLAS12 FT-Hodo
LHCb Preshower
CLAS12 FT-Hodo

## Slide 28: Fiber
WSL fiber in shower, 100/module
  Bicron BCF-91A
    multi-clad, 1/e length >3.5m
    1mmD, bend 20cmD (?)
    $0.87/m
    less rad hard
WLS fiber in preshower pad, 1-2/module
  KURARAY Y-11(200)MS
    multi-clad, 1/e length >3.5m
    0.5mmD, bend 5cmD
    $1/m
    more rad hard
Clear fiber for both, 101-102/module
  Bicron BCF-98
    $1/m

## Slide 29: Fiber connection
Shower will use 1-1 bundle fiber connector.
  Used in previous experiments (LHCb, Minos)
  custom made fiber connector $175/module, quote by LEONI
Preshower will use comercial 1-1 single fiber connector, a few $ each.
LHCb shower
fiber bundle to PMT connector, cost estimate $25/module

## Slide 30: Readout
PMT option - Hamamatsu R3998-02
  28mmD Bialkali Photocathode
  $600 each
  Used by CLAS TPE calorimeter which has COMPASS module
  As our baseline design
APD/SiPM option
  High resistance to magnetic field
  Need to be careful due to high neutron background
  Contacting vendor for high radiation resistance designs (sensor + amp.)
  Estimating neutron background @ photon detectors

## Slide 31: Budget Update

## Slide 32: Budget table – calorimeter group version
+ Prototyping ~ 0.3 M$
Lab estimate : 5.7 (base)+3.8 (Labor)
JP : 6.2 (base) + 1.3 (Labor)

## Slide 33: What we need

## Slide 34: What we need
Engineering support (Zhiwen)
  Support structure
  How to do maintenance and install it back
Inquiries
  IHEP (Xiaochao)
  Fiber connection (Mehdi)
  Photon detectors (Zhiwen)
Background effect (Jin)
  Event mixing with signal and background simulation
Prototyping

## Slide 35: Support structure ideas
Overview
  One support for LAEC, one support
  for FAEC
  Only a few cm gap between outer radius of SIDIS LAEC and inner radius of cryo, is it enough?
  Only a few cm gap between outer radius of FAEC and inner radius of nose cone, is it enough?
  Need to consider the supporting with overall magnet cryo and yoke structure.
“super” Modules
  Group 1-3 row of modules into supermodule
  shift supermodule’s horizontal position to make layers

## Slide 36: backup

## Slide 37: WLS radiation hardness

## Slide 38: Fiber connection (Backup option)
Fiber splicing
  Robust connection and excellent transmission (2%)
  CLAS12 Forward Tagger Hodoscope will fuse WLS and clear fiber. Commercial vendor has been contacted and They are also developing their own method.
  We will collaborate with them to examine the labor and cost requirement.
joint