## Slide 1: SoLID Calorimeter Support Structure
Paul E. Reimer and Vic Gaurino
22 March 2013
This work is supported in part by the U.S. Department of Energy, Office of Nuclear Physics, under Contract No. DE-AC02-06CH11357.

## Slide 2: SoLID EM Calorimeter Overview
PVDIS forward angle
SIDIS forward angle
SIDIS large angle
SoLID EM Calorimeters | Polar Angle (degree) | P (GeV / c) | Max π / e | Cerenkov Coverage | Area (m2)
PVDIS Forward-Angle | 22 - 35 | 2.3 – 6 | ~ 200 | <3-4 GeV/c | ~17
SIDIS Forward-Angle | 8-15 | 1 -7 | ~ 200 | <4.7 GeV/c | ~11
SIDIS Large-Angle | 17-24 | 3 - 6 | ~20 | None | ~5
Slide borrowed from Jin Huang’s presentation at an earlier SoLID collaboration meeting

## Slide 3
Slide borrowed from Jin Huang’s presentation at an earlier SoLID collaboration meeting

## Slide 4: Module Shape
Switched to Hexagonal modules
Better for radially oriented support structure
Kept Front surface area the same
  Almost—allowances for
  Support sag
  Manufacturing tolerance
  Light tight wrapping

## Slide 5: Layout of endplate 2:30 sector
Mount “wedges” on rails at outer raidus
Configuration change
Not moving modules forward-barrel
  Just slide on rails
Moving modules forward-barrel
  Remove from endcap
  restack calorimeter modules
Rail Mount

## Slide 6: Assembly of 3 Wedges
Beam
Rail Slides
Beam

## Slide 7: Plate Thickness
40 mm thick
20 mm thick
Beam

## Slide 8: Wedge-wedge interface
At interface between wedges, need to allow wedges to slide past each other
Forces each end plate to be different
  (there are symmetry axes though)

## Slide 9: Deflection calculation
0.59mm

## Slide 10: Barrel Mounting
Similar design, but cut at different radii
Open question: What will support the rails in the barrel?

## Slide 11: Cost
Vic: “I think this is a pretty high end estimate.”
Next step is to take drawings to shop and get better estimates
Barrel will add another $80k
Item |  | Cost Each | No. | Total |  | 
Upstream Endplate |  |  |  |  |  | 
 | setup | $1,000.00 |  |  |  | 
 | material | $2,000.00 |  |  |  | 
 | shop time | $1,000.00 |  |  |  | 
 | total |  | 1 | $4,000.00 |  | 
Downstream Endplate |  |  |  |  |  | 
 | setup | $500.00 |  |  |  | 
 | material | $2,000.00 |  |  |  | 
 | shop time | $1,000.00 |  |  |  | 
 | total |  | 1 | $3,500.00 |  | 
Inner end piece |  | $200.00 | 1 | $200.00 |  | 
Outer end piece |  | $300.00 | 2 | $600.00 |  | 
Rail Bearing |  | $500.00 | 4 | $2,000.00 |  | 
Rails |  | $400.00 | 2 | $800.00 |  | 
Wedge total |  |  |  | $11,100.00 |  | 
Total cost |  |  |  |  | 12 | $133,200.00

## Slide 12: Conclusions
We have support structure
  Still can be optimized
  Cost:
    thickness of materials
    Shop estimates
  Trade off on upstream vs downstream endplate thickness