## Slide 1: Current Status of Experimental Requirement in Technical Document
Xin Qian
Caltech

## Slide 2: Introduction
Consistent plots for each configuration (Zhiwen)
Two tables summarize key features and detector requirements
We should clarify requirements vs. limitations

## Slide 3: SoLID-PVDIS

## Slide 4: Key Information
Phase Space:
  2035 degrees
  1.5  5.0 GeV (include 6.6 GeV running)
  0.2<x<0.8
  2 < Q2 < 12 GeV2
  Luminosity 5x1038 LH2 1.3x1039 LD2
  ~0.5% relative statistical uncertainties
Requirements:
  0.4% beam polarimetry
  <0.5% pion contamination determination
  <0.5% Q2 calibration
  Baffle + radiation hardness
DAQ rate:
  15 kHz x 30 sectors
  Signal: ~ 8 kHz DIS electron per sector

## Slide 5: Comments about requirement
The physics requirement is straight forward
  Should not be mixed with limitations
See the example below:
  Requirement: ~8 kHz DIS electron rate per sector
    Be included in the data after L3 (to tape)
    No direct requirement on L1 trigger
  Limitations to be considered in the design
    APV25: 3 sample readout  90 kHz maximum
      1 Sample: 280 kHz
    Crate data transfer limit: 20 kHz  140 MB < 300 MB
      2 Crates  600 MB
    Iterations needed, interactions among different sub-groups

## Slide 6: One Word about Safety Margin
Safety margin is linked to the requirement:
  Example: Know the pion contamination to <0.5% level
    Assume 200:1 pion/e ratio  2.5e-5 knowledge in rejection factor by combining calorimeter and gas Cerenkov
    Guideline: gas Cerenkov 500:1 rejection Calorimeter 100:1 rejection
  Calorimeter working group does the design
    With assumptions in background rate, performance, segmentations and …, one can reach 100:1
    The safety margin should be estimated from the evaluation of assumptions
    Uncertainty of assumptions should be clearly stated and listed

## Slide 7: SoLID SIDIS

## Slide 8: Key Information
Kinematics Coverage:
  0.05 ~ 0.6 in x (valence)
  0.3 ~ 0.7 in z (factorization region)
  PT up to ~ 1 GeV (TMD Physics)
  Fixed target  Q2 coverage 1-8 GeV2 (~ 2 GeV2 in ΔQ2 at fixed x)
Polarized 3He Target:
  Unpolarized ~ 1037 N/cm2/s
  ~ 60% higher polarization
  Fast spin flip (<20 mins)
PID:
  <1% Pion contamination
  <1% Kaon contamination
DAQ:
  ~ 3kHz Physics Coincidence
  ~ 120 kHz Single
  ~ 80 kHz Coincidence

## Slide 9: Detector Resolution
Include multiple scattering from target, air, and GEM chambers

## Slide 10: SoLID-proton-SIDIS
Polarized NH3 Target:
  Unpolarized ~ 1036 N/cm2/s
  ~70% higher polarization
  Spin flip
Do we have a plot with better quality?

## Slide 11: Sheet of Flames
How to better illustrate this one?
Shielding or/and removing detectors!

## Slide 12: SoLID J/Psi
Similar design as SIDIS
DAQ: Triple Coincidence Trigger
  scattered electron, decay electron and decay positron from J/ψ ~ 3 kHz
  3 clusters in calorimeters

## Slide 13: Configuration Optimization (Zhiwen)
Eγ < 9.15 GeV
CLEO configuration:
Assume J/ψ target center at -300 cm, require ~ 4.5% increment in GEM area
No additional changes to SIDIS configuration
Factor of 3 increment in FOM
Potential conflict between yoke and target chamber

## Slide 14: Program Summary
Missing anything?

## Slide 15: Detector Summary
Missing anything?
Geometry of Calorimeter and GEMs?