Update on EM Calorimeters
Calorimeter Group

---
SoLID EM Calorimeter Overview
PVDIS forward angle
SIDIS forward angle
SIDIS large angle
SoLID Collaboration Meeting

---
Module Design @ last meeting
Preshower (PS) – HERMES/LHCb style passive radiator + scintillator
2 X0 Pb radiator + 2 cm scintillator tile w/ WLS readout
Shower – COMPASS style Shashlyk calorimeter design
Layer structure : 0.5 mm lead + 1.5 mm scintillator + 0.12 mm gap (x2); X0 = 24cm, RM ~ 5 cm, 194 layers, 43cm total in depth

---
Updates since last meeting
Additional Scintillator pad before Preshower for photon background rejection – for FAEC, being discussed for LAEC.
Module shape changed from 10x10cm2 square to 100cm2 hexagon (6.25cm/side) due to support design.
Now include background in the PID and other performance simulation
today will report on SIDIS FAEC PID & Trigger;
work ongoing for SIDIS LAEC and PVDIS.
Updates on fiber connection and total EC cost estimate

---
Photon-rejecting Scintillator Pad
Scintillator Pad
Scintillator Pad (SPD): 0.5cm, reject high energy photons for electron trigger and hadron trigger at SIDIS forward angle.
Less segmentation than PS, readout by WLS fiber → clear fiber → PMT.

---
Simulation

---
Thin scintillator pad to reject g 's at trigger level
5mm Sc pad;
Background dominated by low energy electrons: 20% from end cap of heavy GC, other from more upstream
Have to be placed before MPRC (which has lots of material for conversion)!
 Electron
Low energy g
All
104
102
0 100 200 R(cm)
background rate per cm2 in Sc:

---
Optimizing # Segment
Photon background dominated by 1-2 GeV.
A 50ns coin window with corresponding calorimeter (Shower) assumed, will be better at FPGA level.
Trigger require 5:1 rejection → 120 segments (could be 60 fans divided into 2 sections/fan) → 2MHz MIP rate/segment
Overall photon rejection
15
10
5
0
 Low-E (1-2 GeV)
 Full E range (1-7 GeV)
0 100 200 300 400 500 600
# segments

---
Hexagon Calorimeter Simulation
Projection in sideview
Projection along z
4cm Al backplane
2X0 lead absorber
2cm PS scint
2cm Al frontplane
3GeV electron shower on hexagon calorimeter grid;
Support Al plates just added, not used in the results of following slides

---
PID with Hexagons
Revised with hexagon, no big diff.
No background yet included
(last meeting: square
module 3x3 clustering
94% electron efficiency)
0.025
0.020
0.015
0.010
0.005
0
 p efficiency
 e efficiency
0.98
0.96
0.94
0.92
0.90
0.88
0.86
0.84
0.82
Expect go high w/ higher stat.
Preshower ID power drop significantly at this bin
1 2 3 4 5 6 7 p(GeV)
1 2 3 4 5 6 7 p(GeV)
1 2 3 4 5 6 7 p(GeV)

---
Status of Background Simulation
3rd iteration of GEMC + CaloSIM background study

---
Calorimeter Background Simulation with GEMC + CaloSIM
GEMC simulate background particles at the front surface of EC (Zhiwen);
CaloSIM build calorimeter response;
Combine above two and sum over all contributions (EM, DIS, pi0, pi+,pi-) stochastically within a 50ns coincidental window → background distribution at each trigger
Embed background into signal simulation (high energy e, pi) and perform analysis (clustering, e/pi separation, etc.)

---
SIDIS FAEC Background
2X0 of Pb in preshower absorbs all electrons, and reduces photon background from 1GHz/cm2 to 10kHz/cm2 (MIP signal), still, 1-100MeV photons dominate.
3MHz MIP rate / 100cm2 PS at inner radius;
10x lower at outer radius, could bundle multiple modules for PMT readout.
SIDIS FAEC background rate per cm2
104
102
 Electron
Low energy g
All
0 100 200 R (cm)

---
Background Energy deposit in Scintillators
bg vs. e-
bg vs. p-
ESH(MeV)
ESH(MeV)
bg vs. p- vs. e-
bg vs. p- vs. e-
EPS(MeV)
ESH(MeV)
significant in preshower
less significant for shower
EPS(MeV)
EPS(MeV)
Counts per 0.2MeV for 50k events
Counts per 0.2MeV for 50k events

---
SIDIS FAEC PID w/ background: No change in eff., reduced rejection at low-p
Rejection reduced due to preshower pile up
 p efficiency
 e efficiency
0.96
0.90
0.84
0.05
0.04
0.03
0.02
0.01
0
w/o background
w/ background
1 2 3 4 5 6 7 p(GeV)
1 2 3 4 5 6 7 p(GeV)

---
Radiation dose prediction now with background – remain stable
Dose is not a problem for SIDIS configuration.
Calorimeter design should stand 500krad, now expect 100krad – nice safety margin
Still missing final PVDIS radiation dose, need final baffle w/o direct line of sight.
SIDIS – He3– Forward Calorimeter
SIDIS – He3– Large Angle Calorimeter

---
Hexagon Calorimeter Trigger with Full Background
6+1 cluster contains ~96% of shower energy

---
Hexagon Calorimeter Electron Trigger Using 6+1 cluster energy
Do observe very high electron efficiency in simulation
However, shower cut must be low to accept low-p electrons. This limits the rejection for high-p pions. See next slide.
Possible solution:
From DAQ group (Xin, Alex): use position dependent threshold,
consider including preshower trigger

---
 p efficiency with cut
 p efficiency with cut
0.50
0.40
0.30
0.20
0.10
0.00
0.55
0.50
0.45
0.40
0.35
0.30
HEX1+6 Trigger
> 0.95GeV
HEX1+6 Trigger
> 1.95GeV
1 2 3 4 5 6 p(GeV)
1 2 3 4 5 6 p(GeV)
* Accepted
* All
E/p vs. p
E/p vs. p
1 2 3 4 5 6 p(GeV)
1 2 3 4 5 6 p(GeV)

---
Hexagon Calorimeter Pion Trigger Efficiency
 p efficiency with cut
0.990
0.980
0.970
Trigger cut: HEX1+6 trigger raw signal > 85% MIP (which is MIP – 2σ = 220MeV calibrated)
Background passes this cut: rate ~20Mhz, dominated by photon.
With a 5:1 photon suppression from scintillator, we get ~4MHz total trigger rate, which fit in the DAQ limit (PR12-10-006)
Will join global DAQ study for final verification
1 2 3 4 5 6 p(GeV)
E/p vs. p
* Accepted
* All
1 2 3 4 5 6 p(GeV)

---
Design Updates – Fiber connectors

---
@ last meeting
LHCb shower

---
Now: Fiber connector conceptual design from LEONI Fiber
100 fibers/connector:
made of Al
35% light loss at worst
$100/each
fiber bundle to PMT connector, estimate $25/module (Leoni)
1-1 fiber for PS: $10 each (other companies)

---
Budget @ last meeting
5.8M, to be compared to next slide
- + Prototyping ~ 0.3 M$
- + Support ~

---
Budget Update (no new Sc Pad yet)
IHEP (not including fibers) for 1700 PS+SH
Preshower: $112k-$120k
Shower: $549k-$651k
Structure+assembly: $255k-$340k
IHEP total: ($1.22-$1.51)M + 24% overhead (2012 rate) = ($1.51-$1.87)M
Fiber connectors+tubing (Leoni+other): ~$300k
WLS+clear fibers(?): $703k (S.G.) - $2.47M (Kuraray)
PMTs: $600x2x(~1900)=$2.28M
Total from above (no contingency): ($4.8M-$5.2M) if using S.G.; $(6.6-7.0)M if using Kuraray
Labor? Shipping? Overhead? Contingency?

---
Plan
PID and Trigger study with background for SIDIS LAEC and PVDIS;
Discussing overlapping module readout with DAQ group;
Ongoing studies to reduce PMT cost:
Multi-anode PMTs ($100/channel) to read out Preshower, but there are gain matching issues.
Smaller PMTs to read out Preshower
Need solid quotes for PMTs

---
backup

---
Simple illustration of timing pileup vs. # segments – using only 1MIP events
60 sectors
4 MHz MIP
(20%)
30 sectors
8 MHz MIP
(40%)
240 sectors
1 MHz MIP
(5%)

---
Online: Trigger with background
Hadronic shower which introduce a pion contamination, usually spread into larger area compared to EM shower
A localized trigger, e.g. HEX1+6 trigger can significantly suppress the hadron response, while maintaining high eff. for electrons
Ratio of EM shower contained
Ratio of Pion shower contained

---
Shower – quick review
Choice of technology
Shashlyk design was chosen based on advantage of radiation resistance + cost + ease of readout
Features
Pb/Scint ratio 1:3 (V) : chosen to reach <5%/√E energy resolution and ~100:1 pion rejection
Scintillator thickness of 1.5mm: based past designs to balance sampling fineness VS lateral light transmission loss
Total length of 20 X0 : contain 98% of shower and maximize pion-electron difference
→ MIP = 270 MeV (real) / 320 MeV (reconstructed)
Lateral size of 10x10 cm2: max size allowed (to reduce $$) before position resolution significantly deteriorates (σ~1 cm after cor.)

---
Preshower – quick review
Choice of technology
HERMES/LHCb style VS full Shashlyk design, former is much easier to readout and high in radiation resistance
Features
Absorber of 2 X0 lead :
Thinner – loose preshower rejection
Thicker – loose shower resolution
Scanned for 1.5, 2 and 3 X0;
2 X0 serve SoLID best
Scintillator of 2 cm:
MIP = 4 MeV, electron cut ~ 3 MIP

---
Simulation setup with hexagon calorimeter modules

---
Back up 1/2 for previous slides
All events
Accepted events w/ 3D cut
Electron eff. for SIDIS large angle calorimeter

---
Back up 2/2 for previous slides
All events
Accepted events w/ 3D cut
Pion eff. for SIDIS large angle calorimeter

---
Backup - Simulated efficiency & rejection
Electron
Pion
Photon
Energy range: 1-7 GeV, flat phase space for SIDIS-forward
MIP peak
~1:7 γ-rej with cut below MIP peak
Efficiency
Cut on energy dep.

---
Backup - Simulated efficiency & rejection
Most photon focus on lower energy side (π0 decay)
And lower energy photon produce less back scattering
Therefore, do the study again with 1<Eγ<2 GeV
Electron
Pion
Photon
1<Eγ<2 GeV
Efficiency
~1:20 γ-rej with cut below MIP peak
E dep for photons (MeV)
Eγ (GeV)
Cut on energy dep.

---
Design Updates
- Shape

---
Change from square to hexagon
Main reason from supporting structure and layout (see Paul Reimer’s talk)
Physics feature should be similar to square shape and we will go through test and prototyping

---
Design Updates
- Layout Update

---
SIDIS and PVDIS FAEC (beam view)
Both can share supporting structure, only need to move along beam direction to change configuration
Supporting structure needs to be made from 100cm to 261cm
261cm
118cm
100cm
215cm
PVDIS FAEC (green + blue)
SIDIS LAEC (blue + red)

---
Ideas to minimize SIDIS LAEC Acceptance gap
We want to cover full azimuthal angle and leave no gap between modules, so module can not be tilted and need to be along Z axis
Prefer having short outer module so that the outer module area can cover more and inner module area can cover less
Inner module need to be special shape to avoid blocking acceptance. One way to solve it is to have smaller 5x5cm (like COMPASS) module with various length
600mm
assume 600mm full module length
Blue: LAEC acceptance angle
Orange : angle between inner and outer
10x10x60cm module
Outer module
(500mm in radius)
24o
5x5x41cm
inner module
(150mm in radius)
5x5x22cm
17.5o
600mm
14.7o
Reviewed using G4 simulation next few pages

---
SIDIS LAEC (beam view)
Type I (10x10cm) module in blue, type II (5x5cm long) module in green, type III (5x5cm short) module in purple.
Supporting structure needs to be made from 75cm to 140cm
140cm
75cm

---
Design Updates
- Edge effects for LAEC

---
LAEC layout in G4 Simulation

---
LAEC in full standalone G4 Simulation
Track transportation provided by GEMC, CLEO field

---
How much does inner modules help?
LAEC catch 80% of shower
Go freely to forward acceptance
Minor improvement
Stand conf. 404 10x10 cm2 modules
+ 116 5x5 cm2 inner modules

---
Design Updates
- Shower cluster size cut

---
Previously showed pion rejection
94% electron eff.
PID selection used 3-D cut on PS, e/p and momentum
PS and e information come from sum signal in all non-zero modules
Enemy here is very specific: almost fully absorved hadronic shower with high energy deposition

---
Shower area difference
Electron shower
Hadronic shower (e/p>80%)
R spread (mm)
R spread (mm)
Φ - spread (mm)
Φ - spread (mm)
Notice the difference in color scale

---
Apply additional cut to limit max size of cluster around track projection
Limit cluster to be not larger than 3x3 modules around track projection to shower central depth
Minor cut on EM shower but effectively removed hadronic showers of very high energy deposition
w/ >=94% electron eff.
Pion
BIG improvement @ high p end
Miss identified
Flat phase
space in PVDIS
acceptance

---
Can it be further improved?
Further limit cluster to be not larger than 2x2 modules around track projection to shower central depth
Now loose ~5% of EM shower, but hadron shower cuts faster
Change cut and maintain
>=94% electron eff.
All hadron rej. better than
100:1
Pion
Miss identified
Flat phase
space in PVDIS
acceptance

---
Design Updates
- Radiation dose

---
What’s new
LHCb/HERMES preshower, instead full Shashlyk preshower
As shown before, the preshower scintillator receive most of the radiation, due to the low energy backgrounds
This part radiation dose are now absorbed in 2X0 absorber, and we just see its EM tail now
Especially, lead absorber effectively kill all low energy electron background
New background distribution updated by Zhiwen
SIDIS:
With target collimator (suppress background by 4)
First large angle simulation
PVDIS: have option to remove direct photon sight (expected to be removed in the final baffle design)
Dominating background, photons 1-10 MeV
After preshower, which attenuate them a lot, they still penetrate ~10 layers in Shashlyk

---
PVDIS – current baffle (with direct γ)
γ dominate
But attenuated quickly
Layer #1 is 2cm preshower scint.

---
PVDIS – preview for a baffle w/o direct γ
γ get reduced by ~5
π- become important here
Layer #1 is 2cm preshower scint.

---
SIDIS – Forward
γ dominate
But attenuated quickly
Layer #1 is 2cm preshower scint.

---
SIDIS – Large-Angle
γ dominate
But attenuated quickly
Layer #1 is 2cm preshower scint.

---
Light Readout

---
WLS fiber in scintillator pad
Drill on scintillator and glue WLS in
Used by LHCb etc.
Will use by CLAS12 FT-Hodo
CLAS12 FT-Hodo
LHCb Preshower

---
Fiber
WSL fiber in shower, 100/module
Bicron BCF-91A
multi-clad, 1/e length >3.5m
1mmD, bend 20cmD (?)
$0.87/m
less rad hard
WLS fiber in preshower pad, 1-2/module
KURARAY Y-11(200)MS
multi-clad, 1/e length >3.5m
0.5mmD, bend 5cmD
$1/m
more rad hard
Clear fiber for both, 101-102/module
Bicron BCF-98
$1/m

---
Fiber connection
LHCb shower
fiber bundle to PMT connector, cost estimate $25/module

---
Readout
PMT option - Hamamatsu R3998-02
28mmD Bialkali Photocathode
$600 each
Used by CLAS TPE calorimeter which has COMPASS module
As our baseline design
APD/SiPM option
High resistance to magnetic field
Need to be careful due to high neutron background
Contacting vendor for high radiation resistance designs (sensor + amp.)
Estimating neutron background @ photon detectors

---
Budget Update

---
Budget table
 – calorimeter group version
+ Prototyping ~ 0.3 M$
Lab estimate : 5.7 (base)+3.8 (Labor)
JP : 6.2 (base) + 1.3 (Labor)

---
Budget Update

---
Budget table
 – calorimeter group version
+ Prototyping ~ 0.3 M$
Lab estimate : 5.7 (base)+3.8 (Labor)
JP : 6.2 (base) + 1.3 (Labor)

---
What we need

---
What we need
Engineering support (Zhiwen)
Support structure
How to do maintenance and install it back
Inquiries
IHEP (Xiaochao)
Fiber connection (Mehdi)
Photon detectors (Zhiwen)
Background effect (Jin)
Event mixing with signal and background simulation
Prototyping

---
Support structure ideas
Overview
One support for LAEC, one support
for FAEC
Only a few cm gap between outer radius of SIDIS LAEC and inner radius of cryo, is it enough?
Only a few cm gap between outer radius of FAEC and inner radius of nose cone, is it enough?
Need to consider the supporting with overall magnet cryo and yoke structure.
“super” Modules
Group 1-3 row of modules into supermodule
shift supermodule’s horizontal position to make layers

---
backup

---
WLS radiation hardness

---
Fiber connection (Backup option)
Fiber splicing
Robust connection and excellent transmission (2%)
CLAS12 Forward Tagger Hodoscope will fuse WLS and clear fiber. Commercial vendor has been contacted and They are also developing their own method.
We will collaborate with them to examine the labor and cost requirement.