1
Light Gas Cherenkov Detector for SoLID
E. Kaczanowicz, Z.-E. Meziani,
M. Paolone, N. Sparveris
Temple University
SoLID Dry Run
July 9th 2014

---
2
Detector Configurations and Requirements
- The LGC is designed to accommodate two primary configurations:
  - SIDIS
  - PVDIS
- Each configuration has different:
  - incident particle angle / momentum ranges
  - luminosity
  - background profiles
  - space constraints
Goal is to have each configuration provide a pion rejection above 99% when combined with the calorimeter.

---
2
Detector Configurations and Requirements
- The LGC is designed to accommodate two primary configurations:
  - SIDIS
    - 1 to 5 GeV
    - ~7 to 15 deg
  - PVDIS
    - 2 to 4 GeV
    - 22 to 35 deg
- Each configuration has different:
  - incident particle angle / momentum ranges
  - luminosity
  - background profiles
  - space constraints
Goal is to have each configuration provide a pion rejection above 99% when combined with the calorimeter.

---
2
Detector Configurations and Requirements
- The LGC is designed to accommodate two primary configurations:
  - SIDIS
    - 15uA on 3He
  - PVDIS
    - 50uA on D / H
- Each configuration has different:
  - incident particle angle / momentum ranges
  - luminosity
  - background profiles
  - space constraints
Goal is to have each configuration provide a pion rejection above 99% when combined with the calorimeter.

---
2
Detector Configurations and Requirements
- The LGC is designed to accommodate two primary configurations:
  - SIDIS
    - Forward Calorimeter
    - Additional Gems
  - PVDIS
    - Baffles
- Each configuration has different:
  - incident particle angle / momentum ranges
  - luminosity
  - background profiles
  - space constraints
Goal is to have each configuration provide a pion rejection above 99% when combined with the calorimeter.

---
2
Detector Configurations and Requirements
- The LGC is designed to accommodate two primary configurations:
  - SIDIS
  - PVDIS
    - Baffles
- Each configuration has different:
  - incident particle angle / momentum ranges
  - luminosity
  - background profiles
  - space constraints
Goal is to have each configuration provide a pion rejection above 99% when combined with the calorimeter.

---
3
LGC geometric / material characteristics
Cherenkov is designed to maximize component use between the two configurations.

---
4
Tank
- Primary tank toroidal shape:
  - 105 cm length
  - 71 to 85 cm inner radius
  - 265 cm outer radius
- Windows
  - Polyvinyl fluoride (Tedlar)
    - 1.45 g/mm3 density
  - 0.05 mm entrance window
  - 0.1 mm exit window
Common
Cherenkov gas is 65% C4F8O and 35% N2
Cherenkov gas
is CO2

---
5
Mirrors
- 30 sectors (defined by baffle segmentation)
  - 2 spherical mirrors per sector (60 mirrors total)
- Blanks are Carbon Fiber Reinforced Polymer [CFRP] (Same as LHCb RICH)
  - Areal density < 6 kg/m2
  - Reflective coating provided by Stony Brook (Al / MgF2 )
    - Total reflective area per mirror is roughly 0.3 m2
Common
SIDIS
PVDIS

---
PMT Assembly
6
- All components are common without adjustment between both configurations.
- PMT assembly is:
  - 3 x 3 array of Hamamatsu H8500C-03 maPMTS
    - 64 pixel PMT array for each H8500C
    - Average QE ~ 15%
  - Reflective cone
  - Mu-metal shielding.
    - 0.04” thickness with 0.125” thick steel reinforcement
    - Reduce BT and BL from 95 and 135 gauss (respectively) to < 50 gauss.

---
PMT Assembly
6
- All components are common without adjustment between both configurations.
- PMT assembly is:
  - 3 x 3 array of Hamamatsu H8500C-03 maPMTS
    - 64 pixel PMT array for each H8500C
    - Average QE ~ 15%
  - Reflective cone
  - Mu-metal shielding.
    - 0.04” thickness with 0.125” thick steel reinforcement
3 x 3 PMTs
Mu-Metal
Glass Cone

---
PMT Assembly
6
- All components are common without adjustment between both configurations.
- PMT assembly is:
  - 3 x 3 array of Hamamatsu H8500C-03 maPMTS
    - 64 pixel PMT array for each H8500C
    - Average QE ~ 15%
  - Reflective cone
  - Mu-metal shielding.
    - 0.04” thickness with 0.125” thick steel reinforcement
3 x 3 PMTs
Glass Cone
Mu-Metal

---
7
Simulation for pi rejection
- Event generation:
  - Electrons from electron generator eicRate.
  - Pions from eicRate (Wiser)
  - Uniformly distributed along target length.
- Propagate tracks out of target to LGC window
  - All interactions are handled by GEMC / Geant4
  - All materials from SoLID design are included in the transport.
  - CLEO magnetic field map is used.
- Simulate Cherenkov radiation through gas and collect optical photons.
  - Collection is recorded at the PMT on a p.e. per pixel level.
  - QE as a function of photon energy is taken into account.
  - Pion triggers below Cherenkov threshold are primarily from delta rays.

---
8
Total Collection Efficiency for Electrons
- Calculated as # optical photons detected at PMT divided by # of reflections from spherical mirrors. Includes:
  - Reflection efficiencies
  - Quantum efficiency (dominant)
  - Geometrical acceptance
- Aside: These simulations were done with older baffles and geometries! (circa 2012).
  - I can easily run all numbers again with latest baffles / geometries. It just takes CPU hours on the farm.
  - I don't expect any major changes.

---
9
Second Aside on Simulations
- All of these simulations are done with a personally modified GEMC 1.8 (additional reflectivity options + small changes).
  - Getting harder to collect all dependencies and install a working version with my modified GEMC.
  - Need to upgrade and update!
    - Should be done in scope of larger simulation efforts.

---
PVDIS
SIDIS

---
11
Pion / electron signal
- Sample of collected PE signal:
  (This MC is for track momentum below pion radiation threshold)
- Three settings possible pion rejection setting shown:
  - Nominal
  - 90% of Nominal
  - 80% of Nominal
Pions (Primarily knock-ons)
electrons

---
12
PVDIS
pi rejection factor is the
inverse pi acceptance
after selection cut.

---
12
PVDIS
pi rejection factor is the
inverse pi acceptance
after selection cut.
No calculation

---
12
PVDIS
pi rejection factor is the
inverse pi acceptance
after selection cut.
Generated pions
Generated electrons
No calculation

---
12
PVDIS
pi rejection factor is the
inverse pi acceptance
after selection cut.
Generated pions
Generated electrons
Pion efficiency is undefined
when there is no pion rate.
No calculation

---
13
SIDIS
pi rejection factor is the
inverse pi acceptance
after selection cut.

---
14
Secondary backgrounds
- All pion rejection shown on previous slides only considers the primary source of pion contamination from pion production at the beam / target nucleon vertex (via Wiser)
- Other sources of background come from secondary particle production.
  - Secondary background simulation is done by putting an 11 GeV electron beam on target in GEMC / Geant4.
    - 200M events are simulated per “pass” on the ifarm.
      - This equates to 0.64 micro-seconds of beam.
    - Geant4 physics list QGSP_BERT controls all EM / hadronic reactions.

---
15
Rate of particles through LGC entrance window
(PVDIS)
- Aside: Now using latest baffle configuration
- High luminosity + large acceptance = large rates
  - High rates can be handled, but care must be taken!
- Total rate through the LGC window for PVDIS.
  - Integrated over all momentums.

---
16
Rate of particles through LGC entrance window
- Aside: Now using latest baffle configuration
- Rate through the LGC window.
  - Only cherenkov radiation candidates.
Energies > LGC threshold
   (10 MeV gamma/electrons)
   (3 GeV pions)
   (2.4 GeV muons)
   (11 GeV kaons)

---
17
Accidental trigger rates per sector
- SIDIS accidental rates are relatively small.
- PVDIS rates are greater, but improved overtime with better baffle design.
PVDIS	Old 6 plane baffle (MHz)	Not as old 11 plane baffle (MHz)
1 or more pe's per sector	4.94	2.99
2 or more pe's per sector	3.44	1.93
1 or more pe's in two different PMTs	2.50	1.56
SIDIS	Rate per sector (MHz)
1 or more pe's per sector	0.319
2 or more pe's per sector	0.219
1 or more pe's in two different PMTs	0.128
PVDIS needs updating
with latest geometries /
baffles.
Rates are large, but manageable:
EC + LGC gives < 20 kHz per sector

---
18
Photons direct on PMTs
- Non-optical photons that interact with the maPMTs may also cause some background.
  - First step: Simulate the rate of these photons incident on the PMTs:
  - Two obvious peaks.
    - Neutron capture with hydrogen in carbon fiber mirrors.
    - e+ e- annihilation
  - Low energy photon rate still dominated by electron production.

---
18
Photons direct on PMTs
- Non-optical photons that interact with the maPMTs may also cause some background.
  - First step: Simulate the rate of these photons incident on the PMTs:
  - Two obvious peaks.
    - Neutron capture with hydrogen in carbon fiber mirrors.
    - e+ e- annihilation
  - Low energy photon rate still dominated by electron production.
e+ e- annihilation (0.51 MeV)
Neutron capture (2.2 MeV)

---
19
Continuing Improvements
- Wavelength shifter for PMTs:
  - Temple is currently coating and testing the clas12 LGCC PMTs with p-Terphenyl.
  - Could increase photoelectron output by 50%.
Coating apparatus
Face plate coating:
Before and after

---
20
Continuing Improvements
- Pattern of photoelectron signal could be recorded (binary signal per pixel) with a MAROC chip.
- Binary output together with pattern recognition (Neural Net?) could provide limited tracking information.
  - Possibly useful for background suppression or better pion rejection.

---
21
Prototyping
- 1st stage (Pre-R&D)
  - maPMT / DAQ testing
  - small Cherenkov tank
  - With electron source → test more realistic PMT response.
  - Ideally with a single aluminized / polished CFRP mirror
- 2nd stage (1st – 2nd year DOE)
  - Construction of 1/6th of total SoLID detector.
    - 5 combined sectors → to be used in final detector.
    - Prototype 1/6th size tank.

---
22
Budget

---
23
Conclusion
- The SoLID LGC is designed to meet the requirements of the SIDIS and PVDIS experimental programs while maximizing inter-component use (minimizing cost).
- Extensive GEMC / Geant4 simulations have been performed testing signal, backgrounds, and pion rejection.
- Continuing efforts to study (and reduce) simulated EM / hadronic backgrounds.
- Wavelength shifting and PMT pixel pattern analysis are being investigated and may lead to even better LGC performance.

---
Backups

---
LGC support and engineering

---
LGC support and engineering

---
LGC support and engineering

---
PMT efficiencies

---
PMT in Magnetic Field