## Slide 1: SoLID DAQ for Transversity and PVDIS
Alexandre Camsonne
SoLID collaboration meeting
November 8th 2014

## Slide 2: Outline
PVDIS
  Calorimeter trigger
  Trigger rates
  Event sizes / data rates
SIDIS
  Electronics layout
  Trigger rates
  Event size / data rates
Costs
Tasks list
Timeline
Conclusion

## Slide 3: PVDIS

## Slide 4: Detector layout and trigger for PVDIS
Trigger
Calorimeter and Gas Cerenkov
200 to 500 KHz of electrons
30 individual sectors
to reduce rate
Max 30 KHz/sector

## Slide 5: FADC readout
FADC readout full waveform 10 samples
Only want to readout FADC channel in the cluster to reduce number of channels readout because of background
CTP generates a 64 bit pattern
Send pattern to TI or FADC directly to trigger FADC
Only channels from pattern are put in buffer

## Slide 6: ECAL trigger

## Slide 7: Calorimeter Geometry
Detector segmented in 30 sectors
One crate per sector
CTP
CTP

## Slide 8: CTP connections
To neighbor CTP
To neighbor CTP

## Slide 9: Neighboring sectors
CTP
CTP
CTP
New CTP : has two additionnal optical links
Can send Cerenkov and calorimeter edges to other sectors.
8 Gbp/s optical link
8 Gbp/s optical link
8 Gbp/s optical link
36 calorimeters
9 Cherenkov
=
150ns + 5 ns per m+ 300 ns ( data ) = 500 ns overhead
=
Trigger decision = 500 ns (Transfer ) + 1us ( clustering ) < 4 us (APV)

## Slide 10: Cerenkov L1 trigger
9 PMTs per sectors
Correct gain per channel
Look for channels above low threshold and coincidence between PMTs ( more than one PMT hit usually )
Sum of all channels with higher threshold
Efficiency need to be studied

## Slide 11: Event size FADC PVDIS with waveform
Detector | Total number of channels | Number of channels firing | Number of samples | Max size detector bytes | Minimal size detector bytes | Typical size
Shower | 58 | 7 | 10 | 2784 | 336 | 772
Preshower | 58 | 7 | 10 | 2784 | 336 | 772
Gas Cerenkov | 9 | 3 | 10 | 432 | 144 | 432
 |  |  | Max total size | 46KB | 0.816KB | 1.544KB
Max rate | Assuming 100 MB/s per crate | One crate |  | 2.1 KHz | 121 KHz | 60 KHz
FADC data rate for 30 KHz = 60 MB/s

## Slide 12: Occupancy

## Slide 13: Occupancy

## Slide 14: Occupancy over 30 sectors
1.522 clusters
In average
1.3 clusters
In average

## Slide 15: GEM event occupancy and size
Sector | Rate | XY | Bytes | 3 samples ( bytes)
0 | 199 | 398 | 184 | 552
1 | 147 | 294 | 96 | 288
2 | 107 | 214 | 80 | 240
3 | 102 | 204 | 72 | 216
4 | 102 | 204 | 72 | 216
Total hits / sector | 657 |  | 432 | 1296
Data rate / sector | 30000 |  | 157680000 | 473040000
Data rate ( sector Mb/s) |  |  | 157,68 | 473.1
Total detector | 19710 |  | 4730.4 | 14191.2
Occupancy detector | 0.14 |  |  | 
Data rate to front end reading 3 samples
Use 4 Gigabit link = 512 MB/s not an issue with SRS

## Slide 16: GEM event occupancy and size
Sector | Rate | XY | Bytes | 3 samples ( bytes)
0 | 23 | 46 | 184 | 552
1 | 12 | 24 | 96 | 288
2 | 10 | 20 | 80 | 240
3 | 9 | 18 | 72 | 216
4 | 9 | 18 | 72 | 216
Total hits / sector | 63 |  | 504 | 1296
Data rate / sector | 30000 |  | 1512000 | 77760000
Data rate ( sector Mb/s) |  |  | 15.12 | 45.36
Total detector | 1620 |  | 453.6 | 1360.8
Occupancy detector | 0.013 |  |  | 
Rates with deconvolution 3 samples readout
Data after processing going to tape

## Slide 17: PVDIS electron trigger
Coincidence ECAL and Gas Cerenkov
Singles ECAL | 290 KHz
Singles rates Cerenkov | 1.9 MHz
Accidental 30 ns | 16.5 KHz
DIS electron | 10 KHz max
Total rate | 27 KHz

## Slide 18: Summary PVDIS
Simulation and trigger were checked and optimized
Max trigger rate estimated to be 27 KHz ( can handle 60 KHz )
GEM data rate assuming 30 KHz around 480 MB/s
GEM data rate after deconvolution around 46 MB/s
FADC data 60 MB/s
Total about 108 MB/s to L3, total 3.24 GB/s
Use L3 to reduce to 250 MB/s ( similar to Hall D ) need to reduce data by a factor of 12

## Slide 19: SIDIS

## Slide 20
65 KHz
120 KHz
7 MHz pions

## Slide 21: Detector layout and trigger for SIDIS
Trigger
Calorimeter
+
Cerenkov
+
MRPC
Coincidences and threshold for global
60 KHz
trigger rates

## Slide 22: SIDIS channel count
Detector | Module type | Number of channels | Number of FADC
Forward Calorimeter | FADC | 1150 x 2 | 144
Large angle calorimeter | FADC | 450 x 2 | 57
Light Gas Cerenkov | FADC | 270 | 8
Heavy Gas Cerenkov | FADC | 480 | 17
Scintillator | FADC | 300 | 8
MRPC | TRB3+Input Register | 3300 | 30

## Slide 23: SIDIS

## Slide 24: SIDIS J/Psi
Read integral and time
Standard zero suppression
J/Psi, look for two clusters instead of one for trigger close to SIDIS trigger
Trigger of a few KHz

## Slide 25: SIDIS: Coincidence @ 30 ns window
Assuming a 30 ns gate
Coincidence rate: 14MHz x 155.5KHz x 30 ns = 65.2 kHz
Total with 4 KHz Physics = 70 KHz
Given the safety margin, expected to handle about 100 KHz.
  Include some single trigger to study detector performance etc.

## Slide 26: MRPC readout
1550 detectors = 3300 channels
Rutgers proposes use GSI TRB3
  10 ps resolution 256 channels around 3.5 K$
  Front end PADIWA amplifier discriminator 200 $ for 16 channels
Development Tsinghua and USTC
VETROC trigger interface board to put signal in L1 trigger ( prototype available )

## Slide 27: GEM event occupancy and size
Sector | Rate | XY | Bytes | 3 samples ( bytes)
0 | 1 | 2 | 8 | 24
1 | 2 | 4 | 16 | 48
2 | 1 | 2 | 8 | 24
3 | 1 | 2 | 8 | 24
4 | 1 | 2 | 8 | 24
5 | 1 | 2 | 8 | 24
Total hits / sector | 7 | 14 | 56 | 1296
Total detector | 210 | 420 | 1680 | 5040
Data rate / sector |  |  | 168000000 | 504000000
Data rate ( sector Mb/s) |  |  | 168 | 504
Occupancy detector | 0.0015 |  |  | 
Using deconvolution gives 168 MB/s for 100 KHz

## Slide 28: FADC data
In 50 ns windows, 11 GeV
Detector | Rate | Hits | Type | Data Size per hit
LC | 120 kHz | 1 | Energy, Hits | 8 Byte x 2 (PS/SH)
FC | 200 MHz | 10 | Energy, Hits | 8 Byte x 2 (PS/SH)
LGC | 40 MHz | 3 | Energy, Hits | 8 Byte x 2 (split)
HGC | 60 MHz | 4 | Energy, Hits | 8 Byte x 2 (split)
MRPC | 850 MHz | 45 | Hits | 4 Byte
SC | 300 MHz | 15 | Energy, Hits | 8 Byte
Total |  |  |  | 2.04kB
204 MB/s at 100 KHz

## Slide 29: Summary SIDIS
Readout only one sample, time and integral for GEM and FADC
70 KHz coincidence rate
Design for 100 KHz gives 368 MB/s to L3 need less than factor 2 reduction
Study feasibility to take all singles ( 150 KHz ) should be doable but need more L3 processing power

## Slide 30: Man power rough estimate
JLAB
Alexandre Camsonne Yi Qiang
Stony Brook
  Krishna Kumar
  Abbey Deshpandes
  Seamus Riordan
 |  | Year 1 | Year 2 | Year 3 | Year 4 | Year 5
1 postdoc |  | Test stand | Test stand | Full electronics | Electronics cabling | Experiment
1 student |  | Test stand | Test stand | Full electronics | Electronics cabling | Experiment
1 tech |  | Rack |  | Rack,cables,weldment | Electronics / detector cabling | 
DAQ |  | Support | Support | Support | Support | 
Designer |  | Layout | Layout |  |  | 
Electronics |  | Trigger | Trigger | Support | Support | Support
Rutgers
  Ron Gilman
  MRPC readout
Tsinghua /USTC
  Yi Wang

## Slide 31: HV and cables
Calorimeter shower | FADC | 1800
Large angle calorimeter preshower | FADC | 114.375
Forward angle calorimeter preshower | FADC | 0
SPD | FADC | 18.75
Light Gas Cerenkov |  | 270
Heavy Gas Cerenkov |  | 480
Total |  | 2714

## Slide 32: HV and cables
 | Total | Needed | Cost
Cables | 2714 | 714 | 27 K$
HV boards | 113 | 30 | 194 K$
HV mainframe | 17 | 5 | 57 K$
 |  | Total | 278 K$
Assume we can reuse 2000 HV channels so need around 714 channels

## Slide 33: Tasks
Hardware
  Trigger design
  Electronics performance testing
  Shielding
  Cabling layout / installation
  L3 / event filtering
Simulation
  Radiation and shielding
  Background in detector event size
  Background in detector event/trigger rates
  Trigger simulation for logic and timing

## Slide 34: DAQ Test stand
Ordered parts / collaboration with Hall A Compton
  2 VXS crates
  4 FADC
  1 CTP, 1SSP
  4 Intel VME CPUs
CODA3 still in the work : test L3 Farm

## Slide 35: Time line
2014
  DVCS : test Intel VME CPU for large amount of data
2015
  Small scale setup for testing : FADC + trigger + APV25
  HCAL Trigger development ( SBS funding accepted )

## Slide 36: Conclusion
SoLID requires high rates low dead time, flexible trigger capability
Rates optimization for SIDIS but push for highest rate depending of GEM chip performances
GEM electronics R&D
Background and trigger rates where checked and close proposal, data rates are sustainable by the DAQ hardware

## Slide 37: Backup slides

## Slide 38: L1 Trigger Diagram
CPU
SSP
SSP
SSP
SSP
SSP
SSP
GTP
SD
SSP
SSP
SSP
SSP
SSP
SSP
TI
VXS Crate
SSP
CPU
FADC
FADC
FADC
FADC
FADC
FADC
CTP
SD
FADC
FADC
FADC
FADC
FADC
FADC
TI
VXS Crate
CPU
TD
TD
SD
TS
VXS Crate
TD
TD
TD
TD
TD
TD
TD
TD
TD
TD
SD
VXS Serial Link
16 bit @ 250 MHz: 4 Gbps
FADC250
12 bit @ 250 MHz, 16 ch
Sums amplitude from all channels
Transfer total energy or hit pattern to CTP
Crate Trigger Processor
Sums energies from FADCs
Transfer total energy or hit pattern to SSP
Fiber Optics
64 bit @ 125 MHz
SSP
CTP

## Slide 39: L1 Trigger Diagram
CPU
SSP
SSP
SSP
SSP
SSP
SSP
GTP
SD
SSP
SSP
SSP
SSP
SSP
SSP
TI
VXS Crate
SSP
CPU
FADC
FADC
FADC
FADC
FADC
FADC
CTP
SD
FADC
FADC
FADC
FADC
FADC
FADC
TI
VXS Crate
CPU
TD
TD
SD
TS
VXS Crate
TD
TD
TD
TD
TD
TD
TD
TD
TD
TD
SD
CTP
TS
Global Trigger Processor
Collect L1 data from SSPs
Calculate trigger equations
Transfer 32 bit trigger pattern to TS
VXS Serial Link
32 bit @ 250 MHz: 8 Gbps
Sub-System Processor
Consolidates multiple crate subsystems
Report total energy or hit pattern to GTP
Copper Ribbon Cable
32 bit @ 250 MHz: 8 Gbps
SSP

## Slide 40
fADC250
CTP Crate Trigger Processor
TI Trigger Interface
SD Signal Distribution
Detector
Signals
VXS Crate
VXS Crate
Trigger Distribution Crate
SSP
GTP
Fiber Optic Link
(~100 m)
(64bits @ 125 MHz)
(8)
(2)
(12)
TD
TS
(1)
TS
VXS Crate
Copper Ribbon Cable
(~1.5 m)
(32bits @ 250 MHz)
Fiber Optic Links
Clock/Trigger
(16bits @ 62.5MHz
Global Trigger Crate
Front-End Crate
VXS Backplane
(16)
(1)
(1)
(1)
(1)
(1)
Trigger Latency ~ 3 μs
( ) – Number in parentheses
refer to number of modules
Custom Designed
Boards at JLAB
Pipelined detector readout electronics:
fADC
Level-1 Trigger Electronics

## Slide 41: Hall staging
10 racks
+ patch panels

## Slide 42: Test run setup
MRPC
  V1290
  JLAB or SIS FADC
GEM / Hadron Blind Detector
  APV25 (UVA)
    SRS readout
    MPD

## Slide 43: SIDIS channel count
Detector | Module type | Number of channels | Number of modules
Forward Calorimeter | FADC+TDC | 2x1150 | 119
Large angle calorimeter | FADC+TDC | 2x450 | 58
Light Gas Cerenkov | FADC+TDC | 270 | 8
Heavy Gas Cerenkov | FADC+TDC | 480 | 17
Scintillator | FADC+TDC | 300 | 8
GEM | VME | 164K | 321

## Slide 44: Hall D L1 Trigger-DAQ Rate
Low luminosity (107 g/s in 8.4 < E < 9.0 GeV)
  20 kHz L1
High luminosity (108 g/s in 8.4 < E < 9.0 GeV)
  200 kHz L1
  Reduced to 20 kHz L3 by online farm
Event size: 15 kB; Rate to disk: 3 GB/s
Detectors which can be used in the Level-1 trigger:
SC
Forward Calorimeter (FCAL) | Energy
Barrel Calorimeter (BCAL) | Energy
Start Counter (SC) | Hits
Time of Flight (TOF) | Hits
Photon Tagger | Hits
Energy FCAL (GeV)
Energy FCAL (GeV)
Energy FCAL (GeV)
Energy BCAL (GeV)
Energy BCAL (GeV)
Energy BCAL (GeV)
Electromagnetic background
Hadronic E < 8 GeV
Hadronic E > 8 GeV
Basic Trigger Requirement:
EBCAL + 4 ∙ EFCAL > 2 GeV
and a hit in Start Counter

## Slide 45: Custom Electronics for JLab
VME Switched Serial (VXS) backplate
  10 Gbps to switch module (J0)
  320 MB/s VME-2eSST (J1/J2)
All payload modules are fully pipelined
  FADC125 (12 bit, 72 ch)
  FADC250 (12 bit, 16 ch)
  F1-TDC (60 ps, 32 ch or 115 ps, 48 ch)
Trigger Related Modules
  Crate Trigger Processor (CTP)
  Sub-System Processor (SSP)
  Global Trigger Processor (GTP)
  Trigger Supervisor (TS)
  Trigger Interface/Distribution(TI/D)
  Signal Distribution (SD)
FADC125
F1-TDC

## Slide 46: L1 Trigger Diagram
CPU
FADC
FADC
FADC
FADC
FADC
FADC
CTP
SD
FADC
FADC
FADC
FADC
FADC
FADC
TI
VXS Crate
TI
CPU
SSP
SSP
SSP
SSP
SSP
SSP
GTP
SD
SSP
SSP
SSP
SSP
SSP
SSP
TI
VXS Crate
SSP
CPU
TD
TD
SD
TS
VXS Crate
TD
TD
TD
TD
TD
TD
TD
TD
TD
TD
SD
Trigger Supervisor
Calculate 8 bit trigger types from 32 bit trigger pattern
Prescale triggers
Transfer trigger and sync signal to TD (16 bit total)
VXS Serial Link
16 bit @ 62.5 MHz: 1 Gbps
Trigger Distribution
Distribute trigger, clock and synchronize signals to TI in each Crate
Fiber Optics
16 bit @ 62.5 MHz: 1 Gbps
GTP

## Slide 47: L1 Trigger Diagram
VME Readout Controller
Gigabit ethernet
CPU
TD
TD
SD
TS
VXS Crate
TD
TD
TD
TD
TD
TD
TD
TD
TD
TD
SD
TD
CPU
SSP
SSP
SSP
SSP
SSP
SSP
GTP
SD
SSP
SSP
SSP
SSP
SSP
SSP
TI
VXS Crate
SSP
CPU
FADC
FADC
FADC
FADC
FADC
FADC
CTP
SD
FADC
FADC
FADC
FADC
FADC
FADC
TI
VXS Crate
Signal Distribution
Distribute common signals to all modules: busy, sync and trigger 1/2
VXS Serial Link
4 bit @ 250 MHz: 1 Gbps
Trigger Interface
Receive trigger, clock and sync signals from TD
Make crate trigger decision
Pass signals to SD
TID

## Slide 48: The GlueX Detector
TOF
time of flight
SC
start counter
2.2T superconducting solenoidal magnet
Fixed target (LH2)
108 tagged g/s (8.4-9.0GeV)
hermetic
2.2 Tesla
Solenoid
Calorimetry
Barrel Calorimeter (lead, fiber sandwich)
Forward Calorimeter (lead-glass blocks)
PID
Time of Flight wall (scintillators)
Start counter
Barrel Calorimeter
Charged particle tracking
Central drift chamber (straw tube)
Forward drift chamber (cathode strip)

## Slide 49: GlueX Data Rate
 | Front End DAQ Rate | Event Size | L1 Trigger Rate | Bandwidth to mass Storage
GlueX | 3 GB/s | 15 kB | 200 kHz | 300 MB/s
CLAS12 | 0.1 GB/s | 20 kB | 10 kHz | 100 MB/s
ALICE | 500 GB/s | 2,500 kB | 200 kHz | 200 MB/s
ATLAS | 113 GB/s | 1,500 kB | 75 kHz | 300 MB/s
CMS | 200 GB/s | 1,000 kB | 100 kHz | 100 MB/s
LHCb | 40 GB/s | 40 kB | 1000 kHz | 100 MB/s
STAR | 50 GB/s | 1,000 kB | 0.6 kHz | 450 MB/s
PHENIX | 0.9 GB/s | ~60 kB | ~ 15 kHz | 450 MB/s
LHC
JLab
BNL
*
CHEP2007 talk
Sylvain Chapelin
private comm.
* Jeff Landgraf Private Comm. 2/11/2010
** CHEP2006 talk MartinL. Purschke
**

## Slide 50: CODA3 – What’s different
CODA 2.5 | CODA 3
Run Control (X, Motif, C++) (rcServer, runcontrol) | Experiment Control – AFECS (pure JAVA) (rcPlatform, rcgui)
Communication/Database (msql, cdev, dptcl, CMLOG) | cMsg – CODA Publish/Subscribe messaging
Event I/O C-based simple API (open/close read/write) | EVIO – JAVA/C++/C APIs Tools for creating data objects, serializing, etc…
Event Builder / ET System / Event Recorder (single build stream) | EMU (Event Management Unit) Parallel/Staged event building
Front-End – vxWorks ROC (Interrupt driven – event by event readout) | Linux ROC, Multithreaded (polling – event blocking)
Triggering: 32 ROC limit, (12 trigger bits -> 16 types) TS required for buffered mode | 128 ROC limit, (32 trigger bits -> 256 types) TI supports TS functionality. Timestamping (4ns)

## Slide 51: FADC Encoding Example

## Slide 52: GTP Trigger Bit Example

## Slide 53: L3 data reduction
Pile up detection
  Only record sample for event with pile up
Calorimeter clustering
GEM readout
  Timing cut
  Clustering
  Crude tracking

## Slide 54
Jefferson Laboratory Pipelined electronics with CODA 3

## Slide 55: Pipelined Hall D DAQ
S
3 us latency
Above
threshold
Electron shower
accidental
accidental

## Slide 56: Pipelined Hall D DAQ
Calorimeter
Light Gas Cerenkov
Heavy Gas Cerenkov
FADC
FADC
FADC
CTP
CTP
CTP
CTP
SSP
GTP
L1 trigger
Calorimeter
+
Cerenkov
+
Pion
In
3 us

## Slide 57: Data readout
L3
Drive
Silo
VME
100 MB/s
Ethernet
100 MB/s
SAS
250 MB/s
DLO6
Tape
250 MB/s
Calo
Cerenkov
Scintillator
GEM
APV
MPD
FADC
CPU
Event
Builder
APV transfer
80 MB/s
VME
100 MB/s
CPU
DAQ bottle necks
CPU

## Slide 58: L3 Farm
ROC
ROC
ROC
ROC
ROC
ROC
ROC
ROC
ROC
Front-End Crates
Read Out Controllers
~60 crates
~50MB/s out per crate
EB1
Event Builder
stage 1
EB1
Event Builder
stage 1
EB1
Event Builder
stage 1
EB2
Event Builder
stage 2
EB2
Event Builder
stage 2
Staged Event Building
blocked event fragments
partially recombined event fragments
N x M array of nodes (exact number to be determined by available hardware at time of purchase)
Level-3 Trigger and monitoring
full events
L3 Farm
node
node
node
node
node
node
node
Raid Disk
ER
Event Recorder
Event Recording
300MB/s in
300MB/s out
All nodes connected with 1GB/s links
Switches connected with 10GB/s fiber optics

## Slide 59: GEM READOUT

## Slide 60: GEM readout
APV25 Front GEM ASICs
Up to 164 000 channels
APV 25 : 128 channels
Readout
  VME based readout : 16 APV25 = 2048 channels
  ( ~ 10 $ / channels )
  SRS readout : ethernet /PC based = 2048 channels ( ~ 3 $ / channels )
1 crate per sectors for FADC and GEM

## Slide 61: APV25 readout
Switch Capacitor Array ASICS with buffer length 192 samples at 40 MHz : 4.8 us Look back 160 samples : 4 us
Estimated occupancy : 220 hits per trigger, X Y data, 440 strips
GEM : 6 Layers 164 000 channels total, 28 000 channels per planes
Occupancy : 1.6 %
APV readout time :
t_APV = 141 x number_of_sample / 40 MHz
t_APV(1 sample) = 3.7 us.
Max rate APV front end :
270 KHz in 1 sample mode
90 KHz in 3 samples mode
Will be triggered at max 60 KHz in 3 samples
100KHz Max in 1 sample
Deadtimeless electronics / parallel read and write

## Slide 62: Other GEM readout chips
APV25 limiting factor
  Need to confirm performance
  Optimize hardware and readout
Chip in development
  CLAS12 Dream CEA/Saclay
  ATLAS VMM1 BNL
  gDSP
  …
SRS readout compatible with other chips
  Ethernet + PC based

## Slide 63: Tape size
 |  | Days | Data rate | Seconds | Total data TB | Double | DLO5 in $ | DLO6 in $
E12-11-108 | Pol proton | 120 | 250 | 10368000 | 2592 | 5184 | 259200 | 155520
E12-12-006 | J/Psi | 60 | 250 | 5184000 | 1296 | 2592 | 129600 | 77760
E12-10-006 | Transv. Pol. 3He | 90 | 250 | 7776000 | 1944 | 3888 | 194400 | 116640
E12-11-007 | Long. Pol. 3 He | 35 | 250 | 3024000 | 756 | 1512 | 75600 | 45360
E12-10-007 | PVDIS | 169 | 250 | 14601600 | 3650.4 | 7300.8 | 365040 | 219024
 | Total | 474 |  | 40953600 | 10238.4 | 20476.8 | 1023840 | 614304