The SoLID EC Working Group
SoLID Collaboration Meeting
November7-8, 2014
Electromagnetic Calorimeters (EC) for SoLID

---
SoLID EC configuration
Provide key e/p separation, modules shared between PVDIS & SIDIS
	q (deg)	z (cm)	R(cm)	P (GeV/c)	Max p/e	Area (m2)
PVDIS FAEC	22 - 35	(320,380)	(110,265)	2.3 - 6	~200	~ 18.3
SIDIS FAEC	7.5 – 14.85	(417,475)	(98,230)	1 - 7	~200	~ 13.6
SIDIS LAEC	16.3 - 24	(-65,-5)	(83,140)	3-6	~20	~ 4.0

---
EC Design Requirements
Electron- hadron separation:
>50:1 p rejection above Cherenkov threshold (~4) to 7GeV/c;
Electron efficiency > 95%;
(energy resolution: )
Provide trigger:
PVDIS: coincidence with CC, suppress background;
Provide shower position to help tracking/suppress background
σ ~ 1 cm
color blue {%sigma (E)/E <10"%"/sqrt{E}}
Radiation resistance: > (4-5)x105 rad
B~1.5 T, high neutron background
Modules easily swapped and rearranged for PVDIS ↔ SIDIS; SIDIS needs 2-fold rotation (180o) symmetry

---
SPD Design Requirements (SIDIS only)
LASPD: Provide primary photon rejection 5:1; combine with RF bunch to provide primary TOF (150ps preferred)
FASPD: Provide photon rej 5:1, secondary to MRPC

---
Material	r / g/cm3	X0 / cm	RM / cm	ll / cm	n / refrac.	t / ns	peak l nm	light yield	Npe /GeV	rad	dE/E
Crystals
NaI(Tl)	3.67	2.59	4.5	41.4	1.85	250	410	1.00	106	102	1.5%/E1/4
CsI	4.53	1.85	3.8	36.5	1.80	30	420	0.05	104	104	2.0%/E1/2
CsI(Tl)	4.53	1.85	3.8	36.5	1.80	1200	550	0.40	106	103	1.5%/E1/2
BGO	7.13	1.12	2.4	22.0	2.20	300	480	0.15	105	103	2%/E1/2
PbWO4	8.28	0.89	2.2	22.4	2.30	15/60%	420	0.013	104	106	2.0%/E1/2
LSO	7.40	1.14	2.3		1.81	40	440	0.7	106	106	1.5%/E1/2
PbF2	7.77	0.93	2.2		1.82	Cher	Cher	0.001	103	106	3.5%/E1/2
Lead glass
TF1	3.86	2.74	4.7		1.65	Cher	Cher	0.001	103	103	5.0%/E1/2
SF-5	4.08	2.54	4.3	21.4	1.73	Cher	Cher	0.001	103	103	5.0%/E1/2
SF-57	5.51	1.54	2.6		1.89	Cher	Cher	0.001	103	103	5.0%/E1/2
Sampling: lead/scintillator
SPACAL	5.0	1.6				5	425	0.3	2x104	106	6.0%/E1/2
Shashlyk	5.0	1.6				5	425	0.3	103	106	10%/E1/2
Shashlyk(K)	2.8	3.5	6.0			5	425	0.3	4x105	105	3.5%/E1/2

---
Choosing EC Type
SoLID radiation level (~400 krad per year) is too high for leadglass and CsI-like crystals (typically 1krad).
Our ECs are large: 6-8m3; use of crystals: PbWO4 ($10/cc) or LSO ($40/cc) is cost prohibitive;
SciFi type needs half volume being scintillating fibers, cost of fiber alone ($4M if 1mm dia, $1/m) exceed total cost of Shashlyk type. Cost of PMT/HV also too high.
Shashlyk: Fairly robust technique, moderate cost, tunable energy resolution, radiation 500krad tested by IHEP
IHEP, COMPASS Shashlik, 2010

---
IHEP Scintillator Facilities
www.ihep.ru/scint/index-e.htm
Polysterene based, injection molding cuts cost drastically, production 200 modules/month possible.

---
Design Consideration 1: Longitudinal
Preshower: 2X0 lead + 20mm scintillator
Preshower+Shower total length: 20X0 (<2% leakage)
Preshower and Shower have the same lateral design, otherwise totally detached

---
Design Consideration 1: Longitudinal
Shower: 100:1 intrinsic pion rejection → 0.5mm Pb/1.5 mm Scint. (BASF143E polysterene) per layer. [4.5-5%/sqrt(E)]
1.00
0.96
0.92
0.88
0.84
0.80
  1/(Pion rejection)
0.030
0.025
0.020
0.015
0.010
0.005
0
   Electron Efficiency
PVDIS 28.5o
SIDIS-FA 12.0o
SIDIS-LA 20.5o
intrinsic

---
Design Consideration 2: Lateral

---
Design Consideration 2: Lateral
PVDIS physics requires the largest incident angle (35o from target center, 37o from downstream target); Calorimeter covers up to ~40o.
1.0
0.8
0.6
0.4
0.2
0.0
P<4GeV
4GeV<P<8GeV
P>8GeV
Physics Need
EC coverage
30 32 34 36 38 40 42 44 46 48 50
electron incident angle (o)
Fractional electron energy deposit
95% contain at 37o

---
Design Consideration 2: Lateral
Hexagon preferred by support design: 100cm2 → 6.25cm side
Al support before Preshower and Shower; May need carbon fiber between Preshower and Shower to minimize effect on PID.

---
Design Consideration 3: Radiation Dose
2X0 lead efficiently block low energy photons
105
104
103
102
10
1
PVDIS, lower γ φ-band
Total
Electron
Photon
proton
p+
p0 → 2g
p-
        1 10 100
layer number
preshower
Radiation dose (rad) per PAC month

---
Design Consideration 3: Radiation Dose
Photon blocker helps
PVDIS, higher γ φ-band
105
104
103
102
10
1
Total
Electron
Photon
proton
p+
p0 → 2g
p-
        1 10 100
layer number
preshower
Radiation dose (rad) per PAC month

---
Design Consideration 3: Radiation Dose
SIDIS: less of an issue
104
103
102
10
1
SIDIS – FAEC
Total
Electron
Photon
proton
p+
p0 → 2g
p-
        1 10 100
layer number
preshower
Radiation dose (rad) per PAC month

---
Design Consideration 3: Radiation Dose
SIDIS: less of an issue
104
103
102
10
1
SIDIS – LAEC
Total
Electron
Photon
proton
p+
p0 → 2g
p-
        1 10 100
layer number
preshower
Radiation dose (rad) per PAC month

---
Design Consideration 4: Fiber Choice
WLS fibers	Kuraray Y11	Saint Gobain BCF91A, BCF92 (faster)
wavelength	~420 → 494nm	~430 → 476nm
1/e length	>3.5m	>3.5m
mechanical property	less bending loss
radiation hardness	13% light loss at 100krad (30% at 700krad)	15% light loss at 100krad (50% at 700krad)
light yield		2-3 times less than Y11
Clear fibers	Kuraray clear-PSM	Saint Gobain BCF98
cost	$$$	$
Will use Y11 for Preshower/FASPD, BCF91A for Shower; Clear fiber yet to be tested.

---
Design Consideration 4: Fiber Choice
Fiber connector options:
Preshower: 4-4 connector
Shower: 100-100 connector
Both can be made in-house using Delrin (as LHCb). Also investigating DDK connectors (Japan, used at Fermilab), sample received.
fiber fusing possible, but switching SIDIS ↔ PVDIS difficult and can't be done locally
Transfer light to outside Solenoid to PMTs (PMT info → later).
128-fiber connector LHCb

---
Performance ― PID, SIDIS LAEC
Background
Black: background, Red: electrons
Black: background, Red: pi-
Scintillator energy dep. in Shower (MeV)
Scintillator energy dep. in Shower (MeV)
Black: background, Red: pi-, blue: e-
Black: background, Red: pi-, blue: e-
Scintillator energy dep. in Shower (MeV)
Scintillator energy dep. in PS (MeV)
Photon Electron Pi- Pi+ Proton
Photon Electron Pi- Pi+ Proton
in Preshower (MeV)
in Preshower (MeV)

---
Performance ― PID, SIDIS
Most inner radius region shown – worse case situation
* Intrinsic
* W/ Background
Forward Calorimeter
1.00
0.95
0.90
0.85
0.80
 p efficiency
electron efficiency
0.04
0.03
0.02
0.01
0
 1 2 3 4 5 6 7 8
 1 2 3 4 5 6 7 8
p (GeV)
Large-Angle Calorimeter
 p efficiency
electron efficiency
1.00
0.95
0.90
0.85
0.80
0.02
0.01
0
2 3 4 5 6 7 8
2 3 4 5 6 7 8

---
Performance ― PID, PVDIS
Background
Black: background, Red: electrons
Black: background, Red: pi-
Scintillator energy dep. in Shower (MeV)
Scintillator energy dep. in Shower (MeV)
Black: background, Red: pi-, blue: e-
Black: background, Red: pi-, blue: e-
Scintillator energy dep. in PS (MeV)
Scintillator energy dep. in Shower (MeV)
Photon Electron Pi- Pi+ Proton
in Preshower (MeV)
in Preshower (MeV)

---
Performance ― PID, PVDIS (low g)
Background worsens PID. Will require full waveform recording if better PID is desired.
  1/(Pion rejection)
   Electron Efficiency
1.00
0.95
0.90
0.85
0.80
0.75
0.07
0.06
0.05
0.04
0.03
0.02
0.01
0.00
2 3 4 5 6
2 3 4 5 6
p (GeV)
2D-cut PID, with latest background embedding
PVDIS: p=2.3~6 GeV

---
Performance ― PID, PVDIS (high g)
Background worsens PID. Will require full waveform recording if better PID is desired.
  1/(Pion rejection)
   Electron Efficiency
1.00
0.95
0.90
0.85
0.80
0.75
0.07
0.06
0.05
0.04
0.03
0.02
0.01
0.0
2 3 4 5 6
2 3 4 5 6
p (GeV)
2D-cut PID, with latest background embedding
PVDIS: p=2.3~6 GeV

---
Performance ― Triggering
SIDIS, large angle, electron trigger
Most inner radius region shown – worse case situation
1.0
0.8
0.6
0.4
0.2
0
electron trigger efficiency
 p trigger efficiency
0.20
0.16
0.12
0.08
0.04
0
   1.5 2 2.5 3 3.5 4 4.5
   1.5 2 2.5 3 3.5 4 4.5
p (GeV)
threshold: 2.6 GeV → 3 GeV momentum

---
Performance ― Triggering SIDIS, forward
most inner radius (5 GeV threshold)
most outer radius (1 GeV threshold)
0.16
0.12
0.08
0.04
0.00
0.6
0.5
0.4
0.3
0.2
0.1
p efficiency in electron trigger
1.0
0.8
0.6
0.4
0.2
0.0
1.00
0.95
0.90
0.85
0.80
0.75
0.70
electron efficiency in electron trigger
   0 1 2 3 4 5 6 7 8
   0 1 2 3 4 5 6 7 8
p (GeV)

---
Performance ― Triggering
SIDIS, forward MIP trigger
Pion trigger: 2-sigma below MIP
0.995
0.990
0.985
0.980
0.975
 p efficiency in MIP trigger
   1 2 3 4 5 6 7 8
p (GeV)

---
Performance ― Triggering
SIDIS, trigger rates (whole EC)

---
Performance ― Triggering
PVDIS, higher photon background region
1.0
0.8
0.6
0.4
0.2
0.0
1.0
0.8
0.6
0.4
0.2
0.0
electron trigger efficiency
 p trigger efficiency
1 2 3 4 5 6
1 2 3 4 5 6
p (GeV)
preserve DIS electron of x>0.35

---
Performance ― Triggering
PVDIS, trigger rates (whole EC)

---
SPD Design for SIDIS

---
SPD Design for SIDIS
Starting point: 5mm LASPD (60 azimuthal) provides 10:1 photon rej; 5mm FASPD (60 azimuthal x 4 radial) provides 5:1;
15
10
5
0
Forward photon rejection
Large-Angle photon rejection
20
15
10
5
0
10 100 1000
1 10 100 1000
N segment
N segment

---
SPD Design for SIDIS
Starting point: 5mm LASPD (60 azimuthal) provides 10:1 photon rej; 5mm FASPD (60 azimuthal x 4 radial) provides 5:1;
Then, check:
feasibility: with x50 preamp, require (20-40)p.e./MIP to keep 1/2MIP at 20mV and anode current below 1/2 of maximum
LASPD timing resolution < 150ps

---
SPD photon yield simulation
3E3 photon/MeV scintillator efficiency as obtained from Preshower data (1/3 of Eljen EJ200 or BC408 and 1/2 of expected polysterene-based material);
Propagate down SPD, use 0.95 reflectivity and add scintillator decay (use BC408);
Assuming 50% light guide efficiency
Good agreement with data for: HRS S2 (300ps), CLAS12TOF (2 sizes, 35ps, 55ps), moderate for CLAS6TOF (120ps).
For SPD, timing resolution dominated by PMT TTS, also affected by TDC channel setting

---
LASPD photon yield simulation
120
 80
 40
0
200
160
120
 80
 40
0 20 40 60 0 20 40 60
distance from inner edge (cm)
LASPD: 15-20 mm thickness needed for both yield and timing, direct light readout required;
FASPD: Too long for direct readout, use WLS fiber embedding, 1cm → 20p.e., 1.3ns timing spread; 2cm → 40 p.e., 1.0ns timing spread.
prototype test to be done to check simulation (LASPD ordered, FASPD still being designed)
effect on photon rejection being studied.
timing resolution (ps)
# p.e.

---
EC & SPD PMT Choice
Guide light to low-B region to be read by PMTs
Shower: 100x f-1mm fibers → f-1in PMT (good area match), Hamamatsu R11102, custom divider with x5 preamp, 5E4 PMT gain;
Preshower: (4)x f-1mm fiber → 16-ch MAPMT, Hamamatsu R11265-100-M16, 2E4 PMT gain limited by anode current (1/10 of max), require x50 preamp;
FASPD: (4)x f-1mm fiber → 16-ch MAPMT, Hamamatsu R11265-100-M16, require half-MIT=20mV, need 1.6E5 PMT gain to combine with the max x50 preamp gain. Anode current 50uA total (1/2 of max).
Working with JLab detector group on PMT base/preamp design

---
LASPD readout by Fine-Mesh PMTs
FMPMT and APD both are field resistant, similar radiation hardness, but APD gain is much lower.
Existing data on FMPMT (INFN, FIU) show
gain drops by 100 at 1.2T, 0 deg, 10-30 at 30 deg. Above a critical angle (45-55 deg) FMPMT is unusable.
timing worsens (30%-100% larger) at 0deg, but nearly independent of field at 30 deg, up to 1.2T.
→ Indicate the use of 55-deg bending light guides.
Will use Hamamatsu R5924-70 FMPMT (2in) due to higher Ianode limit (100uA vs. 10uA), but will test all 3 FMPMTs (under SoR) using a 5-in 5T solenoid in the test lab.
Cost: $3k*60
Eljen light guide design

---
Pre-R&D: preshower prototype testing
Tested: IHEP, CHN#1 (similar yield)
WLS fiber: Y11, BCF91A(55% rel.), BCF92(35% rel.)
wrapping: printer paper, Tyvek 1055B(10% higher), al mylar (17% higher)
Fiber routing: optimized to double fiber, 2.5 turns each
Max output: 71p.e. at WLS fiber end, expect 40 at PMT
To do: test CHN#2; parallel testing UVa/SDU; fiber connector; clear fiber; PID simulation with 40 p.e.

---
Preshower Prototyping and Production
Vendor	polymer base	light yield anthracene	Price for mass production (20mm)
IHEP	polysterene	40% from CERN data	$216k tot + 30%, or $156 each
Chn #1 高能科迪科技有限公司?		40% from UVa data	$100*1800=$180k
Chn#2 中核控制系统工程有限公司	ST401 phenylethene	40%	$100*1800=$180k
Eljen Technology	EJ200 polyvinyltoluene	64%	[$77 (no groove)/$204 (grooved)] *1800; or $212/$418x3
Saint Gobain Crystal	BC408 polyvinyltoluene	64%	$430x2 no groove
? Chinese: subject to 20% transverse (横向) overhead or not?

---
LASPD Prototyping and Production
Vendor	polymer base	light yield % anthracene	Price for mass production (20mm)
IHEP (material only)	polysterene	40% from CERN data	$10k total, 5mm, no light guide, +30%
Chn #1 高能科迪科技有限公司 ?		40% from UVa data	$533*60, $32k tot (1/3 SPD, 2/3 l.g.)
Chn#2 中核控制系统工程有限公司	ST401 phenylethene	40%	$420EA, $25k total, no l.g.(?)
Eljen Technology	EJ200 polyvinyltoluene	64%	$578*60, $35k tot (1/3 SPD, 2/3 l.g.)
Saint Gobain Crystal	BC408 polyvinyltoluene	64%	$1062*60, no groove, no l.g.
? Chinese: subject to 20% transverse (横向) overhead or not?

---
FASPD Prototyping and Production
Vendor	polymer base	light yield % anthracene	Price for mass production (20mm)
IHEP (material only)	polysterene	40% from CERN data	$40k total, 5mm; +30%
Chn #1 高能科迪科技有限公司?		40% from UVa data
Chn#2 中核控制系统工程有限公司?	ST401 phenylethene	40%	($1500)*60=, $90k total
Eljen Technology	EJ200 polyvinyltoluene	64%	$1160*60=$66k tot
Saint Gobain Crystal	BC408 polyvinyltoluene	64%	$1062 EA, no groove, no l.g.
? Chinese: subject to 20% transverse (横向) overhead or not?

---
Shashlyk Production (IHEP)
Mold: $30k x 2 (scintillator), $15k (lead); plus
$1270 per module, see below
Same prototyping and mass production
Not including 30% overhead
Component	Cost per module
Scintillator	$200
Lead	$240
flanges, nuts	$230
assembly	$320
add fiber mirror, testing	$110
Prototyping (8 modules): $55k+30%, plus fiber ($2,961)
Mass production: $2,361k + 30% = $3,069k, plus fiber

---
Shashlyk Production (Alternate)
Component	3 modules	8 modules	1800 modules
scintillator (CHN#1)	$10k	$27k	$1kx1800=$1.8M
lead (Kolgashield)	$7,776	$17k	$488k
paper (Kolgashield)	$1,152	$2.5k	$130k
flanges, nuts, rods	$600	$1.6k	$150x1800=$270k
fiber mirror, testing	?
Total w/o assembly	$19.5k	$48.1k	$2,688k
CHN: only #1 can do injection molding

---
Cost Estimation
based on 1800 modules, IHEP cost includes 30% overhead
$100k
$180k

---
To Do
Preshower: CHN#1 prototype, SDU/UVa parallel testing;
LASPD: Test Eljen prototype with both R9779 and FMPMT;
FASPD: same as LASPD, with fiber embedding;
Fiber connector test, DDK custom design;
Shower: look for prototype funding, engineering support.
Simulation PID: Preshower with 30-40 p.e.
Simulation SPD: photon rejection at 10-20mm
Support structure design (ANL/P.R.)

---
Backup

---
Forward

---
Preshower light collection simulation
Simulation by Kai Jin: Dependence on # of turns agree with data; absolute efficiency seems to be reasonable
Previously assumed SPD light yield to be 1/4 of Preshower (scale by thickness), but light collection efficiency only depend on fiber routing and # of turns → yield for SPD will be (1/4)*(1/2) of Preshower if using 3 turns of fiber and same groove density → readout needs careful study.
3mm and 5mm hexagons ordered (SDU) for testing SPD light collection

---
Design Consideration 1: Pb/scintillator ratio
Experiment	COMPASS	PANDA	KOPIO
Pb Thick/Layer (mm)	0.8	0.3	0.28
Sci Thick/Layer (mm)	1.5	1.5	1.5
Energy Res. a/sqrt(E)	6.5%	~3%	~3%
Rad. length, X0 (mm)	17.5	34	35
Total rad length in X0	22.5	20	16
Moliere radius (mm)	36	59	60
Typical Detecting Energy	101~102GeV?	<10GeV	<1GeV
Lateral Size (cm)	~4x4	11x11	11x11
Active depth(cm)	400	680	555
Thinner Pb layers give better energy resolution, but requires more layers → Balancing between energy resolution and module length

---
Design Consideration 1.1: Pb/scintillator ratio
Minimize scintillator ratio while reaching 100:1 intrinsic pion rejection → 0.5mm Pb/1.5 mm Scint. (BASF143E) per layer. [4.5-5%/sqrt(E)]
1.00
0.96
0.92
0.88
0.84
0.80
  1/(Pion rejection)
   Electron Efficiency
0.030
0.025
0.020
0.015
0.010
0.005
0
PVDIS 28.5o
SIDIS-FA 12.0o
SIDIS-LA 20.5o
intrinsic
 1 2 3 4 5 6 7 8
1 2 3 4 5 6 7 8
p (GeV)

---
Design Consideration 1.3: Total Length
0.98
0.978
0.976
0.974
0.972
Electron Efficiency
Reach Best rejection at ~20X0
intrinsic
10 15 20 25 30
0.06
0.05
0.04
0.03
0.02
Total Rad Length
1/(Pion rejection)
10 15 20 25 30
Can not contain EM shower
More hadron shower

---
Design Consideration 1.4: Preshower Thickness
1.0
0.9
0.8
0.7
0.6
0.5
0.4
0.3
0.2
0.1
0.0
2X0 Pb efficiently reject pions and add to radiation hardness
Electron Efficiency
Pion Efficiency
1 1.5 2 2.5 3 3.5 4 4.5 5
Preshower lead thickness in X0

---
Design Consideration 2: Lateral
4.0
3.5
3.0
2.5
2.0
1.5
1.0
0.5
0.0
w/ 50ns ADC gate
Background (%)
Resolution(cm)
module
+readout
cost ($M)
0 25 100 225 400 625
block size (cm2)
Good Balance

---
Understanding Preshower light collection
Typical scintillator efficiency: (10-15)% (google search), 2-3eV/photon → 5E7 photons/(GeV of energy deposit)
light collection/absorption of WLS fiber from Kai's simulation: 0.02 for 4 turns, f1mm, f9cm-groove (200ppm) fiber, printer paper wrapping → 1E6 photos/GeV
QE of Y11 dye: unknown, assume to be 100%
WLS fiber trapping of emitted light: 3% for single-clad, 5% for multi-clad → 5E4 photons/GeV
PMT QE: assume 20% → 1E4 photons/GeV
WLS fiber attenuation: 3m gives 0.651 (if decay length 3.5m) or 0.472 (2.0m) → (5-6.5)E3 photons/GeV → (20-26) p.e. for MIP response of 20-mm thick Preshower hexagon (4MeV deposit), consistent with the observed 20-ish p.e. in the lab.