## Slide 1: SoLID DAQ update
Alexandre Camsonne
January 12th 2016
SoLID collaboration meeting

## Slide 2: Recommendations 2c
The plans for the High Level Trigger and the needs for slow control need to be worked out in detail and the implications for resources need to be evaluated.
The implications of the need for these resources in the context of availability of resources at the laboratory need to be understood.
Closer communication with the other JLab experiments and the JLab computing center is strongly encouraged.
Having a functional simulation and reconstruction routines as soon as possible should be a high priority in the software effort. Such software will pay off many times over in experimental design and avoiding pitfalls.

## Slide 3: DAQ observations

## Slide 4: Dead time correction PVDIS 1b.2 ( no major progress since last meeting)
Test with small scale setup
Simulation
Discuss with DAQ group for particular features needed
  Example : helicity gated deadtimes
Rework CDR to add parity specific electronics
Need to write a separate document about DAQ requirements for DAQ group, Electronics group and potential collaborators on electronics (Saclay)

## Slide 5: L3 trigger 2c1
Test on small scale L1 trigger
L3 farm : collaborate with Hall D, try to test simulated data on their setup
Need simulated digitized data and tracking algorithm to test online
Need to figure out funding
Progress : DAQ group advised to first test on simulated data the L3 farm algorithm
  Need digitized background simulation data
  Need algorithm to do analysis

## Slide 6: Ressources 2c2
Computing ressources needed for L3
Tape SILO needs, network
Manpower

## Slide 7: L3 trigger 2c2
Test on small scale L1 trigger
L3 farm : collaborate with Hall D, try to test simulated data on their setup
Need to figure out funding

## Slide 8: Forgotten recommendation
Bunker design
  Radiation
  Cooling of bunker to be evaluated / design

## Slide 9: Hardware
FADC availables
VXS crates and Intel CPU
GTP borrowed
VETROC available
R&D need
  Individual FADC reading
  Trigger setup
  Deadtime measurement for PVDIS
  ( High resolution TDC )

## Slide 10: FADC new VTP design
New CTP for Hall B
Allow readout FADC in parallel : 16 times faster
FADC readout is not a bottle neck : max rate with 8 Gbps link assuming 20 samples
Can read all channels 64 channels per sector and reduce on VTP : clustering
2 additionnal optical links for trigger for triggering neighboring sector
First prototype in about 1 month

## Slide 11: Cerenkov PMT readout
MAROC3 close to what we need
  64 channels
  Variable gain
  Discriminated fast logic signal
  Missing : analog sum of 8, need sum of 64
  8 sum of 8 available just need to sum them, will check with INFN for modified RICH board, requested 10 K$ preRD money
  Radiation hardness is pretty good, need to be tested, possibility of new version to handle Single Event Upset
  MAROC default option
  Will check design with electronics group for FADC analog output
Possible readout schemes
  FADC only ( default )
  FADC + VETROC
  VETROC only : needs to be evaluated
  Preferred : Add TDC readout for each Cerenkov channel 232 VETROC additionnal 700 K$, could improve Cerenkov trigger

## Slide 12: MRPC
Expected timing resolution 80 to 50 ps
Default readout
  NINO + VETROC : 20 ps timing resolution
R&D MRPC : 20 ps
  Sampling TDC ASICs : PSEC4/5, SAMPIC, DRS4 give 5 to 1 ps resolution
  TDC ASIC SBIR : 2ps LSB
Need to determine effect of background
More details in TOF talk, would go for sampling electronics though add deadtime and event size

## Slide 14: GEM readout
VMM3
  Peaking time 25 to 200 ns
  6 bit ADC 25 ns
  10 bit ADC and time 200 ns : 38 bit
  200 MHz readout
  Digital readout
Promising option though no multiple samples, or low resolution ADC might be an issue with background
Test board available after ATLAS testing ( 1 to 2 years)
Requested 10 K$ preRD for evaluation board

## Slide 15: DREAM CLAS12
Pro
  Close to APV25
  Longueur pipeline 12.8 us
  Or64 channel trigger
Cons
  Designed for low trigger rate
  No zero suppression
Proposal for 1 MHz chip development : US funding might help

## Slide 16: Tape costs
 |  | Days | Data rate | Seconds | Total data TB | Double | DLO5 in $ | DLO6 in $
E12-11-108 | Pol proton | 120 | 250 | 10368000 | 2592 | 5184 | 259200 | 155520
E12-12-006 | J/Psi | 60 | 250 | 5184000 | 1296 | 2592 | 129600 | 77760
E12-10-006 | Transv. Pol. 3He | 90 | 250 | 7776000 | 1944 | 3888 | 194400 | 116640
E12-11-007 | Long. Pol. 3 He | 35 | 250 | 3024000 | 756 | 1512 | 75600 | 45360
E12-10-007 | PVDIS | 169 | 250 | 14601600 | 3650.4 | 7300.8 | 365040 | 219024
 | Total | 474 |  | 40953600 | 10238.4 | 20476.8 | 1023840 | 614304
Actual days | Actual years |  | Time in s |  |  | Per year | 394200 | 236520
948 | 2.60 | 474 | 40953600 |  |  |  |  | 
650 K$ total tape cost, if double 1.3 M$ total tape cost
( might be cheaper with improved technology )
500 MB/s should be ok for hard drives, need estimate network upgrade ( less than 100 K$ since fiber are already being pulled , to be confirmed )

## Slide 17: Total PreRD
Cost estimation |  |  | 
FADC 250 | 4500 | 4 | 18000
Cables |  |  | 0
V1290 | 11000 | 0 | 0
VME64X | 11000 | 0 | 0
VETROC | 4500 | 2 | 9000
TD | 3000 | 1 | 3000
CTP | 7000 | 1 | 7000
SSP | 5000 | 1 | 5000
GTP | 5000 | 1 | 5000
TS | 3500 | 1 | 3500
TID | 3000 | 3 | 9000
SD | 2500 | 3 | 7500
FADC trigger Dist | 4000 | 3 | 12000
VXS crate | 15000 | 3 | 45000
VME CPU | 4500 | 4 | 18000
Optical fiber | 100 | 20 | 2000
SRS computers | 3000 | 1 | 3000
MPD | 4500 | 1 | 4500
L3 farm node | 5000 | 1 | 5000
Network router | 10000 | 1 | 10000
 | Total | 49 | 151500

## Slide 18: Pre RD hardware : detector test stand
FADC 250 | 4500 | 4 | 18000
VETROC | 4500 | 2 | 9000
TD | 3000 | 1 | 3000
CTP | 7000 | 1 | 7000
SSP | 5000 | 1 | 5000
TID | 3000 | 1 | 3000
SD | 2500 | 1 | 2500
FADC trigger Dist | 4000 | 1 | 4000
VXS crate | 15000 | 1 | 15000
VME CPU | 4500 | 1 | 4500
Optical fiber | 100 | 20 | 2000
Computer | 3000 | 1 | 3000
MPD | 4500 | 1 | 4500
Network router | 10000 | 1 | 10000
Total |  |  | 72500
Added additionnal 10 K$ for MAROC and 15 K$ for VMM3 : total 97 K$

## Slide 19: Manpower
JLAB :
  Alexandre Camsonne
  Robert Michaels ( Compton development )
  Steve Wood
  Electronics group
  DAQ group
Stony Brook
  Seamus Riordan
  Krishna Kumar
  Postdoc
  Student
UVA : Danning Di GEM readout ( SBS / Tritium )
Need to make detailed manpower and task schedule for R&D and experiment

## Slide 20: Simulations needs
  GEM occupancies and digitization SIDIS for event size, occupancy (Ole, Zhiwen, Duke )
  Updated trigger rates PVDIS, SIDIS(Zhiwen, Rakitah)
  FADC digitization PVDIS : realistic PID (Zhiwen, Yuxiao?)
  Cerenkov simulation only timing readout no FADC(Zhiwen?)
Effect 1 sample vs 3 samples GEM and 20 samples vs time integral SIDIS
Full FADC trigger simulation SIDIS

## Slide 21: Timeline before next collaboration meeting (September 2015)
Summer SBS projects
  GTP : calorimeter
  VETROC : used by Compton
  FADC : FADC counting DAQ deployment and HCAL trigger
  L3 farm test will Hall D and DAQ group
  GEM : MPD test
Development :
  Deadtime mesurement
  FADC readout and trigger serialization ( could be used by other experiments NPS, SBS )

## Slide 22: Pre R&D manpower
Test trigger rate capability ( 3 months + 1 JLAB )
Test full triggering schemes ( implementation 3month / test 6 month + 1 person JLAB)
GEM APV rate capability ( 3 months +1 person (UVA+Stony Brook)
MRPC : high resolution timing ( 6 month + 1 JLAB )
L3 : performance tests and data reduction ( 1 year / 1 student or postdoc and JLAB staff)
  Implementation of L3 farm
  Need simulated data ( software ) (Ole, Zhiwen, Duke )
  Reconstruction algorithm to test ( software )
Can be covered by operation funds DAQ and electronics
Could use addition student for training

## Slide 23: SBS update
Trigger test HCAL : 16 FADC + GTP
  Trigger test completion in about 2 months
GEM MPD :
  5 MPDs
  First iteration of CODA library
  Implementation optical link readout ( 2 months )
SRS : PRAD this year

## Slide 24: Timeline before next collaboration meeting
SBS projects
  GTP calorimeter trigger test
  GEM : preliminary performance
DAQ document

## Slide 25: Document update
Add parity specific requirements ?
  Deadtime
  Helicity
  BPM/charge measurement
  Pion trigger
Address comment :
  L3 farm performance and cost
New Hardware
New GEM chip
Tape price
Network upgrade
Give total price with dependencies and project price
Steve started editing

## Slide 26: Conclusion
Progress from SBS on calorimeter trigger and GEM
Need digitized data for
  SIDIS GEM occupancies
  L3 Farm evaluation
  Trigger rates and efficiencies
MAROC default option for Cerenkov readout
Request for PreRD fund
Start work on document update