## Slide 1: SoLID DAQ update
Alexandre Camsonne
May 6th 2016
SoLID collaboration meeting

## Slide 2: Overview
Document
Updated trigger artes
New FADC readout
PVDIS deadtime
Cerenkov readout
TOF readout options
Simulations needs
L3 farm

## Slide 3: Hardware
FADC availables
VXS crates and Intel CPU
GTP borrowed
VETROC available
R&D need
  Individual FADC reading
  Trigger setup
  Deadtime measurement for PVDIS
  ( High resolution TDC )

## Slide 4: DAQ document summary
Add parity specific requirements ?
  Deadtime
  Helicity
  BPM/charge measurement
  Pion trigger
Address comment :
  L3 farm performance and cost
Integrate new FADC fast readout
TOF electronics options
New GEM chip option
Tape price
Network upgrade
Give total price with dependencies and project price
Steve Wood summarizing preCDR and develop in contact with electronics and DAQ group

## Slide 5: PVDIS electron trigger
Coincidence ECAL and Gas Cerenkov
Singles ECAL | 290 KHz
Singles rates Cerenkov | 1.9 MHz
Accidental 30 ns | 16.5 KHz
DIS electron | 10 KHz max
Total rate | 27 KHz

## Slide 6: Updated PVDIS electron trigger
Coincidence ECAL and Gas Cerenkov
Singles ECAL | 170 KHz
Singles rates Cerenkov | 1.9 MHz
Accidental 30 ns | 9.7 KHz
DIS electron | 10 KHz max
Total rate | 20 KHz

## Slide 7: Calorimeter FADC readout
New readout scheme through VTP
  VME backplane 100 MB/s
  VXS 16x500 MB/s
Can transfer a full ADC ( 16 channels * 20 samples =1.3 KB) up to 390 KHz, transfer is not a bottle neck any more
GEM is limiting factor

## Slide 8: Deadtime measuremt
Can deadtime affect PVDIS asymmetry ?
Test stand Compton FADC
Helicity gated scalers
TI firmware modification
Generate assymmetry same order of PVDIS
Add random background
Check asymmetry value
Target date August

## Slide 9: Cerenkov PMT readout
MAROC3 close to what we need
  64 channels
  Variable gain
  Discriminated fast logic signal
  Missing : analog sum of 8, need sum of 64
  8 sum of 8 available just need to sum them, will check with INFN for modified RICH board, requested 10 K$ preRD money
  Radiation hardness is pretty good, need to be tested, possibility of new version to handle Single Event Upset
  MAROC default option
  MAROC testboard available
  Will check design with electronics group for FADC analog output
Possible readout schemes
  FADC only ( default )
  FADC + VETROC
  VETROC only : needs to be evaluated
  Preferred : Add TDC readout for each Cerenkov channel 232 VETROC additionnal 700 K$, could improve Cerenkov trigger
  Need simulation to evaluate options
  Need to follow with electronics group to start testing ( anyone from Cernkov group interested ? )

## Slide 10: TOF options
Expected timing resolution 80 to 50 ps
Default readout
  NINO + TDC : 20 ps timing resolution
R&D MRPC : 20 ps
  Sampling TDC ASICs : PSEC4/5, SAMPIC, DRS4 give 5 to 1 ps resolution
  Need new chip DRS5 or PSEC5 to handle SoLID trigger rate ( analog pipeline ) ( might develop for EIC )
Depends on final detector choice
Need to determine effect of photon background, might need sampling to deal with pile up

## Slide 11: GEM readout
SRS deployed in Hall B Prad
MPD implemented in CODA
  BLT testing few KHz
  Optical fiber readout to be implemented for high rate test
Preliminary results from Weizhi : one sample no deconvolution not sufficient
High priority to one sample + on chip deconvolution ( implemented in MPD ) will test this summer

## Slide 12: Pre RD hardware : detector test stand
FADC 250 | 4500 | 4 | 18000
VETROC | 4500 | 2 | 9000
TD | 3000 | 1 | 3000
CTP | 7000 | 1 | 7000
SSP | 5000 | 1 | 5000
TID | 3000 | 1 | 3000
SD | 2500 | 1 | 2500
FADC trigger Dist | 4000 | 1 | 4000
VXS crate | 15000 | 1 | 15000
VME CPU | 4500 | 1 | 4500
Optical fiber | 100 | 20 | 2000
Computer | 3000 | 1 | 3000
MPD | 4500 | 1 | 4500
Network router | 10000 | 1 | 10000
Total |  |  | 72500
Added additionnal 10 K$ for MAROC and 15 K$ for VMM3 : total 97 K$

## Slide 13: Manpower
JLAB :
  Alexandre Camsonne
  Robert Michaels ( Compton development )
  Steve Wood
  Electronics group
  DAQ group
Stony Brook
  Seamus Riordan
  Krishna Kumar
  Postdoc
  Student
UVA : Danning Di GEM readout ( SBS / Tritium )

## Slide 14: Simulations needs
  GEM occupancies and digitization SIDIS for event size, occupancy and tracking (Ole, Zhiwen, Weizhi Duke )
  Updated trigger rates PVDIS, SIDIS(Zhiwen, Rakitah)
  FADC digitization PVDIS : realistic PID (?)
  Cerenkov simulation only timing readout no FADC(?)
Effect 1 sample vs 3 samples GEM (Weizhi ) and 20 samples vs time integral SIDIS (?)
Full FADC trigger simulation
MRPC simulation : response to background

## Slide 15: L3 farm
Have digitized data for GEM for SIDIS and PVDIS
Weizhi has tracking algorithm
Need :
  Other detector data
  Additionnal reduction algorithm
  Implement tracking
  Test on Hall D or DAQ cluster

## Slide 16: PreRD tasks
Ecal trigger | 3
GEM performance | 3
FADC performance | 3
Deadtime for PVDIS | 3
Data reduction algorithm implentation | 6
L3 farm need evaluation | 3
Cerenkov readout | 3
Test stand - beam test | 6
PVDIS trigger prototype | 3
SIDIS trigger prototype | 3

## Slide 17: Beam test
11 GeV beam available
  Test detectors :
    GEM
    Calorimeter
    MRPC
    Cerenkov
  Background measurements
Some hardware available :
  FADCs, MAROC

## Slide 18: Hardware
Trigger test HCAL : 16 FADC + GTP
  Trigger test completion in about 2 months
GEM :
  5 MPDs
  First iteration of CODA library
  Implementation optical link readout ( 2 months )
  SRS : PRAD this year

## Slide 19: Timeline before next collaboration meeting and director review
SBS projects
  GTP/VTP calorimeter trigger test
  GEM : preliminary performance
DAQ document
PVDIS deadtime systematic using Compton test stand, implement simulation if enough time
L3 first implementation results

## Slide 20: Conclusion
Still need simulation data for
  Reevaluate with new background
  L3 Farm evaluation
  Trigger rates and efficiencies
  TOF background
  Ocuppancies and event size
MAROC default option for Cerenkov readout
PreRD task to be done before directors review
Start work on document update