## Slide 1: Time-of-flight with LAPPD MCP-PMTs & MRPC
Junqi Xie, Mickey Chiu
on behalf of Detector R&D group
Argonne National Laboratory
Brookhaven National Laboratory
SoLID Collaboration Meeting, May 6-7, 2016

## Slide 2: Glad to join SoLID collaboration to contribute
Junqi Xie
Assistant Physicist
Detector R&D group
Argonne National Laboratory
Mickey Chiu
Physicist
Director of Operations, PHENIX
Brookhaven National Laboratory
We are also collaborating in particle identification detectors for sPHENIX and EIC

## Slide 3
Goal(s):
- Initial plan is to have MRPC <100 ps for pion identification up to 2.5 GeV/c
- Above 2.5 GeV/c Heavy Gas Cherenkov for pion identification
- Kaon identification more demanding requirements:
better separation and higher in momentum
requires <30 ps resolution with the SoLID SIDIS environment
- Tsinghua U: upgrade/improved hardware could make MRPC intrinsic to <20 ps
need readout system upgrade
Expanding collaboration effort
- Joint effort with EIC R&D project, Micky Chiu joined SoLID
EIC R&D achieved <20 ps on bench test, lab test now
options for readout system
- Option with (LA)PPD detector R&D, Junqi Xie joined SoLID
See Junqi’s talk for details
Time-Of-Flight Detectors
J.P. Chen’s slide

## Slide 4: Option 1: MCP-PMTs
Micro-channel plate (MCP) replacing traditional
dynode
Thin plate with micro pores (pore size < 30 μm, thickness ~ 5 mm)
Each pore behaves like an electron multiplier
E field

## Slide 5: Large Area Picosecond PhotoDetector (LAPPD)
The LAPPD project reinvents photodetectors using transformational technologies.
Goals: low-cost, large-area (20 cm x 20 cm), picosecond-timing
Applications: picosecond timing, millimeter spatial resolution on large-area
High energy physics: optical TPC, TOF, RICH
Medical imaging: PET scanner, X-ray imaging devices
National security: Detection of neutron and radioactive materials

## Slide 6: Tube production
11 tubes are produced Jun. – Dec. 2015
Assembling a pre-baking chamber to produce 1 tube/week
Glass LTA
MCP & Resistive Grid Spacer Stack
Completed Tube

## Slide 7: Key performances
18%
goal 20%
Spectra response
Signals / frequency components
0.5 ns
rise time
Signal bandwidth
up to1.3 GHz

## Slide 8: Key performances
Gain
108
107
106
Gain as high as 7X107
Time resolution overall ~35 ps, TTS <20 ps
Laser start time jitter: laser ~30ps
Rate capability: > 75KHz/cm2/s
30 ps
100 ps
50 ps
Overall time resolution
Rate capability
75KHz/cm2/s

## Slide 9: Future development path
Small-scale adoption
in various experiments
Today
Feedback
from users helps to improve
the design
TARDIS
SoLID, sPHENIX, EIC
Optimization in geometry for fast timing, magnetic field immunity
Pad readout
Background testing at JLab for Solid
……
Notes: Cryogenic user? Have a plan.

## Slide 10: Option 2: Multi Gas Gap Resistive Plate Chamber (MRPC)
Invented in 1996, Crispin Williams et al, CERN → New generation of TOF detector
Cost effective compared to scintillator + PMT based TOF
Easy to build a large area detector
Free from the magnetic field effect
Working, ~ 80 ps time resol. : ALICE, STAR, PHENIX, FOPI
Achieved for high rates (20 kHz/cm2), ~80 ps time resol: CBM
Aiming for 10 ps time resol. : EIC
Aiming for 10 ps AND high rates? : SOLID
Floating resistive plates in between electrodes
Space charge limits avalanche growth to be below streamer transition
Recombination cuts ionic charge residual in the gas gap
Differential readout reduces noise and is helpful to obtain good time resolution.
130 mm
active area 70 mm
Essential Concepts
Notes: Basic slide on mRPC.

## Slide 11: Improving Resolution Down to 10 ps?
 | MRPC ( C. Williams et al. ) | MRPC ( UIUC & BNL)
Gas Gap Width | 160um (fishing line) | 105um (diameter of fishing line)
# of Gas Gaps | 4 stack x 6 gas gaps = 24 | 4 stack x 9 gas gaps = 36
# of thin glass layers | 4 stacks x 5 layers = 20 (250um thick glass) | 4 stack x 8 layers = 32 (210um thick glass)
Preamplifier | Differential type, NINO chip (3GHz bandwidth) | LMH6554 2.8-GHz + Evaluation Board
TDC and DAQ | Oscilloscope (Sampling speed of 10Gs) | DRS4-V5(5Gs) + PC
Time resolution | 30 ps with cosmic ray/ 16 ps at T10 beam test CERN | Cosmic ray test / Beam halo test at COMPASS
Crispin Williams et al, NIMA 594 (2008) 39– 43
Gas gap width : 160um
BNL&UIUC Prototype, eRD14, 2015
Gas gap width : 105um
PCB
Glass
Gas gap
Narrower gap width → fast charge dominant in the induced signal → Better timing resolution
Efficiency recovered by adding more gas gaps (as well as more signal)
Notes: Main points are that making more gaps and thinner gaps will improve the timing resolution. We compare here to the mRPC built by C. Williams (parameters are on the left), and to that built by us for eRD14. Main differences are that we use 105 um gaps (vs 160), and we also have 36 gaps vs 24.

## Slide 12: eRD14 Glass MRPCs
MRPC1
MRPC2
Differential Preamp.
TI, LMH 6881
2.8GHz bandwidth
28 v/v
Waveform
Analyzer
(DRS4-V5)
5GHz sampling
speed
Gas chamber in the cosmic ray test stand at UIUC
Gas Input & Output
HV : 20kV ( +11kV, -11kV)
Notes: Here is a picture of our setup, including our test readout system (TI differential preamp and DRS4 eval board). Major work would need to be done in making a custom readout for any experiment, such as SOLID (also the same case for MCP-PMTs).

## Slide 13: eRD14 mRPC: Efficiency and Time Resolution
25.4ps / √2
~ 18ps
Cosmic rays
22kV
[ns]
[ns]
MRPC1- MRPC2
MRPC1- MRPC2
Cosmic rays
22kV
Efficiency
Preamp : NINO, 10 GHz, Oscilloscope
C. Williams
CERN, 2010
Notes: Our efficiency, correlation plot, and time resolution plot (starting from upper left). Lower right is the published result from Crispin Williams, so you can compare his ~20 ps with our ~18 ps.

## Slide 14: Use different material than glass (eg Mylar)?
Glass mRPC
Mylar mRPC
One way to improve fast signal is to bring signal closer to pickup strips, or have more gaps
Thinner glass gets very expensive (and starts to become flexible)
    Use Mylar instead? Can then replace 210 um glass with 125 um Mylar
  However, rate capability should be bad? Mylar has much higher volume resistivities, 1019 Ω-cm2
Possible major technical challenge: create flat mylar layer separated from next by ~100 um (solved?)
48 gas gaps!
Notes: Here I argue why going to Mylar replacing glass should produce a better performing mRPC… The basic idea is that using thinner material such as mylar, you can make the signals closer to the pickup cathodes, or you can create more gas gaps which creates more signal. The mylar we created for the FNAL beam test had 48 gas gaps, compared to 36 for the eRD14 glass one, and 24 for the one built by Crispin Williams.

## Slide 15: Summary
The Argonne MCP photodetector program has been highly successful, benefiting from advances in different disciplines.
The success of the photodetector program brings in lots of interests from many areas of science: TOF at collider, HEP neutrino experiments, medical imaging, nuclear physics experiments, national security…
Sent out devices to early users for evaluation and incorporation to experiments.
Progress has been made on MRPC for <20ps timing resolution.
Different material other than glass is planned for even faster MRPC design.
Thanks for your attention!

## Slide 16: Backup Slides

## Slide 17
2 stacks, 10 gas gaps, 0.3mm gas gap width
(No need to wire fishing lines)
First Signals from the 3D Printed MRPCs
Signals captured at COMPASS hall
Not enough time to setup 3D MRPC properly for data taking before the COMPSS beam was end
Expected the first time resolution results in the beam test at Fermilab 2016!
Two 3D printed gas gap MRPC assembled
Signals
Trigger bias

## Slide 18: Stacking Glass with Fishing Line
105um diameter of fishing line
Stacking glass plates and fishing lines
4 stacks : 36 gas gaps
Uniform gas gaps
Between glass plates