## Slide 1
High time resolution TOF for SoLID
Outline:
  Conceptual design of SoLID-TOF
  Performance and aging
  Structure of narrow-gap MRPC
Cosmic and beam test
Conclusions
  Wang Yi
Department of Engineering Physics, Tsinghua University

## Slide 2
Motivation
JLab 6 GeV: precision measurements
high luminosity (1039) but small acceptance (HRS/HMS: < 10 msr)
or large acceptance but low luminosity (CLAS6: 1034)
JLab 12 GeV upgrade opens up a window of opportunities (DIS, SIDIS, Deep Exclusive Processes) to study valence quark (3-d) structure of the nucleon and other high impact physics (PVDIS, J/y, …)
High precision in multi-dimension or rare processes requires very high statistics  large acceptance and high luminosity
CLAS12: luminosity upgrade (one order of magnitude) to 1035
To fully exploit the potential of 12 GeV, taking advantage of the latest technical (detectors, DAQ, simulations, …) development
SoLID: large acceptance detector can handle 1037 luminosity (no baffles)
1039 with baffles

## Slide 3
Overview of SoLID
Full exploitation of JLab 12 GeV Upgrade
 A Large Acceptance Detector AND Can Handle High Luminosity (1037-1039)
Take advantage of latest development in detectors , data acquisitions and simulations
Reach ultimate precision for SIDIS (TMDs), PVDIS in high-x region and threshold J/y
5 highly rated experiments approved (+3)
Three SIDIS experiments, one PVDIS, one J/y production (+ three run group experiments)
Strong collaboration (250+ collaborators from 70+ institutes, 13 countries)
Significant international contributions (Chinese collaboration)
Solenoidal Large Intensity Device

## Slide 4
Main requirements for TOF
The MRPC is developed for the TOF of SoLID
Main Requirements for TOF:
  /k separation up to 2.5GeV/c
  Time resolution < 100ps
  Rate capability > 10kHz/cm²
To separate very few K from , we require the TOF time resolution as good as possible.
We have to improve the time resolution to about 20ps.

## Slide 5
Conceptual design of SOLID-TOF
MRPC TOF wall we designed contain 150 MRPC modules in total, with 50 gas boxes and 3 counters in each box, covering the area of 10m².
MRPC1
MRPC2
MRPC3
100cm
16cmm
28cm
Total channel ~3600

## Slide 6
6
Introduction of MRPC
Application in nuclear physics experiments
Application in industry（Muon tomography)
Application in medicine（TOF-PET）
6
Standard parameters:
Resistivity of glass: ~1012 Ω.cm
Time resolution <100ps
Efficiency >95%
Dark current: a few nA
Noise <1Hz/cm2
MRPC is made of thin
glass, large area and cheap
The inner glasses are
floating, take and keep
correct voltage by
electrostatics. it is
transparent to fast signals
Thin gap->good timing
Multi-gap-> high efficiency
Read out
Read out
Insulator
Carbon
Insulator
Resistive plate

## Slide 7
7
Dimension Bulk resistivity Standard thickness Thickness uniformity Surface roughness Dielectric constant DC measurement | 33 x27.6cm2 ~1010Ωcm 0.7, 1.1mm 20μm <10nm 7.5 - 9.5 Ohmic behavior stable up to 1C/cm2
Performance of low resistive glass

## Slide 8
Continuous melting
Continuous pouring
Continuous annealing
Glass mass production
The roughcast of glass

## Slide 9
Volume resistivity: ~1010.cm
363mm
219mm
171mm
25mm
 | Length/mm | Width/mm | Thickness/mm
Gas gap | - | - | 0.25×10
Inner glass | 320 | 130-171 | 0.7
Outer glass | 330 | 138-182 | 1.1
Mylar | 335 | 153-198 | 0.18
Inner PCB | 350 | 182-228 | 1.6
Outer PCB | 350 | 172-218 | 0.8
Honeycomb | 330 | 153-198 | 6
Material dimensions
A MRPC prototype for SoLID-TOF

## Slide 10
Beam test @ Hall A
Shield
High Energy e-
Top View
PMT1
PMT2
PMT3
PMT4
PMT0
Target
Target
Test setup
The diagram of DAQ system

## Slide 11
Rate Performance
Voltage: 6800V
Flux:11kHz/cm²
Efficiency:~95%
Time Resolution: 78ps
Flux:16kHz/cm²
Efficiency:~95%
Time Resolution: 82ps
Wan Yi. A MRPC prototype for SOLID-TOF in Jlab.
2013_JINST_8_P03003

## Slide 12
12
Aging test of low resistive glass
This glass was applied with 1000V for about 32days, integrated charge: 1 C/cm2
--roughly corresponding to the CBM life-time over 5 years operation at the maximum particle rate.
Glass specifications:

## Slide 13
13
Hign rate MRPC
X-ray Generator
130cm
60cm
Online irradiation test
This is online test system. The efficiency and time resolution can be obtained by cosmic ray while irradiated by X-rays. 0.1C/cm2 charge is accumulated in 35 days.

## Slide 14
14
Performance Vs Dosage
~500 events/5days
More events ->Better statistics

## Slide 15
TOF electronics
Fast preamplifier：
Ninos (TOT) (ALICE)
Padi (TOT) (GSI)
CAD (TOT) (Tsinghua)
Low time jitter faster FEE
TDC
HPTDC (ALICE, 25ps/ch)
GET4 (GSI, 25ps/ch)
FPGA TDC (GSI and other)
Pulse wave form digitizer
DAQ

## Slide 16
MRPC
Preamplifier
&
Discriminator
Time to Digital Converter
ROC
DCB
Preamplifier
&
Discriminator
Time to Digital Converter
ROC
MRPC
CLK
TOF readout chain with PADI and GET4

## Slide 17
Intrinsic resolution of 10gap-MRPC
Time jitter of HPTDC 25ps
NINOs ASIC+Interface card 24ps
MRPC resolution tested 40ps
So the intrinsic resolution of MRPC is:
MRPC
Differential FEE
TDC
START

## Slide 18
18
Resolution of 24 x140m MRPC
Fast wave form digitizer 30-> 5ps
Low time jitter fast FEE 24-> 5ps
MRPC intrinsic 20-> 13ps
Time resolution of TOF:

## Slide 19
PID and time resolution
TOF Positives
Compact (10-15 cm of space needed), allowing more room for, e.g., RICH
More clean PID
Can contribute to e/h identification using TPC dE/dx
TOF Negatives
Start counter?
@ 1m distance | Distance | Pion-Kaon Separation | Kaon-Proton Separation
σtot=100 ps | 1m |  | 
σtot=10 ps | 1m |  | 
σtot=10 ps | 3m |  | 
Momentum reach of TOF PID reaches interesting levels if one can achieve ~ 10 ps

## Slide 20
Item | dimension/mm
Honeycomb | 90×265×7.5
Outer PCB | 120×298×0.6
Middle PCB1 | 120×298×1.2
Middle PCB2 | 120×328×1.2
Strip length | 268
Strip width | 7
Mylar | 90×268×0.25
Glass | 80×258×0.5
Carbon | 72×250
Gas gap width | 0.104
Number of gas gap | 32
Structure of high time MRPC
Honey comb plate
PCB
Mylar
Carbon electrode
Glass

## Slide 21
Fast amplifier
Waveform Digitizer
DT5742
Test equipment
Gas box
DRS4-V5 chip
16 channels
12bit 5GS/s
5 points for leading edge of MRPC

## Slide 22
Cosmic test
Gas Mixture : “Freon” (R134a) 90% : Iso 5% : SF6 5%

## Slide 23
Efficiency HV=5.5kV
5600V
5500V
Test results
Charge
Charge
Efficiency of MRPC1
Efficiency of MRPC2
98.37%
99.10%

## Slide 24
σ =89.92ps
Walk correction
Time resolution
Time difference of two MRPC

## Slide 25
Particle |  | e+, e-,+,-,p
momentum | e | 200MeV/c~1.3GeV/c
 |  | 400MeV/c~900MeV/c
 | p | 500MeV/c~1GeV/c
rate |  | 10~20Hz
Beam Test at IHEP
Trigger
S
C
2
S
C
1
M
W
P
C
C
0
e
,
,
p
5
0
c
m
5
0
c
m
6
0
c
m
MRPC

## Slide 26
Time
Time
Count

P
Signal selection

## Slide 27
Time resolution
Difference between time of two MRPC: Δt = t2 – t1= 52ps
  σt = Δt/√2 = 37 ps
  Only protons are used
  Used a “Leading Edge Discriminator technique” in software from waveform, slewing correction
  Wings manily due to noise, cross-talk, or something else?
We believe best published result is 20 ps
  Nucl.Instrum.Meth. A594 (2008) 39-43
  Nucl.Instrum.Meth. A629 (2011) 106-110

## Slide 28
Conclusions
A SoLID-TOF MRPC prototype is developed, its time resolution is 75ps, rate capability reach 16kHz/cm2.
MRPC intrinsic resolution can reach 13ps. Fast FEE and high band width wave form digitizer has to be used to improve TOF resolution -> 15ps.
Very narrow-gap MRPC were designed and tested, its efficiency can reach 98% and time resolution around 37ps. More detailed research should be done to improve time resolution.

## Slide 29
Thanks for your attention !