## Slide 1: Trigger rate estimation
Yuxiang Zhao
Aug-27-2016

## Slide 2: Introduction
PVDIS trigger: EC + LGC (x>0.35 && W>2 GeV)
  EC response study updated by Rakitha using Hall D generator
  LGC with working gas and threshold updated (Michael)
SIDIS trigger
  Electron trigger
    Forward: EC + LGC + SPD + MRPC (Q2 > 1GeV2)
    Large: EC + SPD (P > 3 GeV)
  Hadron trigger
    EC + SPD + MRPC (could be different depending on further study)

## Slide 3
PVDIS trigger rate

## Slide 4: Singles rate on EC
Singles particles | Rate (MHz) Jin’s curve, wiser generator, extrapolation below 1 GeV | Rate (MHz) Rakitha’s curve, Hall D generator, cut off at 1 GeV
Electron | 0.282 | 0.241
Pim (Hall D) | 5.05 | 4.4
Pip (Hall D) | 1.0 | 0.43
Pi0(Hall D) | 0.031 | 0.015
Total | 6.36=(212 KHz/sector) | 5.09=(170 KHz/sector)
Rate becomes lower by using Hall D generator based simulation

## Slide 5: Singles rate on LGC
singles | Rate (MHz)
Electron | 0.4465
Pim (Hall D) | 0.823
Pip (Hall D) | 0.436
Pi0(Hall D) | 21.76
EM background only (beam on target with hadron processes blocked) | 0.6 (18 out of 1066 windows can produce a lgc trigger)
Total | 24.1 MHZ (803KHz/sector)
Beam on target with all processes on: 42MHz
Different by 17.9 MHz
From difference of pi0 rate between G4 and Hall D generator
Threshold: PMT=2, P.E on each pmt=2

## Slide 6: Coincidence rate among detectors
PID | Only EC fired | Rate with EC and lgc both fired for the same e or pion event | Efficiency of LGC
Electron | 0.24 MHz | 0.23 MHz | 95.7%
Pim | 4.43 MHz | 0.64 KHz | 0.01%
Pip | 0.43 MHz | 0 (limit: 0.04kHz) | 0.01%
Pi0 | 0.015 MHz | 8.5 KHz | 55%
Well defined particles with EC&LGC = (230 + 0.64 + 0.04 + 8.5) KHz = 239 KHz = 8 KHz/sector
Random coincidence per sector = 170 KHz * 803 KHz * 30ns = 4.1 KHz/sector
Total: (8+4.1) KHz = 12.1 KHz/sector

## Slide 7: Concern of particle correlations
High singles rate: pim on EC, pi0 on LGC
How large is the correlation between pim and pi0 ???
  Hall D generator can have all possible pions in one event
  Looking at EC&LGC coincidence will give us hints on the correlations between pions
0.3% of “all-pion” events will fire EC and LGC at the same time
Seems that correlation of pions on EC and LGC is small

## Slide 8: Short summary of PVDIS trigger rate
Study based on Hall D generator
  Total rate: (8+4.1) KHz = 12.1 KHz/sector

## Slide 9
SIDIS trigger rate
EC response using Hall D generator is under way (Rakitha)
SPD
  Forward angle: 60 in phi dimension, 4 in r dimension
  Large angle: 60 in phi dimension
  Optimization of threshold is ongoing (Sanghwa)
MRPC
  60 in phi dimension, 4 in r dimension, each module has 10 layers of gas gap
Using wiser simulation to get start while waiting for Hall D generator based study

## Slide 10: Current Thresholds used for individual detectors
EC
  Forward angle: Q2 > 1 GeV2
  Large angle: P>3 GeV
LGC: 2 PMTs in a sector, 2 P.E for each PMT
SPD: 0.35MeV for energy deposition
MRPC
  16eV energy deposition in a gas gap
  at least 5 gaps to be fired

## Slide 11: SIDIS forward angle electron trigger
Singles particle | EC Rate (kHz) | LGC Rate(KHz) | SPD Rate(MHz) | MRPC Rate(MHz) | All 4 fired Rate(KHz)
electron | 53.9 | 77.2 | 2.0 | 1.16 | 42
Pim | 864 | 82.4 | 15.7 | 14.4 | 6.4
Pip | 1036 | 85.7 | 19.1 | 17.6 | 7.5
Pi0 | 2210 | 2045 | 10.8 | 7.6 | 88.1
Using Wiser simulation to start
Total electron-like trigger rate in forward angle: 144 KHz + random coincidence among detectors
Random coincidence is high, need to define the “track match” area to decrease rate

## Slide 12: SIDIS large angle electron trigger
Singles particle | EC Rate (kHz) | SPD Rate(MHz) | Both fired Rate(KHz)
electron | 2.9 | 2.56 | 2.8
Pim | 8.2 | 21.9 | 8.2
Pip | 10 | 26.5 | 10
Pi0 | 20.4 | 18.1 | 8
Using Wiser generator to start
Total electron-like trigger rate in large angle: 29 KHz + random coincidence

## Slide 13: To-do list for SIDIS trigger rate estimation
Update EC response using Hall D generator (Rakitha)
Update SPD threshold (Sanghwa)
Update MRPC threshold (Sanghwa?)
Hadron-like trigger rate estimation
Define how to do “track match” at trigger level to reduce random coincidence rate (among detectors)
Efficiency study by combining all the individual detectors in the trigger design
Still long way to go…

## Slide 14: Summary
PVDIS trigger rate: (8+4.1) KHz = 12.1 KHz/sector
SIDIS study needs more efforts

## Slide 15: Backups

## Slide 16: Number of p.e produced by EM on lgc within 30ns
EM is not an issue on lgc, only the pile up effects
On whole LGC, not per sector