## Slide 1
High time resolution TOF for SoLID
Outline:
  Requirement of SoLID-TOF
  Development of high rate and high time TOF
  Next to do
  Wang Yi
Department of Engineering Physics, Tsinghua University

## Slide 2: Particle rate entering MRPC
Dominant by photon in MeV
γ : 250kHz/cm2
e: 5kHz/cm2
n: 3kHz/cm2
Particle rate in front of MRPC

## Slide 3: Energy of Photon, electron and neutron
Energy range
γ : 10-5 – 10GeV
e: 10-6 – 10GeV
n: 10-6 – 1GeV

## Slide 4: Particle rate detected by MRPC
Detected particle rate
γ : 12.5kHz/cm2
e: 5kHz/cm2
n: 0.05kHz/cm2
γ
n
e
Total: 18kHz/cm2

## Slide 5
Main requirements for TOF
The MRPC is developed for the TOF of SoLID
Main Requirements for TOF:
  /k separation up to 7GeV/c & 3 
  Time resolution < 20ps
  Rate capability : 18kHz/cm²
This is big challenge of MRPC-TOF!!

## Slide 6
High rate, high time precision TOF

## Slide 7
Continuous melting
Continuous pouring
Continuous annealing
Glass mass production
The roughcast of glass

## Slide 8
Item | dimension/mm
Honeycomb | 90×265×7.5
Outer PCB | 120×298×0.6
Middle PCB1 | 120×298×1.2
Middle PCB2 | 120×328×1.2
Strip length | 268
Strip width | 7
Mylar | 90×268×0.25
Glass | 80×258×0.5
Carbon | 72×250
Gas gap width | 0.104
Number of gas gap | 32
Structure of high time MRPC
Honey comb plate
PCB
Mylar
Carbon electrode
Glass

## Slide 9
Fast amplifier
Waveform Digitizer
DT5742
Test equipment
Gas box
DRS4-V5 chip
16 channels
12bit 5GS/s
5 points for leading edge of MRPC

## Slide 10
SCA based waveform digitizer

## Slide 11
Calibration of DC offset

## Slide 12
Calibration of sampling interval

## Slide 13
Cosmic test
Gas Mixture : “Freon” (R134a) 90% : Iso 5% : SF6 5%

## Slide 14
Efficiency HV=5.5kV
5600V
5500V
Test results
Charge
Charge
Efficiency of MRPC1
Efficiency of MRPC2
98.37%
99.10%

## Slide 15
σ =89.92ps
Walk correction
Time resolution
Time difference of two MRPC

## Slide 16
Particle |  | e+, e-,+,-,p
momentum | e | 200MeV/c~1.3GeV/c
 |  | 400MeV/c~900MeV/c
 | p | 500MeV/c~1GeV/c
rate |  | 10~20Hz
Beam Test at IHEP
Trigger
S
C
2
S
C
1
M
W
P
C
C
0
e
,
,
p
5
0
c
m
5
0
c
m
6
0
c
m
MRPC

## Slide 17
Time
Time
Count

P
Signal selection

## Slide 18
Time resolution
Difference between time of two MRPC: Δt = t2 – t1= 52ps
  σt = Δt/√2 = 37 ps
  Only protons are used
  Used a “Leading Edge Discriminator technique” in software from waveform, slewing correction
  Wings manily due to jitter of waveform digitizer, low electric field, noise or analysis method.
We believe best result is 20 ps

## Slide 19
Next to do
Detailed calibration of DT5742 (DRS4)
Improve analysis method
Improve connect between MRPC and fast amplifier
Propose R&D NSFC key project (collaborate with CCNU, USTC)

## Slide 20
Thanks for your attention !