## Slide 1
Overview of SoLID
Jian-ping Chen
Jefferson Lab
Director’s Review of SoLID
Febuary 9-10, 2020
Acknowledgement: Thanks to many of my SoLID collaborators for helping with slides:
Alexandre Camsonne, David Flay, Haiyan Gao, Ole Hansen, Garth Hubert,
Nilanga Liyanaga, Zein-Eddine Meziani, Chao Peng, Michael Paolone, Whit Seay,
Paul Souder, Steve Wood, Zhihong Ye, Jixie Zhang, Zhiwen Zhao, Xiaochao Zheng, …

## Slide 2
Outline
Introduction and Overview of SoLID:
Physics, Timeline, Collaboration
Technical Requirements
2. Pre-Conceptual Design
Subsystems, Simulated Performance,
Risk Assessments
3. Pre-R&D Activities
Previous Director’s Reviews
Cost and Schedule Estimation
6. Summary

## Slide 3
The JLab Director’s Review Charge:
(C1) The significance of scientific questions identified by the SoLID Collaboration.
(C2) The impact of the planned scientific program on the advancement of nuclear physics in the context of current and planned world-wide capabilities, including the US Electron Ion Collider.
(C3) The new experimental and theoretical research efforts and technical capabilities needed to accomplish the proposed scientific program.
(C4) The feasibility of the approach or method presented to carry out the proposed scientific program and the likelihood that significant results can be obtained in the first three years of detector operations.
This presentation will give an introduction/overview,
then provide information related to C3 and C4.

## Slide 4
Introduction and Overview of SoLID
Physics, Timeline, Collaboration
Technical Requirements

## Slide 5
Full exploitation of JLab 12 GeV Upgrade to maximize scientific return
A Large Acceptance Detector AND Can Handle High Luminosity (1037-1039)
  SIDIS: 3D momentum imaging of a relativistic strongly interacting confined system (nucleon spin)
  PVDIS: pushing the phase space in the search of new physics and of hadronic physics
  Precision threshold J/y - probing strong color fields in the nucleon (proton mass)
Strong collaboration (270+ collaborators from +70 institutions, 13 countries)
  Anticipate international contributions
  Strong theoretical support
SoLID physics complementary and synergistic with the EIC science (proton spin and mass, two important EIC science questions) – high-luminosity SoLID unique for valence quark tomography and precision J/𝝍 production near the threshold
SoLID Physics Overview

## Slide 6
Timeline
- Since 2010: Five SoLID experiments approved by PAC with high rating
3 SIDIS with polarized 3He/p target, 1 PVDIS, 1 threshold J/y
Six additional run-group experiments approved
SoLID collaboration, with JLab support, has been continuously working on
pre-conceptual design and pre-R&D
2013: CLEO-II magnet requested, agreed, arrived at JLab 2016,
2014: pCDR submitted to JLab with cost estimation
2015: 1st Director’s Review: positive with many recommendations
- 2017: Updated pCDR submitted to JLab with responses to the recommendations
- 2018: DOE NP visit and discussion:  update cost estimation
- 1/2019: Updated pCDR (new cost estimation) submitted to JLab
9/2019: 2nd Director’s Review: successful with only few recommendations
Late 2019: Pre-R&D plan approved, funding started 2/2020
2/2020: SoLID MIE (with updated pCDR) Submission to DOE
3/2021: SoLID DOE Science (Scheduled)

## Slide 7
Strong Collaboration
- 270+ collaborators, 70+ institutions from 13 countries
Large international participations and anticipate contributions
Strong theory support

## Slide 8
Technical Requirements
High luminosity (1037 for SIDIS and J/y, 1039 for PVDIS with baffle)
Particle detection:
PVDIS: single e-
SIDIS: coincidence e and pi+/pi- (K+/K- with enhanced configuration)
J/y: e- and e+e- (also e+e- for photoproduction, e-, e+e-, p for systematics)
Large acceptance: 2p in f angle, q angle: 8-24 degrees for SIDIS, J/y
22-35 degrees for PVDIS
Momentum range: 1 - 7 GeV/c
High rates (100 KHz trigger rate for SIDIS, 600KHz/30 for PVDIS)
High background (~ GHz, dominated by low energy photons/electrons)
High radiation environment
Moderate resolutions (~2% in momentum, 1-3 mr in q, 6 mr in f)
Good electron PID
Moderate pion PID (SIDIS)
Demanding Kaon PID (SIDIS-Kaon, enhanced configuration)
High precision with low systematics
* Targets (cryogenic LH2/LD2, T/L polarized 3He, T polarized NH3)
* Beam polarimetry (demanding precision for PVDIS, 0.4%)
* Dependencies (see talk by Rolf Ent)

## Slide 9
2. Pre-Conceptual Design
Subsystems, Simulated Performance,
Risk Assessments
Related to Charges C3 and C4

## Slide 10
SoLID in Hall A
Plan for installing SoLID in Hall A with other equipment moved out of the way.

## Slide 11
SoLID Apparatus
High Luminosity (1037-1039)
High data rate
High background
Low systematics
High Radiation
Large scale
Modern Technologies
  GEM’s
  Shashlik ECal
  Pipeline DAQ
Requirements are Challenging
Polarized 3He (``neutron”) @ SoLID

## Slide 12
SoLID Detector Subsystems
Uses full capability of JLab electronics
PVDIS: Baffle 3xGEMS LGC 2xGEMs EC
SIDIS&J/y:
4xGEMs LASPD LAEC 2xGEMs LGC HGC FASPD (MRPC) FAEC
Pre-R&D items: LGC, HGC, GEM’s, DAQ/Electronics, Magnet

## Slide 13
Magnet: Requirement and Design
Requirements:
Acceptance: P: 1.0 – 7.0 GeV/c;
Φ: 2π; θ: 8o-24o (SIDIS), 22o-35o (PVDIS)
 Resolution: δP/P ~ 2%
(requires 0.1 mm tracking resolution)
 Fringe field at the 3He target < 5 Gauss
Use CLEO II magnet with the following
modifications
  Two of three layers of return yoke
  needed
  Add thickness to front endcap
  Add extended endcap
CLEO II coil at JLab
Yoke for SoLID

## Slide 14: Cold Test Update – Cold Test Milestones
Test Lab Control Room
Cryo Dist Can
Solenoid rehab will confirm condition of the magnet
Provide risk reduction to the project
Improve magnet cost estimate
Estimated completion Sept 2021

## Slide 15
PVDIS Baffle Design
SoLID PVDIS needs to run 1x1039/cm2/s luminosity
Baffle is made of 12 planes of 9cm thick lead with slits following electron bending in SoLID field
It blocks neutral and positive tracks from target, and thus reduces background by 1-2 orders of magnitude and reduces trigger rate to be within DAQ capability
Acceptance ~30% for DIS electrons is maintained at P>3GeV and x>0.4 region

## Slide 16
EIC Prototype: similar to SoLID design
GEM tracking
GEM Technology
GEM configuration
Rate capabilities > many MHz/cm2
High position resolution
Cover large areas at reasonable cost
Low thickness (~0.5 radiation length)
Used in many experiments (COMPASS, STAR, ALICE, PRad@JLab…) and planned for many future experiments SBS@JLab, CMS upgrade, EIC…)

## Slide 17
Simulated GEM Performance
Risk:
VMM chips need testing: addressed in Pre R&D plan
Efficiency and accuracy for
PVDIS versus kinematics
APV versus VMM
Electron Momentum Resolution versus angle
<2% for > 10o

## Slide 18
Light Gas Cerenkov: Requirements
General Requirement A: Provide 500:1 electron / pion separation for the major SoLID programs: PVDIS, J/Psi, and SIDIS.
General Requirement B: Provide trigger level input while maximizing efficiency and minimizing cost.

## Slide 19
LGC Performance and Risk
PVDIS
J/Psi SIDIS
With the proposed LGC design, pion rejection factors stay above 500:1 for both configurations.
Pion threshold at 20C and 1 atm:
  N2: 5.73 GeV/c
  CO2: 4.67 GeV/c
Technical risk: optimizing performance at high rates, addressed in Pre-R&D plan.

## Slide 20
Heavy Gas Cerenkov (HGC)
HGC is used to identify charged pions and reject charged kaons.
It is only used for SIDIS experiments.
Field at photonsensor location: ~100G
Radiator: ~1m C4F8 gas at 1.7atm at 20C
Not in trigger
Otherwise, similar to the LGC

## Slide 21
Heavy Gas Cerenkov: Simulated Performance
7.0-7.5GeV, 14-15deg
Simulated NPE versus momentum
Simulated Response to pions and kaons
2.5-3.0GeV, 8-9deg
Kinematic coverage: 2.5GeV < P < 7.5GeV, 8o < θ < 15o, full azimuthal angle
π+/π- detection: efficiency >90%, Np.e. > 10
K+/K- rejection: factor >10

## Slide 22
ECal Requirement and Design
– Combined with LGC to provide triggering;
– 50:1 pion rejection with 90% electron efficiency;
– provide ~1cm shower position for background suppression;
– radiation hard: >500 krad, high neutron background;
– inside 1.5 T field
– modules swappable between PVDIS and SIDIS

## Slide 23
ECAL Performance
Realistic simulation with background and supporting material
Resolution: for all angles, reached p0~(5-6)% and p2~(5-6)%
FAEC electron
FAEC pion

## Slide 24: Fermilab Beam Test with Shashlyk Modules
Goal: Understand the detection resolution and efficiency of the Shashlyk modules
Beam time: Jan 13-26, 2021
Setup: 2X0 lead, 3 preshower, 2-cm Al support, 3 Shashlyk modules; FTBF’s MWPC+Cherenkov
People power: (UVA) Jixie Zhang, Xinzhan Bai; (JLab) Alexandre Camsonne, David Flay;
(ANL) Paul Reimer, Junqi Xie, Manoj Jadhav
beam
pre-shower
shower
scintillator
Beam energy (GeV) | total trigger | total electron trigger (online)
1 | 3.1M | 3.0M
2 | 2.9M | 2.7M
4 | 4.5M | 3.9M
6 | 2.8M | 2.1M
8 | 5.5M | 3.4M
10 | 6.8M | 3.6M
12 | 3.0M | 1.3M
16 | 7.6M | 2.3M

## Slide 25
Scintillator Pad Detector: Requirements and Design
LASPD: photon rejection 5:1;
coincidence TOF (150ps)
→ design: 20mm-thick,
60 azimuthal segments,
direct coupling to fine-mesh PMT
FASPD: photon rejection 5:1
→ design: 5-10mm-thick
240 segments (60 X 4)
WLS fiber embedding,
MAPMT (outside magnet)

## Slide 26
LASPD: photon rejection 5:1;
coincidence TOF (150ps)
→ design: 20mm-thick,
60 azimuthal segments,
direct coupling to fine-mesh PMT (for FMPMT study see NIMA 827 (2016) 137-144)
FASPD: photon rejection 5:1
→ design: 5-10mm-thick
240 segments (60 X 4)
WLS fiber embedding,
MAPMT (outside magnet)
a LASPD prototype equipped with (regular) PMTs
Scintillator Pad Detector: Requirements and Design

## Slide 27
Long-term goals
Develop end-to-end simulation and reconstruction chain.
  Integrated software environment for (almost) all parts of data processing
  Modern, multi-threaded, grid-enabled framework written in C++
  Common conditions data and geometry database API
  Consistent ROOT-based event data file format w/ metadata storage
  Python or JSON/YAML-based job configuration
Provide online and offline analysis software, event display, calibration tools etc. as well as complete set of simulation and digitization modules.
Feasibility studies underway in collaboration with other JLab groups.
Software and Simulations
Existing simulations: SoLID_GEMC
GEMC is a Geant4-based simulation package, used by CLAS12.
Added SoLID detector description and signal digitization, esp. for GEMs.
Used extensively for SoLID pre-CDR and in current pre-R&D studies.
Variety of physics generators available.

## Slide 28
DAQ Requirements and Design
DAQ based on 12 GeV FADC base pipelined electronics designed for 200 KHz trigger rates,100 kHz rates demonstrated in Hall B and D
VMM chip based readout for GEMs
  ATLAS Small Wheel Micromegas readout chip : up to 4 MHz trigger rate per channel, limited by occupancy in detector – designed for 200 KHz
  Older chip APV25 used by SBS as backup option
Design goal well within hardware capabilities with some safety margin
  60 KHz/sector for PVDIS, expect 20 KHz/sector, ~ 2 GB/s, 30 sectors
  120 KHz total for SIDIS, expect 100 KHz, ~ 2 GB/s
  100 KHz total for J/Psi, expect 60 KHz, ~ 3 GB/s
Pre-R&D to validate required rates and determine maximum rates achievable
Existing infrastructure
  Network : 10 GB/s
  Silo
    Current setup: data rate 6 GB/s
    IBM TS3500 highly scalable: Data rate upgradable up to 69 GB/s
    Maximum data 250 PB
Rate limitation mostly from storage cost

## Slide 29: DAQ Risk Assessment
Technical risk low : existing with current technologies available
(deadtime less pipeline electronics, network, data bandwidth )
for example data rates much smaller than CERN LHC
Making sure all requirements are met within cost
  Simulation with full background
    Trigger rates
    Data reduction algorithms
    Occupancies
    Systematic errors
    Evaluation of amount of data to be recorded
  Small scale prototyping and beam tests to validate simulation and modeling of the DAQ
Addressed in the Pre-R&D plan

## Slide 30
Chart: Raw Data Rate (MB/s)
| 2029 | 2030 | 2031 | 2032 | 2033 | 2034
 | 2000 | 2000 | 2000 | 2400 | 2000 | 2000 | 2000 | 0 | 1500 | 1500 | 1500 | 1500
Raw data rate comparable to GlueX & CLAS12 (~2 GB/s).
Estimated CPU requirements already manageable with today's farm resources
Tape requirements (25–30 PB/yr) significantly higher than current experiments.
J/y has ~50% higher storage requirements due to larger event size.
2020 Farm Capacity
SIDIS-3He
SIDIS-p
PVDIS
J/y
Chart: CPU Requirements (M-core-hours)
| 2029 | 2030 | 2031 | 2032 | 2033 | 2034
Simulation | 5.4 | 5.4 | 4.2 | 4.32 | 5.4 | 5.4 | 3.6 | 0 | 16.2 | 16.2 | 16.2 | 12.24
Production | 9.72 | 9.72 | 7.56 | 12.96 | 9.72 | 9.72 | 6.48 | 0 | 19.44 | 19.44 | 19.44 | 14.688
Chart: Tape Requirements (PB)
| 2029 | 2030 | 2031 | 2032 | 2033 | 2034
Raw (no duplicates) | 7.776 | 7.776 | 6.048 | 12.4416 | 7.776 | 7.776 | 5.184 | 0 | 5.832 | 5.832 | 5.832 | 4.4064
Simulated | 0.7776 | 0.7776 | 0.6048 | 1.2442 | 0.7776 | 0.7776 | 0.5184 | 0 | 0.2916 | 0.2916 | 0.2916 | 0.22032
Production | 4.6656 | 4.6656 | 3.6288 | 7.465 | 4.6656 | 4.6656 | 3.1104 | 0 | 8.748 | 8.748 | 8.748 | 6.6096
Computing Requirements

## Slide 31
3. Pre-R&D Activities
Objectives, DAQ,
Cherenkov
Address Charge C4

## Slide 32: Pre-R&D objectives
No "show-stoppers", regardless of pre-R&D activities.
Pre-R&D: help steer design, better define contingency.
Better understanding of the capabilities and response of existing technologies
when applied to the SoLID detector can optimize efficiency and reduce cost.
Objectives:
  Better understand the realistic response of our proposed electronics under high-rates expected during SoLID production running.
  Determine the most efficient high-rate electron trigger configuration for SoLID
  Better match true response to Monte Carlo.
Identified pre-R&D items:
  DAQ (JLab, UVa, U-Mass)
  Cherenkov at high rates (ANL, Duke, JLab, Temple and NMSU)
  Magnet cold test (JLab)

## Slide 33: SoLID DAQ pre-R&D
5 systems are being tested
  GEM VMM3 testing in high background
    Evaluation board readout almost complete : will test with detector end of December / beginning of January
    128 channels prototype design close to complete
    VMM3 chips ordered
    On track for testing with X-ray source in spring 2021
  GEM APV25 maximum trigger rate with SBS electronics
    Tested 10 KHz 6 samples with 5 APV at 100 % occupancy gives more than 100 KHz with one sample and 30% occupancy for SIDIS
    Parts ordered for full scale testing at 100 KHz 1 sample
    Fast readout development started
  Gas Cerenkov readout and trigger with FADC and MAROC
    Data taken with FADC with MaPMT and FADC
    MAROC prototype being tested on the bench
  FADC fast readout and dead time measurement for PVDIS
    Test stand setup at UMass for FADC and VTP : development of trigger
    Fast FADC readout through VXS started : 16x faster readout than using regular VME
  Time of flight sampling chip
    Board setup and setting up testing with cosmics and source

## Slide 34: Cherenkov Pre-R&D Timeline
Prototyping Cherenkov detector was designed and construction was completed at Temple in winter of 2019.
In early 2020, Cosmic testing was performed at the ESB and initial data was collected in Hall-C before MEDCON shutdown.
Additional high-rate data was collected in the fall of 2020.
Design
Construction @ Temple U
Cosmic Testing @ ESB
Parasitic running @ Hall-C
2020

## Slide 35: Progress on Cherenkov pre-R&D goals
Primary:
  Understand the exact response of Hamamatsu H12700 MaPMTs, aligned in a square array, under high- rate conditions to:
  Best understand the realistic response of our proposed electronics
  Determine the most efficient high-rate electron trigger configuration for in SoLID
  Better match true response to Monte Carlo.
Secondary:
  Test alternate technologies:
    WLS coated LAPPD
    MAROC summing electronics (pixel+quad+sum readout)
  Test components of Cherenkov detectors
    Simple summing board design
    Mirror fabrication (reflective lexan film + carbon fiber blanks)
    C4F8 gas response and interaction with electronics under realistic conditions.
    WLS coated MaPMT response with pixel/quadrant/sum logic.
These goals are either completed, or we collected the data and analysis is underway!
Remaining goals are being evaluated on the bench.

## Slide 36
4. Previous Director’s Reviews
Recommendations
Responses

## Slide 37: Previous JLab Director’s Reviews
JLab Director’s Reviews were held in 2/2015 and 9/2019
Benefited greatly from the very helpful recommendations
Science Related Recommendations
1. Demonstrate performance and technical capability, develop end-to-end simulations, address technical risks
2. Show impacts with respect to the other world and JLab programs
3. “Investigate the possibility of kaon identification”
(R&D on MRPC with <30 ps performance)
4. “Investigate the feasibility of carrying out a competitive GPD program”

## Slide 38: Developing SoLID GPD program
, M. Boer

## Slide 39
5. Cost and Schedule Estimations

## Slide 40
SoLID Cost Estimation
WBS | Subsystem | Cost –M$ (with overhead)
1.01 | PM | 1.5
1.02 | EM | 10.1
1.03 | LGC | 5.6
1.04 | HGC | 6.0
1.05 | GEM | 5.8
1.06 | DAQ | 6.2
1.07 | Software | 0.7
1.08 | Magnet | 7.8
1.09 | Infrastructure | 9.6
1.10 | OPC | 
Cost before contingency and escalation: 53.3 M$
With contingency 72.2 M$
With escalation 82.4 M$ (Total Equipment Cost)
Each L2 WBS includes design and construction

## Slide 41
Assumptions:
1.5 Years pre-R&D (in progress)
Project starts in FY2022, 2 Years Project Engineering and Design (PED) (FY22-FY23), Construction long-lead items start in FY23
Main construction starts in FY24, 3+ Years construction, complete by end of 2026.
1 Year Installation 2027
Testing/commissioning: start with magnet/testing, then ECal/GEM with DAQ for testing, Then HGC/LGC
Schedule contingency ~ 1 year
SoLID Project Schedule Estimations
Start Physics in 2029

## Slide 42: Summary
SoLID: A large acceptance device which can handle very high luminosity to allow full exploitation of JLab 12 GeV potential
 pushing the limit of the luminosity frontier
After a decade of hard work, we have a mature pre-conceptual design with expected performance to meet the challenging requirements for the three major science programs
SoLID benefited greatly from the previous Director’s Reviews
Technical risks are assessed and addressed in the pre-R&D activities.
Cost and schedule have been evaluated multiple times