## Slide 1: PR12-25-010, JLab PAC 53 Double Deeply Virtual Compton Scattering with SoLIDμ spectrometer
Juan-Sebastian Alvarado, IJCLab Alexandre Camsonne, Jlab (contact) Marie Boer, Virginia Tech Eric Voutier, IJCLab Xinzhan Bai, JLab Zhiwen Zhao, Duke (presenter)
and SoLID Collaboration
July 21, 2025

## Slide 2: Outline
Generalized Parton Distribution
Double Deeply Virtual Compton Scattering
SoLIDµ setup
Muon detector
Simulation study
Physics projection
Beam time request
Summary

## Slide 3: Generalized Parton Distribution (GPD)
A unified description of partons (quarks and gluons) in the momentum and impact parameter space
Parton Distribution Functions Longitudinal momentum distributions
Elastic form factors Transverse spatial distributions
Notes: GPD describe 3D nucleon structure in long momentum and transverse spatial distribution

## Slide 4: Nucleon Structure and GPD
d
A.W. Thomas, PRL 101 (2008) 102003
u
GPDs encode correlations between partons and contain information about internal dynamics of hadrons like angular momentum or distribution of the forces experienced by quarks and gluons
imaging
spin
gravitational form factor
The experimental knowledge of the x-dependence of GPDs at fixed longitudinal momentum fraction is a crucial step for unraveling the 3D structure and internal dynamics of the nucleon

## Slide 5: General Compton Process accessing GPD
γ*(q) + p(p) → γ*(q′) + p(p′)
DVCS (γ* → γ, Q’2=0, ξ’ = ξ)
Timelike CS (γ → γ*, Q2=0, ξ’ = - ξ)
Double DVCS (γ* → γ*, Q2 Q’2 ξ’ ξ vary)
Generalized
Bjorken variable
Skewness
Because of the virtuality of the initial and final photon, DDVCS allows direct access to GPDs at crucial for modeling and investigation of nuclear imaging, spin, and internal dynamics
Following the sign change of x’ around Q’2=Q2, the imaginary part of and change sign, providing a testing ground of GPD universality.
Compton Form Factor (CFF)
GPD combination
Notes: DDVCS with both virtual photon provide gpd access beyond the diagonal lines.

## Slide 6: Elementary Cross Section
DDVCS cross section is about ~1/100 of DVCS, involves two Bethe-Heitler (BH) processes
DDVCS
BH1
BH2

## Slide 7
5-fold TCS-like observables obtained from the integration over the polar angle of muon and the azimuthal angle of initial virtual photon, also minimizing the contribution of the BH2 process
Integrated Cross Section
Our study focuses on using TCS-like observables for projection to allow access to both terms above
DVCS-like observables obtained by integrating over muon phi angle may also be considered as crosscheck
TCS-like xs
θ0=π/4
Notes: TCS-like observables allow access to both both terms

## Slide 8: Beam Spin Asymmetry
Access to the imaginary part of CFFs
BSA changes sign when transitioning from DVCS-like region (ξ’>0, Q²>Q'²) to TCS-like region (ξ’<0, Q²<Q'²)
DDVCS BSAs are dominated by the CFF , thus providing a measurement of the GPD at to DVCS
BSA in two regions

## Slide 9: Muon Charge Asymmetry
Access to the real part of CFFs (no dispersion relation has been established)
μCA predicted to have significant amplitude and rich harmonic composition, like the forward-backward asymmetry of TCS
Curvature change is a highly-discriminating feature for models
DDVCS μCA access a CFF combination different from BSA. This feature distinguishes DDVCS from DVCS and TCS.
aka Forward Backward Asymmetry
μCA in two regions

## Slide 10: Experimental Setup
SoLID can detect e-, e+, proton, pion
Based on SoLID J/Psi and TCS setup (1.2e37/cm2/s) with forward angle muon detector added to form SoLIDμ spectrometer
Sharing beam time with approved J/Psi and TCS di-e experiment
Forward Angle (FA) covers 8.5-16.5deg and Large Angle (LA) covers 18-30deg

## Slide 11: Forward Angle Muon Detector (FAMD)
3 layers of iron+tracker+scintillator (Rin=1m, Rout=3m)
Iron for pion blocking
µRWell trackers to connect with tracks in SoLID inner GEM trackers
  track resolution from SoLID inner trackers only
scintillators for muon PID with pion suppression and trigger

## Slide 12
Reuse 6 of CLEO octagon outer layer iron
Each one is about 36x254x533cm
No problem with space
Field (<10G),force(<1N),torque(<2Nm) are small
CLEO drawing
Conceptual support design
TOSCA field model
Iron of FAMD

## Slide 13: µRWell trackers of FAMD
µRWell tracker with good rate capability and lower cost than GEM
VMM electronics for readout
2D UV strips with capacitive charge sharing to have rate 30KHz/cm2 and position resolution of 1 mm
RWELL Detector – G. Bencivenni et al 2019 JINST 14 P05014
A plane of RWELL detector
RWELL Detector for EPIC outer barrel tracking layer

## Slide 14: Scintillators of FAMD
3 layers of scintillator planes
Each plane has 60 azimuthal segments
Readout with light guide and PMTs from both inner and outer radial ends
Design similar to CLAS12 forward scintillator and SoLID large angle scintillator with similar performance
10cm
Thickness 5cm
30cm
185cm
570cm
200cm
A plane of scintillator detector
A module of scintillator detector

## Slide 15: Event Acceptance
Best topology 3-fold(e+mu+mu): scattered e- at FA+LA, both muons at FA, proton not detected
Additional topology 4-fold(e+mu+mu+p): recoil proton at FA+LA (clean)
BH generator "grape-dilepton" used by HERA and verified by CLAS12
particle acceptance
accepted BH 3-fold events
full azimuthal coverage and large acceptance
Solenoid field helps control systematics

## Slide 16: Event Distribution
3-fold BH events covers a large kinematic range
0.7 overall detection efficiency
Enough counts with 1.2e37/cm2/s luminosity and 100 days to have multidimensional binning
accepted BH 3-fold events

## Slide 17: Exclusivity cut
Both BH with 4 final particles (elastic) and more than 4 particles (quasi-elastic), generated by "grape-dilepton"
Missing proton mass of 3 fold BH events with resolution from SoLID inner GEM trackers, for resonance free region (muon pair InvM>1.2GeV)
3-4% background after cutting MM>1.15GeV

## Slide 18: Pion blocking
Geant4 simulation of pions from target with some probabilities creating hits at FAMD
"pion hit probability", hits of charged particles entering each layer, used for FAMD background and trigger rate estimate
"pion surviving probability", hits of pion and muon at the last layer of FAMD with tracks passing all SoLID inner GEM trackers, used for physics event rate estimation

## Slide 19: Pion suppression within FAMD
Muons behave as Minimum Ionizing Particle (MIP)
Pions often deposit more energy over 3 layers of scintillators.
Use a moderate pion suppression factor 2 from energy cut
muon
pion

## Slide 20: Single pion background
Combining single pion generator "evgen_bggen" (pythia+MAID) events with "pion hit probability", study charged particle rate at 3 layers. Full simulation confirmed the result
Single particle trigger 600khz rate with hits in all 3 layers of scintillators in nearby phi sectors
Coincidence of two hits from 2 single particle trigger from 2 different phi sectors within 50ns time windows leads to 18khz final trigger rate
Fake coin rate from single pion is below 1khz. BH di-muon events have two muons separated at least by 60 degrees in phi angle for the main physics region (muon pair InvM>1.2GeV)

## Slide 21: Two pion exclusive background
Main physics background from two pion exclusive channel (missing mass cut won't reject it because pions and muons have similar mass)
Combine event generator "twopeg" (fit to CLAS data) and "pion hit probability" with pion suppression factor 2, study "2pi" rate and compare to BH rate
5-7% background, while the channel be measured by the internal SoLID detector at the same time to control systematics

## Slide 22: Experimental projection binning
100 days would allow for measurements on a five-dimensional grid (ξ’ ξ t xB φμ)
Covers both DVCS-like region (ξ’>0, Q²>Q'²) to TCS-like region (ξ’<0, Q²<Q'²)

## Slide 23: BSA experimental projections
First time measurement of the BSA sign change between the two regions
Possibility to constrain GPD models
DVCS-like region
All projection plots include statistical and polarization errors
TCS-like region
arXiv:2502.02346

## Slide 24: BSA experimental projections
All plots over the entire kinematic range

## Slide 25: BSA experimental projections
First time exploratory measurement of BSA constraining shadow GPD models (a class of functions with null CFF and forward limit contributing to GPD solutions in the deconvolution problem)
Phys. Rev. D 103 (2021) 114019
Notes: Shadow GPD models are parametrizations providing null Compton Form Factors and a vanishing forward limit appearing as solutions to the GPD inverse problem. Processes sensitive to the x-dependence of GPDs like DDVCS are required for setting strong constraints on them

## Slide 26: µCA experimental projections
known BH contribution is small in certain regions and can be subtracted
µCA has contributions from cos(φ) and cos(3φ) modulations
cos(φ) component can be extracted from fitting
First time exploratory measurement of µCA to access the CFF real part with curvature change

## Slide 27: Systematic effects
BSA systematics originates mainly from electron beam polarization, electron detection efficiency, and muon detection efficiency
l = 0.85
0.04
are the kinematic dependent number of bins, typically (20,10)
Bin independence hyptothesis
Control systematics through reference channels
SoLID will have crosssection measurement before this experiment
For e- detection, use inclusive DIS and elastic measurements
For muon detection, use both resonance and resonance free region and cross check both di-e and di-mu channels
Pion channel measurement are also taken at the same time
CLAS12 BH di-e data and sim comparison

## Slide 28: Beam time request
Main trigger on di-muon to take DDVCS, J/psi and TCS di-mu data at the same time
Independent di-e trigger for approved J/psi and TCS di-e data taking at the same time
Comprehensive program including muons and electrons within same runs. It can also help cross check systematics

## Slide 29: Summary
This proposed experiment
complement SoLID J/psi setup with a forward angle muon detector to form SoLIDμ spectrometer
measure DDVCS in the di-muon channel
share approved J/psi beamtime 60 days and request additional 50 days
Its physics impact
first time measurement of DDVCS (mainly BSA and exploratory µCA) over a broad kinematic range
first time to access GPD as input for models and global fitting

## Slide 30
Proposal to PAC53 PR12-25-010
Spokesperson : Juan-Sebastian Alvarado, Alexandre Camsonne, Marie Boer,
Eric Voutier, Xinzhan Bai, Zhiwen Zhao
and SoLID Collaboration

## Slide 31: Backup

## Slide 32
At leading twist–2, four quark chirality conserving GPDs for each quark type and gluon.
Because quark helicity is conserved in the hard scattering regime, the produced meson acts as a helicity filter.
GPDs are universal quantities and reflect nucleon structure independently of the probing reaction.
Need a variety of Hard Exclusive Measurements to disentangle the different GPDs.
Compton Scattering:
Sensitive to all four GPDs.
Deep Exclusive Meson Production:
Vector mesons sensitive to spin–average H E.
Pseudoscalar sensitive to spin–difference , .
GPD Parameterization

## Slide 33
The transverse densities of partons in nucleons and nuclei is related to the transverse momentum transfer () dependence of GPDs at zero-skewness.
DVCS and TCS cannot map out zero-skewness GPDs over the full physics phase space.
M. Burkardt PRD 62 (2000) 071503. M. Diehl EPJC 25 (2002) 223 A.V. Belitsky, D. Müller, NPA 711 (2002) 118c J.P. Ralston; B. Pire PRD 66 (2002) 111501
The experimental knowledge of the x-dependence of GPDs at fixed longitudinal momentum fraction allows to control the zero-skewness extrapolation required for nucleon imaging.
Nucleon Femtography
R. Dupré, M. Guidal, M. Vanderhaeghen, PRD 95 (2017) 011501

## Slide 34
u
d
A.W. Thomas, PRL 101 (2008) 102003
The experimental knowledge of the x-dependence of GPDs at fixed longitudinal momentum fraction is a mandatory step for unraveling the nucleon spin.
The total angular momentum of partons inside the nucleon can be inferred from the Ji sum rule which involves the forward limit of the first Mellin moment of partons helicity conserving GPDs.
DVCS and TCS cannot access GPDs at over the full physics phase space.
Nucleon Spin

## Slide 35
V. Burkert, L. Elouadrhiri, F.-X. Girod, Nat. 557 (2018) 396; arXiv:2104.02031
The skewness dependence of the first Mellin moment of the GPD H provides an access to the gravitational form factors of the energy momentum tensor of the nucleon.
-DVCS and TCS offers another path via dispersion relations.
The x-dependence of GPDs reveals the internal dynamics of the nucleon.
Nucleon Forces

## Slide 36
5-fold observables obtained from the integration over the polar angle of the muon and the azimuthal angle of initial virtual photon or final virtual photon are required, also minimizing the contribution of the BH2 process
Integrated Cross Section
DVCS-like xs
(integral of φμ)
TCS-like xs
(integral over ϕ)
DVCS-like xs
TCS-like xs
Our study focuses on using TCS-like xs for projection

## Slide 37: Muon Charge Asymmetry
Access to the real part of CFFs (no existing dispersion relation)
μCA predicted to have significant amplitude and rich harmonic composition, like the forward-backward asymmetry of TCS
Curvature change is a highly-discriminating feature for models
DDVCS μCA access a CFF combination different from BSA. This feature distinguishes DDVCS from DVCS and TCS.
aka Forward Backward Asymmetry

## Slide 38
Muon Detector Tracker
Utilize RWELL detectors for muon tracking layers
  Current RWELL detector rate capability – ~200 (High-rate version in development – 10)
  Discharge resistant thanks to integrated DLC layers – a huge improvement on electronics stability – less interruption on DAQ during running
  No spacers needed compared with GEM detectors – no dead area
A similar technology adopted by EIC
  Our muon detector unit would be roughly in the same size as EIC prototypes
  Total cost (3 complete layers covering a total of 75 ) around 900K
RWELL Detector – G. Bencivenni et al 2019 JINST 14 P05014
A plane of RWELL detectors for muon detection
RWELL Detector for EPIC outer barrel tracking layer

## Slide 39
Muon Detector Tracker
Use capacitive charge sharing technique to reduce total readout channels while maintain the same space resolution
Works for all readout patterns – strip, pad, zigzag, …
With Capacitive charge sharing:
Space resolution : 1 mm
Total readout channel can be reduced to around 22K for all 3 layers combined
Detector rate will be determined by the final readout strip width, larger strip width leads to lower detector rate capability
For 22K readout channels, 1 mm space resolution, with capacitive charge sharing technique – rate capability: (assume 300 ns signal integral time)
Concept for capacitive charge sharing – K. Gnanvo et al, Nuclear Inst. and Methods in Physics Research, A 1047 (2023) 167782

## Slide 40: SoLIDµ vs µCLAS12
100 days comparison

## Slide 41: SoLIDµ vs µCLAS12
Angles in the muon center-of-mass frame
Larger coverage with SoLIDµ
µCLAS12
SoLIDµ

## Slide 42: BH and trigger

## Slide 43: Systematic effects
Systematics of the measurements will be controlled via simulations and the measurement of reference processes. The solenoidal field and the symmetrical configuration of SoLIDm offer further cross-checks
Muon solid angle : extensive simulations based on the SoLIDm GEANT4 model ()
Electron detection efficiency : measurement of DIS and elastic electron scattering ()
Muon detection efficiency : measurement of Bethe-Heitler and comparison of the and decay of specific meson (f, J/Y) ()

## Slide 44: Background asymmetry
signal channel asymmetry As=0.1 and rate Rs
background channel asymmetry Ab=0.5 and rate Rb
Background/signal rate Rb/Rs=0.05 with error ER=0.01
Rel_Error of As = (As-Ab)/(1-Rb/Rs)^2*ER/As
            = (0.1-0.5)/(1-0.05)^2*0.01/0.1=-0.045
With those conservative assumptions, background only give about 5% error on signal asymmetry

## Slide 46: Cost

## Slide 47: Binning

## Slide 48
Coordinates Layer 1
Y
X
Z
Iron wall 1
Ch 1 -
Ch 1 +
Ch 2 -
Ch 2 +
Reference = Magnet

## Slide 49
Coordinates Layer 2
Y
X
Z
Iron wall 2
Ch 3 -
Ch 3 +
Ch 4 -
Ch 4 +
Reference = Magnet

## Slide 50
E12-12-006: Near Threshold J/Psi production on LH2 target
Most precise measurement near threshold

## Slide 51
E12-12-006A: TCS with circular polarized beam and LH2 target
SoLID TCS coverage
SoLID TCS will have at least 1 order larger statistics than CLAS12 and usher TCS study into precision era with multi-dimensional binning
    SoLID has 250 times more integrated luminosity than the CLAS12 TCS published result
    SoLID acceptance to TCS events is about ¼ of CLAS12. But with full azimuthal coverage, (ideal for the forward backward asymmetry)
    Crosssection measurement (moment)
SoLID TCS could lead to study of NLO correction