## Slide 1: SoLID JPsi_LH2 Hit and Occupancy
Zhiwen Zhao
2017/05/16

## Slide 2: Introduction
“Hit”, look at detector response from different source particles to get hit rate
“Occupancy”, assume certain threshold cut on hit information to get event rate
We look at each detector channels (no GEM or MRPC yet)
We assume each particle entering a detector is independent, so no time window for integration yet
Simulation data of “JPsi_LH2_JLAB_VERSION_1.3/pass5” is used

## Slide 3: All source
all source from target and windows
  BeamOnTarget, BeamOnTargetEM by Geant4
  eDIS, pions and proton by HallD
Occupancy threshold cut (low)
  LGC > 0 N of p.e.
  HGC > 0 N of p.e.
  SPD_FA > 0.1MeV (1/5 of trigger cut 0.5MeV)
  SPD_LA > 0.3MeV (1/5 of trigger cut 1.5MeV)
  EC preshower > 0.4MeV
  EC shower > 6MeV
Occupancy threshold cut (high)
  LGC > 1 N of p.e.
  HGC > 1 N of p.e.
  SPD_FA > 0.25MeV (1/2 of trigger cut 0.5MeV)
  SPD_LA > 0.75MeV (1/2 of trigger cut 1.5MeV)
  EC preshower > 0.8MeV
  EC shower > 12MeV

## Slide 4: LGC and HGC
  Occupancy cut (low), LGC > 0 N of p.e. HGC > 0 N of p.e.

## Slide 5: LGC and HGC
  Occupancy cut (high), LGC > 1 N of p.e. HGC > 1 N of p.e.

## Slide 6: SPD
  Occupancy cut (low), FA > 0.1 MeV, LA > 0.3 MeV

## Slide 7: SPD
  Occupancy cut (high), FA > 0.25 MeV, LA > 0.75 MeV

## Slide 8: EC
  Occupancy cut (low), preshower > 0.4 MeV, shower > 6 MeV

## Slide 9: EC
  Occupancy cut (high), preshower > 0.8 MeV, shower > 12 MeV

## Slide 10: Occupancy Result: LGC and HGC
Occ(kHz) | BeamOnTarget | BeamOnTargetEM | Pi0 Halld | allnoe HallD | eDIS Halld
LGC (>0) | 5455 | 2179 | 1536 | 1945 | 122
LGC (>1) | 2649 | 745 | 728 | 915 | 93
HGC (>0) | 4845 | 4757 | 92 | 199 | 15
HGC (>1) | 3358 | 3211 | 72 | 157 | 12
  For LGC, EM and hadron contribute half and half
  For HGC, EM is dominating
  The table shows
    For LGC: sum of 9 channels
    For HGC: sum of 16 channels

## Slide 11: Occupancy Result: SPD
Occ(kHz) | BeamOnTarget | BeamOnTargetEM
SPD_FA (>0.1) | 3.65e6 | 3.44e6
SPD_FA (>0.25) | 2.70e6 | 2.52e6
SPD_LA (>0.3) | 5.18e6 | 4.90e6
SPD_LA (>0.75) | 2.56e6 | 2.35e6
  The table shows
    For SPD_FA: sum of 240 channels
    For SPD_LA: sum of 60 channels
  For SPD, EM is dominating

## Slide 12: Occupancy Result: EC
Occ(kHz) | BeamOnTarget | BeamOnTargetEM
EC_preshower_FA (>0.4) | 5.32e6 | 5.00e6
EC_preshower_FA (>0.8) | 3.89e6 | 3.65e6
EC_shower_FA (>6) | 1.72e6 | 1.40e6
EC_shower_FA (>12) | 4.38e5 | 2.07e5
EC_preshower_LA (>0.4) | 1.87e6 | 1.64e6
EC_preshower_LA (>0.8) | 1.17e6 | 0.99e6
EC_shower_LA (>6) | 4.89e5 | 1.92e5
EC_shower_LA (>12) | 2.26e5 | 0.07e5
  The table shows
    For EC_FA: sum of ~1300 channels
    For EC_LA: sum of ~500 channels
  For shower, EM and hadron contribute half and half
  For preshower, EM is dominating

## Slide 13: Result Summary A
 | Max Occ(kHz/channel) low cut | Max Occ(kHz/channel) high cut | Average Occ(kHz/channel) low cut | Average Occ(kHz/channel) high cut | Number of channel | Total Occ(kHz) low cut | Total Occ(kHz) high cut
LGC | 954 | 503 | 606 | 294 | 270 | 16.4e4 | 7.95e4
HGC | 372 | 272 | 303 | 210 | 480 | 14.5e4 | 10.1e4
SPD_FA | 24.1e3 | 17.5e3 | 15.2e3 | 11.3e3 | 240 | 3.65e6 | 2.70e6
SPD_LA | 89.4e3 | 44.4e3 | 86.3e3 | 42.7e3 | 60 | 5.18e6 | 2.56e6
EC_preshower_FA | 10087 | 7650 | 4092 | 2992 | ~1300 | 5.32e6 | 3.89e6
EC_shower_FA | 9337 | 2344 | 1323 | 337 | ~1300 | 1.72e6 | 4.38e5
EC_preshower_LA | 12806 | 8119 | 3740 | 2340 | ~500 | 1.87e6 | 1.17e6
EC_shower_LA | 6562 | 1894 | 978 | 452 | ~500 | 4.89e5 | 2.26e5
Total |  |  |  |  | 4650 | 18.5e6 | 11.2e6
  All values from “BeamOnTarget”

## Slide 14: Result Summary B
 | Max Occ(kHz/channel) | Average Occ(kHz/channel) low cut | Number of channel | Total Occ(kHz)
GEM 1 |  |  | 906*30 | 
GEM 2 |  |  | 1020*30 | 
GEM 3 |  |  | 1166*30 | 
GEM 4 |  |  | 1404*30 | 
GEM 5 |  |  | 1040*30 | 
GEM 6 |  |  | 1280*30 | 
MRPC |  | 1210 | 33*50*2 | 4e6
Total |  |  | 207780 | 
  All values from “BeamOnTarget”

## Slide 15: Other thoughts
So far all hit rates and particles rate are based on detector response from individual particles.
Some detector like SPD and EC have high rate. There are many particles entering them within their integration time windows. If we consider this, the hit rate, occupancy cut value, occupancy rate could be different