## Slide 1: SoLID simulation with GEMC update
Zhiwen Zhao
2015/12/03

## Slide 2: FAEC in simulation with layout from ANL

## Slide 3: EC module size and layout
Use ANL layout, 5cm edge modules look ok, but 6.25cm edge modules have overlap
Our default module design is 6.25cm
FAEC layout needs to change, LAEC layout is still missing
5cm
6.25cm

## Slide 4: SIDIS hadron trigger
To record all hadron (mainly pion)
Dominate by charge pions and gamma from pi0
Previous trigger rate estimation 14MHz for SIDIS He3
Trigger is made of
  EC cut below MIP to reserve hadron and suppress low energy background
  SPD and MRPC anti-cut below MIP to reject gamma
A simple test with full SoLID simulation under conditions:
  Incoming particles evenly distributed within 1-11GeV
  No background yet

## Slide 5: pi- energy deposition
MIP in all three detectors
Counts
MeV

## Slide 6: gamma energy deposition
Full energy deposition in EC
Mostly no energy in SPD and MRPC
Counts
MeV

## Slide 7: e- energy deposition
Full energy deposition in EC
MIP in SPD and MRPC
Counts
MeV

## Slide 8: Trigger estimation (just an exercise)
incoming | EC yes && SPD no | EC yes && MRPC no | SPD no && MRPC no | EC yes && (SPD no ¦¦ MRPC no)
pi- | 0.44 | 0.44 | 0.66 | 0.44
gamma | 79 | 71 | 65 | 85
e- | 0.67 | 0.55 | 0.55 | 0.67
incoming | EC yes && SPD yes | EC yes && MRPC yes | SPD yes && MRPC yes | EC yes && (SPD yes && MRPC yes)
pi- | 99.6 | 99.6 | 99.6 | 99.6
gamma | 21 | 29 | 15 | 15
e- | 99.3 | 99.3 | 99.3 | 99.3
Logic for gamma
Logic for hadron
pi- detection ~100%
gamma rejection factor 6.6, No electron rejection
unit in percent