## Slide 1: SIDIS trigger study
Yuxiang Zhao

## Slide 2: Planned trigger detectors
SIDIS electron trigger
  Forward angle: EC + LGC + SPD + MRPC
  Large angle: EC + SPD
SIDIS hadron trigger
  EC + SPD + MRPC (could be different depending on further study)
Working plan
  Get singles rate on each detectors for different particles
  Get total singles rate with detector coincidence
    electron-like total rate
    hadron-like total rate
  Estimate electron-like & hadron-like random coincidence rate
  Estimate Real physics SIDIS rate with SIDIS generator

## Slide 3
Forward electron trigger
EC + LGC + SPD + MRPC
SPD threshold: 0.35 MeV
MRPC threshold: edep of 16eV in one gap and at least 5 gaps to be fired

## Slide 4: SIDIS forward electron trigger ---Individual detectors
Singles particle | EC Rate (kHz) | LGC Rate(KHz) | SPD Rate(MHz) | MRPC Rate(MHz) | All 4 fired Rate(KHz)
electron | 82.8 | 169 | 3.3 | 1.9 | 64.4
Pim | 861 | 82.4 | 15.5 | 14.4 | 6.2
Pip | 1036 | 85.7 | 18.7 | 17.6 | 7.2
Pi0 | 2210 | 2045 | 10.8 | 7.6 | 88.1
Total: | 4193 | 2382 | 49 | 41.5 | 166.5
Using Wiser generator
Total electron-like trigger rate in forward angle: 166.5 KHz + random coincidence among detectors
Random coincidence: if track match is done with 10 segmentations in each detector, random coincidence rate=55Hz

## Slide 5
Large angle electron trigger
EC + SPD
SPD threshold: 0.35 MeV

## Slide 6: SIDIS large electron trigger ---Individual detectors
Singles particle | EC Rate (kHz) | SPD Rate(MHz) | Both fired Rate(KHz)
electron | 4.47 | 2.3 | 4.3
Pim | 9.8 | 17.7 | 9.1
Pip | 10 | 21.8 | 10
Pi0 | 18.5 | 7.8 | 2.3
Total: | 42.8 | 49.6 | 25.7
Using Wiser generator
Total electron-like trigger rate in forward angle: 25.7KHz + random coincidence among detectors
Random coincidence: if track match is done with 10 segmentations in each detector, random coincidence rate=914Hz

## Slide 7
SIDIS hadron trigger
  EC + SPD + MRPC

## Slide 8: SIDIS hadron trigger
Singles particle | EC Rate (MHz) | SPD Rate(MHz) | MRPC Rate(MHz) | All 3 fired Rate(MHz)
electron | 0.21 | 3.5 | 1.9 | 0.17
Pim | 13.7 | 15.7 | 14.4 | 12.1
Pip | 16.7 | 19.1 | 17.6 | 14.8
Pi0 | 17.5 | 10.8 | 7.6 | 2.5
Total: | 48.1 | 49.1 | 41.5 | 29.6
Total hadron rate based on EC+SPD+MRPC = 29.6 MHz + random coincidence among detectors
Wiser curve and wiser data
Random coincidence: if track match is done with 10 segmentations in each detector, random coincidence rate=84KHz

## Slide 9: Electron-like & hadron-like random coincidence ---assuming 30 ns window
Forward angle electron trigger rate: 166.5KHz
Large angle electron trigger rate: 25.7KHz
Hadron trigger rate: 29.6MHz
e&h random coincidence rate: (144KHz+29.8KHz)*29.58MHz*30ns=176KHz
No detector correlations study yet, should be taken into account

## Slide 10: My concern for hadron trigger
Forward electron trigger: EC(high threshold)+LGC+SPD+MRPC
Forward hadron trigger: EC(low threshold) + SPD+MRPC
Those particles passed electron trigger in the forward angle will also pass hadron trigger: will cause additional e&h coincidence rate by 144KHz in the forward angle
VETO on LGC ??? Not practical, could have an electron in this sector
Make judgement on hit position on EC??? Will have bias on phi_h
Only inclusive triggers in forward angle??? A big project, not doable shortly

## Slide 11: Hit position constraint to form hadron trigger ---5 cm away from electron trigger
Using singles particle to do a test
Pid | Pass electron trigger (kHz) | Pass electron trigger and hadron trigger without R constrain (kHz) | Pass electron trigger and hadron trigger with R constrain (kHz)
electron | 42 | 42 | 11.3
pim | 6.2 | 6.2 | 0.8
pip | 8.1 | 8.1 | 1.3
pi0 | 89.7 | 89.7 | 37.6
Electron trigger and hadron trigger at forward angle has a correlation of about 35%
e&h trigger correlation in the forward angle will give additional 51kHz coincidence trigger rate

## Slide 12: SIDIS trigger rate by using wiser
e&h random coincidence:(144KHz+29.8KHz)*29.58MHz*30ns=154KHz
e trigger and hadron trigger correlation in forward angle: 51KHz
SIDIS physics rate: ~10KHz
Detector correlations---impact on e or h rates---haven’t been studied yet

## Slide 13: To-do list for SIDIS trigger rate estimation
Update EC response using Hall D generator (Rakitha)
Update SPD threshold (Sanghwa)
Update MRPC threshold (Sanghwa)
Hadron-like trigger rate estimation done by using wiser based study
Define how to do “track match” at trigger level to reduce random coincidence rate (among detectors)
   10 segmentations in phi dimension (3 adjacent sectors)
Efficiency study by combining all the individual detectors in the trigger design

## Slide 14
Backups

## Slide 15: SIDIS hadron trigger
Singles particle | EC Rate (MHz) | SPD Rate(MHz) | MRPC Rate(MHz) | All 3 fired Rate(MHz) | All 3 fired + lgc veto (MHz)
electron | 0.14 | 2.0 | 1.16 | 0.11 | 0.047
Pim | 13.7 | 15.7 | 14.4 | 12.1 | 12.06
Pip | 16.7 | 19.1 | 17.6 | 14.8 | 14.76
Pi0 | 17.5 | 10.8 | 7.6 | 2.5 | 1.81
Total: | 48 | 47.6 | 40.8 | 29.5 | 28.7
Wiser curve and wiser data
By putting a VETO on LGC for hadron trigger, we almost keep all the pi+/-
Forward electron trigger now doesn’t have any overlap with hadron trigger

## Slide 16: SIDIS forward electron trigger ---EC singles rate
Singles particle | Rate (kHz)
electron | 53.9
Pim | 864
Pip | 1036
Pi0 | 2210
Total: | 
Using Wiser generator

## Slide 17: SIDIS forward electron trigger ---LGC singles rate with threshold=2 p.e & 2 pmts
Singles particle | Rate (kHz)
electron | 77.2
Pim | 82.4
Pip | 85.7
Pi0 | 2045
Total: | 
Using Wiser generator

## Slide 18: SIDIS forward electron trigger ---SPD singles rate with threshold=0.35MeV
Singles particle | Rate (MHz)
electron | 2.0
Pim | 15.7
Pip | 19.1
Pi0 | 10.8
Total: | 
Using Wiser generator
60 pieces in phi dimension, 4 pieces in r dimension

## Slide 19: SIDIS forward electron trigger ---MRPC singles rate with threshold=16eV and 5 laylers to be fired
Singles particle | Rate (MHz)
electron | 1.16
Pim | 14.4
Pip | 17.6
Pi0 | 7.6
Total: | 
Using Wiser generator
60 pieces in phi dimension, 4 pieces in r dimension, 10 gas layers