## Slide 1: SoLID simulation with GEMC
Zhiwen Zhao
2015/03/26

## Slide 2: Outline
GEMC Update
SoLID simulation with GEMC 2.x
  “solid_gemc” in general
  EC simulation as an example
Summary

## Slide 3: GEMC Update: Outline
GEMC 1.x to 2.x, a major code rewrite
use factory method as much as possible, easy to add plug-in and expand functionality
Field map
  Field info embedded in field map file, no separated definition needed
  Map Reading 3-4x faster Swimming 30% faster
Modular physics list (hadron+EM+optical)
Updated GUI
geometry and parameters, material, optical properties, hit process and output are all external
Built-in hit type “flux” and step-by-step hit info
New features like customized event generator input, voltage signal and FADC support
Took a lot suggestion from SoLID and MEIC simulation and we contribute to its code and structure also

## Slide 4: GEMC Update: installation
software installation streamlined by a set of scripts
part of the general jlab software framework (including jana, ccdb and more)
Everything in release package, no SVN or github download
a single version control by env “Jlab_version”
Just an “App” to download on Mac, no install needed
Jlab_version | 1.0 | 1.1 | 1.2 | devel
GEMC | 1.8 | 2.1 | 2.2 | 2.3?
geant4 | 9.5 | 9.5/9.6 | 10.0 | 10.1?

## Slide 5: GEMC update: GUI
qt5 and openGL

## Slide 6: GEMC update: Input
All generators are still fully independent, interface by txt file in customized LUND format
Fully pass customized header info into output

## Slide 7: GEMC Update: Optical
All properties defined external in “table” format similar to geometry

## Slide 8: GEMC Update: Voltage Signal

## Slide 9: GEMC Update: Outlook
FADC banks will emulate FADC output, including translation tables
Hit process routines will be a plugin - completely independent from GEMC, to be loaded at run time. The routines can be stored together with the geometry / materials scripts.
multithreading, following G4
C++ 11

## Slide 10: SoLID simulation with GEMC 2.x solid_gemc
    GEMC compiled as a lib during installation by default
    Then add customized hit process routing and other things and link to libgemc.so to keep all GEMC features, similar idea to “solgemc”
    This becomes “solid_gemc” with matching version of GEMC
Solid_gemc2/source
2.1
2.2
Solid_gemc.cc
Hitprocess
Solid_hitprocess.h
Solid_ec_hitprocess.cc
Solid_ec_hitprocess.h
……

## Slide 11: EC simulation with solid_gemc
solid - Revision 746: /subsystem/ec/ec_solid_gemc
..
config_solid_PVDIS_ec_forwardangle.dat configuration file for generating
readme
solid_PVDIS_ec_forwardangle.gcard input file to run simulation
solid_PVDIS_ec_forwardangle.pl file to generate geomtry,bank,hit
solid_PVDIS_ec_forwardangle__bank.txt generated bank
solid_PVDIS_ec_forwardangle__geometry_Original.txt generated geometry
solid_PVDIS_ec_forwardangle__hit_Original.txt generated hit
solid_PVDIS_ec_forwardangle__materials_Original.txt generated material
solid_PVDIS_ec_forwardangle__parameters_Original.txt parameters defines geometry
solid_PVDIS_ec_forwardangle_real.pl file to generate geometry
solid_ec_bank.pl file to generate bank
solid_ec_hit.pl file to generate hit
solid_ec_materials.pl file to generate material
solid_slice.vis
    Purple and orange files needed to generate files for simulation
    Red files needed to run simulation
    Red and orange files are in “table” format, they can be in
      txt file
      Database (mysql now, CCDB soon)
      expanded to more sources
    An example line of a txt file
    solid_PVDIS_ec_forwardangle_real_shower | root |solid_PVDIS_ec_forwardangle_real_shower | 0*cm 0*cm 350*cm | 0*deg 0*deg 0*deg | ff0000 | Tube | 110*cm 365*cm 21.728*cm 0*deg 360*deg | G4_AIR | no | 1 | 1 | 1 | 1 | 1 | no | no | no

## Slide 12: Customized hit process routine “solid_ec”
insert_bank_variable(\%configuration, $bankname, "bankid", $bankId, "Di", "$bankname bank ID");
insert_bank_variable(\%configuration, $bankname, "pid", 1, "Di", "ID of the first particle entering the sensitive volume");
insert_bank_variable(\%configuration, $bankname, "mpid", 2, "Di", "ID of the mother of the first particle entering the sensitive volume");
insert_bank_variable(\%configuration, $bankname, "tid", 3, "Di", "Track ID of the first particle entering the sensitive volume");
…………………
insert_bank_variable(\%configuration, $bankname, "id", 24, "Di", "id number");
insert_bank_variable(\%configuration, $bankname, "hitn", 99, "Di", "Hit Number");
dgtz["pid"] = (double) aHit->GetPID();
dgtz["mpid"] = (double) aHit->GetmPID();
dgtz["tid"] = (double) aHit->GetTId();
………….........
dgtz["id"] = id;
dgtz["hitn"] = hitn;
solid_ec_bank.pl
solid_ec_hitprocess.cc
    Totally flexible to any raw and digitized hit processing and output, fit any level of simulation and digitization need
    As far as the two match each other to give consistent result, “solid_gemc” need recompile if any change

## Slide 13: Hit process control
Fine tuning hit processing without source code change
No need to recompile solid_gemc
solid_ec_hit.pl
$hit{"name"} = "solid_ec";
$hit{"description"} = "solid ec hit definition";
$hit{"identifiers"} = "id";
$hit{"signalThreshold"} = "0*MeV";
$hit{"timeWindow"} = "400*ns";
$hit{"prodThreshold"} = "1*mm";
$hit{"maxStep"} = "1*cm";
$hit{"delay"} = "10*ns";
$hit{"riseTime"} = "1*ns";
$hit{"fallTime"} = "1*ns";
$hit{"mvToMeV"} = 100;
$hit{"pedestal"} = -20;

## Slide 14: External parameters
It can take source from survey data
And can be part of calibration database
solid_PVDIS_ec_forwardangle__parameters_Original.txt
Nlayer | 194 | | Nlayer | - | - | - | - | - | -
Thickness_lead | 0.05 | cm | Thickness_lead | - | - | - | - | - | -
Thickness_scint | 0.15 | cm | Thickness_scint | - | - | - | - | - | -
Thickness_gap | 0.024 | cm | Thickness_gap | - | - | - | - | - | -
Thickness_shield | 1.0274 | cm | Thickness_shield | - | - | - | - | - | -
Thickness_prescint | 2 | cm | Thickness_prescint | - | - | - | - | - | -
Thickness_support | 2 | cm | Thickness_support | - | - | - | - | - | -
z_shower | 350 | cm | z_shower | - | - | - | - | - | -
Rmin | 110 | cm | Rmin | - | - | - | - | - | -
Rmax | 365 | cm | Rmax | - | - | - | - | - | -
Sphi | 0 | deg | Sphi | - | - | - | - | - | -
Dphi | 360 | deg | Dphi | - | - | - | - | - | -

## Slide 15: solid_gemc summary
status
  EC, GEM, MRPC, SPD have initial implementation at various stages
  Cherenkov implementation is under work
advantage
  fast MC and full MC within one framework
  The exact same files for standalone simulation and combined simulation

## Slide 16: Other things
Record simulation condition
  GEMC record all input options into EVIO file
  We can think of ways to record detector related input (as SVN or github version or database entry with index like run number? It will depends on where we store them)
Output file format
  “evio2root”, convert evio to root tree, included with framework
  “clas-root”, read evio like a root tree, will include
  https://userweb.jlab.org/~gavalian/clas12docs/sphinx/html/rootio/introduction.html
Documentation
  Nice GEMC tutorials available
  Doxygen for source code
  Wiki https://hallaweb.jlab.org/wiki/index.php/Solid_Software